## Slide 1
Embedded Linux Design
Session 2: Toolchains & Bootloaders
UCSC Extension | Instructor: Juergen Kienhoefer

## Slide 2
Today's Roadmap
Toolchains
Cross-development model
Toolchain components
Building vs. pre-built
Verification
Bootloaders
Boot flow overview
SPL + U-Boot
U-Boot hands-on
Kernel Build
Config → Build → Verify
Device Tree basics
Kernel + DTB handoff
Root Filesystem
Directory structure
Init process
Buildroot quick start
Lab
Build a bootable system
Flash and boot
Common pitfalls

## Slide 3
The Cross-Development Model
Development Host
x86_64 Linux workstation
Cross-compiler (e.g., arm-linux-gnueabihf-gcc)
Debugger, serial terminal, build tools
Produces binaries for target architecture
Target Hardware
ARM / RISC-V / MIPS board
Bootloader (U-Boot)
Linux kernel + device tree
Root filesystem
Your application
You develop on the host, deploy to the target.

## Slide 4
Part 1: Toolchains
Cross-compilation fundamentals

## Slide 5
What Is a Toolchain?
A toolchain is a set of compilation tools that runs on one architecture (the host) and produces executable code for another (the target). Core components: • GCC (cross-compiler) — compiles C/C++ for the target • Binutils — linker, assembler, object tools • C library (glibc, musl, uClibc) — standard library for target • GDB (cross-debugger) — debug target binaries from the host The toolchain is defined by a target tuple: arm-linux-gnueabihf → ARM, Linux, hard-float ABI

## Slide 6
Toolchain Anatomy
Source Code (.c/.cpp)
Your application and kernel source
Cross-Compiler (gcc)
Translates to target ISA — produces .o files
Linker (ld)
Links .o + libraries → target binary
C Library (libc)
Provides stdio, stdlib, POSIX APIs for target
Binary Utilities
readelf, objdump, strip, ar — inspect/manipulate

## Slide 7
Choosing Your Toolchain
Approach
Pros
Cons
When to Use
crosstool-NG
Fully customizable, any arch/libc combo
Takes hours to build for first time
You need a specific target tuple not available pre-built
Pre-built (Linaro/ Bootlin/vendor)
Ready in minutes, well-tested
Limited arch/libc combinations
Standard ARM boards — fastest path
Yocto SDK
Matches your Yocto image exactly
Requires Yocto build first
You are using Yocto for your distro

## Slide 8
Verify Your Toolchain
# Check the cross-compiler is in PATH $ which arm-linux-gnueabihf-gcc /usr/bin/arm-linux-gnueabihf-gcc # Check version and target $ arm-linux-gnueabihf-gcc --version gcc 12.2.0 (crosstool-NG 1.25.0) Target: arm-linux-gnueabihf # Check what ABI/hardware it targets $ arm-linux-gnueabihf-readelf -h /usr/lib/libc.so.6 | grep Machine Machine: ARM # Compile a test program $ echo 'int main(){return 0;}' > test.c $ arm-linux-gnueabihf-gcc -o test test.c $ file test test: ELF 32-bit LSB executable, ARM, EABI5

## Slide 9
Part 2: Bootloaders
From power-on to kernel

## Slide 10
What Is a Bootloader?
Definition
First software that runs after chip ROM
Initializes essential hardware: DRAM, clocks, storage
Loads the kernel image into RAM
Passes boot arguments and jumps to kernel entry
Embedded Linux boot flow
ROM → SPL → Bootloader → Kernel → Userspace
The bootloader is the critical handoff point
Most common: U-Boot (Universal Boot Loader)

## Slide 11
Two-Stage Boot: SPL + U-Boot
ROM (SoC)
Hard-coded first code. Loads SPL from flash/SD.
SPL (Secondary Program Loader)
Minimal init: DRAM, clocks. Loads main U-Boot. Tiny (~64KB), runs from SRAM.
U-Boot (Main Bootloader)
Full environment: USB, network, filesystem. Loads kernel, DTB, initramfs into RAM.
Linux Kernel
Takes over. Mounts root filesystem. Starts init.

## Slide 12
U-Boot: The Standard Bootloader for Embedded Linux
Hardware Support
ARM, x86, RISC-V, MIPS, PowerPC
SD/eMMC, NAND, NOR, SPI flash
USB, Ethernet, UART, I2C, SPI
Filesystem: ext4, FAT, squashfs
Developer Features
Interactive command-line console (serial)
Environment variables (bootcmd, bootargs)
Network boot: TFTP, NFS
Scripted boot sequences
FIT image support (kernel+DTB+ramdisk)

## Slide 13
U-Boot Console: What You'll See
U-Boot SPL 2024.01 (Jan 15 2024 - 10:23:45) DRAM: 512 MiB MMC: SD@ee140000: 0 Loading Environment from MMC... OK U-Boot 2024.01 (Jan 15 2024 - 10:23:45 +0000) Model: MyBoard Rev 1.0 DRAM: 512 MiB MMC: SD@ee140000: 0 Loading Environment from MMC... OK Net: eth0: ethernet@ff0b0000 Hit any key to stop autoboot: 0 <- you must press a key! => <- U-Boot prompt

## Slide 14
U-Boot: Essential Commands
=> help # List all available commands => printenv # Show all environment variables => setenv bootargs 'console=ttyS0,115200 root=/dev/mmcblk0p2' => saveenv # Persist environment to flash => mmc list # List MMC devices => mmc dev 0 # Select MMC device 0 => fatls mmc 0:1 # List files on partition 1 => fatload mmc 0:1 ${loadaddr} zImage => bootz ${loadaddr} # Boot the kernel => tftpboot ${loadaddr} zImage # Load via network => bdinfo # Board information => reset # Reset the board

## Slide 15
U-Boot Boot Sequence
Power On
SoC ROM loads SPL from boot media (SD/eMMC/SPI)
SPL Runs
Initializes DRAM, clocks. Loads U-Boot proper.
U-Boot Init
Full hardware init: UART, USB, network, storage
bootcmd Executes
Default script: loads kernel, DTB, rootfs from media
Kernel Handoff
Decompresses kernel, sets up ATAGS/DTB, jumps to entry
Linux Takes Over
Kernel mounts rootfs, starts init/systemd

## Slide 16
Part 3: Kernel Build & Device Tree
Configuring and compiling the Linux kernel

## Slide 17
Kernel Image Types
Format
Description
Use Case
zImage
Compressed kernel (gzip), self-decompressing
Most common for ARM, standard bootloader format
uImage
U-Boot wrapped zImage (has U-Boot header)
Older U-Boot versions (legacy)
Image
Uncompressed raw kernel image
x86, or when bootloader does decompression
FIT (Flattened Image Tree)
Bundle: kernel + DTB + initramfs + config in one image
Secure boot, multi-config boot, modern U-Boot

## Slide 18
Kernel Build: Configuration
# Download and extract kernel source $ tar xf linux-6.6.tar.xz && cd linux-6.6 # Option A: Use a default config for your board $ make ARCH=arm myboard_defconfig # Option B: Start from your running config $ zcat /proc/config.gz > .config $ make ARCH=arm oldconfig # Interactive config (menu-driven) $ make ARCH=arm menuconfig # Save a minimal defconfig for sharing $ make ARCH=arm savedefconfig # Produces: defconfig (human-readable, shareable)

## Slide 19
Kernel Build: Compilation
# Build kernel image, modules, and device tree blobs $ make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- \ -j$(nproc) Image modules dtbs # Output: # arch/arm/boot/zImage <- kernel # arch/arm/boot/dts/*.dtb <- device tree blobs # drivers/**/*.ko <- kernel modules # Install modules to a staging directory $ make ARCH=arm INSTALL_MOD_PATH=./modules_install \ modules_install # Verify the kernel was built for the right arch $ file arch/arm/boot/zImage zImage: Linux kernel ARM boot executable zImage

## Slide 20
Kernel Build: Verification
# Check kernel version and build info $ strings arch/arm/boot/zImage | grep 'Linux version' Linux version 6.6.0 (user@host) (arm-linux-gnueabihf-gcc 12.2.0) #1 SMP # Check what machine it's built for $ arm-linux-gnueabihf-readelf -h arch/arm/boot/zImage | grep Machine Machine: ARM # Check DTB matches your board $ fdtdump arch/arm/boot/dts/myboard.dtb | head /dts-v1/; / { model = "MyBoard Rev 1.0"; compatible = "myvendor,myboard"; ... # Size check — know what fits in flash $ ls -lh arch/arm/boot/zImage arch/arm/boot/dts/*.dtb 5.2M zImage 48K myboard.dtb

## Slide 21
Part 3b: Device Tree
Hardware description without C code

## Slide 22
Device Tree: What & Why
The Problem
Every board needed a C 'board file' in kernel source
Hundreds of board files, most code duplicated
Changing a GPIO pin meant recompiling the kernel
Vendor BSPs were a maintenance nightmare
The Solution
Device Tree (DTS): data structure describing hardware
Compiled to DTB (binary) — passed to kernel at boot
One kernel image supports many boards via different DTBs
Standard on ARM, RISC-V; x86 uses ACPI instead

## Slide 23
Device Tree: Structure
A device tree is a tree of nodes, each representing a device or bus: / { model = "MyBoard"; compatible = "myvendor,myboard"; #address-cells = <1>; #size-cells = <1>; cpus { ... }; memory@80000000 { ... }; soc { uart0: serial@ff000000 { ... }; i2c0: i2c@ff010000 { ... }; mmc0: mmc@ff020000 { ... }; }; }; Key concepts: • Nodes — devices, buses, peripherals • Properties — name=value pairs (strings, integers, arrays) • Labels — references (&uart0) for cross-referencing • Compatible strings — match devices to drivers

## Slide 24
Device Tree: Annotated Example
// myboard.dts — device tree source for MyBoard /dts-v1/; #include "armv7.dtsi" // Include SoC-level definitions / { model = "MyBoard Rev 1.0"; // Human-readable name compatible = "myvendor,myboard"; // Matches kernel driver chosen { // Kernel cmdline, stdout stdout-path = "serial0:115200n8"; bootargs = "console=ttyS0,115200 root=/dev/mmcblk0p2"; }; memory@80000000 { // RAM: start 0x80000000, 512MB device_type = "memory"; reg = <0x80000000 0x20000000>; }; leds { // On-board LEDs compatible = "gpio-leds"; status_led: led0 { label = "status"; gpios = <&gpio0 12 GPIO_ACTIVE_HIGH>; }; }; };

## Slide 25
Kernel + DTB: How They Work Together
U-Boot Loads Images
Reads zImage and .dtb from flash into RAM at different addresses
Passes DTB Address
U-Boot passes the DTB physical address in a CPU register (r2 on ARM)
Kernel Decompresses
Kernel self-decompresses, early init reads the DTB from register
DTB Parsing
Kernel walks the DTB tree, discovers devices, loads matching drivers
Driver Probe
Drivers with matching 'compatible' strings are bound to devices
Userspace
Kernel finishes boot, mounts rootfs, starts init — all initialized

## Slide 26
Part 4: Root Filesystem
What lives on the target

## Slide 27
Root Filesystem: Structure
Essential Directories
/bin — Core user commands (ls, cp, cat, echo)
/sbin — System commands (init, mount, fdisk)
/etc — Configuration files (fstab, inittab, hostname)
/lib — Shared libraries, kernel modules
/dev — Device nodes (created by kernel/udev)
/proc — Kernel/process information (virtual)
/sys — Kernel/device information (virtual)
/tmp — Temporary files
/usr — Secondary hierarchy (usr/bin, usr/lib)
/var — Variable data (logs, spool)
Embedded Considerations
Can fit in as little as 4–16 MB with BusyBox
No package manager on most embedded systems
Buildroot or Yocto create the rootfs at build time
Often read-only (squashfs) or read-write (ext4/ubifs)

## Slide 28
Init Process: First Userspace Program
BusyBox init (typical embedded)
Minimal — single BusyBox binary provides all tools
Reads /etc/inittab for runlevel configuration
Starts /etc/init.d/rcS on boot
Spawns a shell on console (no login required)
Very fast boot (milliseconds to shell)
Size: ~1–2 MB total rootfs
systemd (larger embedded / complex)
Full-featured init system (parallel startup)
Service management, dependencies, socket activation
Logging (journald), device management (udev)
Mounts filesystems, configures network
More overhead but better for complex systems
Size: ~20–50 MB with systemd + dependencies

## Slide 29
Buildroot: Your First Root Filesystem
# Download and extract Buildroot $ tar xf buildroot-2024.02.tar.gz && cd buildroot-2024.02 # Select a default configuration $ make myboard_defconfig # Customize (optional) $ make menuconfig # Build everything: toolchain, kernel, rootfs $ make -j$(nproc) # Takes 30–60 minutes first time, 2–3 minutes incremental # Output location: # output/images/rootfs.tar <- compressed rootfs archive # output/images/rootfs.ext4 <- ready-to-flash ext4 image # output/images/zImage <- kernel # output/images/myboard.dtb <- device tree # Deploy to SD card partition 2 $ sudo tar xf output/images/rootfs.tar -C /mnt/p2

## Slide 30
Part 5: Lab
Build a bootable system from scratch

## Slide 31
Complete Boot Sequence
Power On
SoC internal ROM runs first
ROM → SPL
ROM loads Secondary Program Loader from SD card sector 0
SPL
Initializes DRAM, clocks, minimal peripherals
SPL → U-Boot
SPL loads U-Boot proper from SD partition
U-Boot
Full hardware init: UART, MMC, USB, network
U-Boot → Kernel
Loads zImage and .dtb into RAM, passes DTB address
Kernel
Decompresses, parses DTB, probes devices, mounts rootfs
Init
systemd or BusyBox init starts userspace services
Shell
Login prompt on serial console — you're in!

## Slide 32
Lab: Build a Bootable System
1
Set up toolchain
Install or download pre-built arm-linux-gnueabihf toolchain. Verify: arm-linux-gnueabihf-gcc --version
2
Build kernel
make ARCH=arm myboard_defconfig && make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- -j$(nproc) Image dtbs
3
Build rootfs with Buildroot
make myboard_defconfig && make -j$(nproc). Output: output/images/rootfs.ext4
4
Prepare SD card
Partition: 1 FAT32 (boot), 2 ext4 (rootfs). Copy zImage + .dtb to partition 1, extract rootfs to partition 2
5
Boot!
Insert SD card, connect serial cable, power on. Hit a key at U-Boot prompt to stop autoboot if needed.

## Slide 33
Lab: Flash and Boot — What to Look For
1
Serial console connection
Connect USB-to-serial adapter. screen /dev/ttyUSB0 115200. You should see U-Boot output immediately on power-on.
2
U-Boot output
Look for: DRAM init OK, MMC detected, kernel loaded. If you see 'Error' or 'CRC failed', your images are corrupted.
3
Kernel boot messages
After 'Starting kernel...', you will see Linux boot log. Look for: MMC probed, ext4 mounted, init started.
4
Login prompt
The final test: you get a login prompt. Login as root (no password in lab). Run 'uname -a' to verify.
5
Checkpoint
If you see 'Welcome to Buildroot' or a shell prompt, your bootable system is working!

## Slide 34
Common Pitfalls
Toolchain Issues
Wrong ABI: hard-float toolchain on soft-float kernel (or vice versa)
C library mismatch: compiled against glibc, running on musl
Always match toolchain to rootfs C library
Boot Issues
Wrong DTB: kernel can't find hardware, crashes early
Kernel entry point mismatch: U-Boot loads at wrong address
bootargs missing console= — no serial output after kernel starts
Root FS Issues
Missing /dev nodes: kernel can't find console or storage
Init not found: 'Kernel panic - not syncing: No init found'
Wrong filesystem type: kernel lacks ext4/ubifs support

## Slide 35
Session Summary
A toolchain compiles code for a target architecture — verify yours before building anything.
U-Boot is the standard embedded bootloader — learn the console commands early.
Kernel build is a 3-step cycle: configure, compile, verify — always check arch and ABI.
Device Tree replaces board files — one kernel, many boards via different DTBs.
Root filesystem contains everything userspace needs — Buildroot makes it easy to build.
The full boot chain is: ROM → SPL → U-Boot → Kernel → Init — know each stage.