## Slide 1
Session 5: Linux Kernel Overview
Modules, Build, Boot, and Init
UCSC Extension • Embedded Linux Design
Embedded Linux Design • Session 5 • Linux Kernel Overview

## Slide 2
Today's Roadmap
Kernel Fundamentals
Kernel Modules
Kernel Build & Config
Boot & Init Process
Debug & Summary

## Slide 3
Kernel Architecture
Userspace
▸ Applications (bash, python, sshd, etc.)
▸ C Library (glibc, musl)
▸ System Call Interface
System Calls (read, write, open, ioctl, mmap, fork, exec...) The kernel boundary. Userspace calls kernel via system calls. Kernel validates requests, accesses hardware, returns results.
Kernel Space
▸ Process Scheduler (CFS, RT scheduler)
▸ Virtual Memory Manager (page tables, swap)
▸ VFS → ext4, UBIFS, proc, sysfs
▸ Network Stack (TCP/IP, sockets)
▸ Device Drivers (MMC, I2C, SPI, USB, GPU)
Hardware (CPU, DRAM, Flash, Peripherals)

## Slide 4
Kernel Space vs Userspace
Userspace
✓ Virtual memory (own address space)
✓ Restricted CPU mode (unprivileged)
✓ Access kernel via system calls only
✓ Crashed process → kernel handles it
✓ Examples: bash, sshd, Python apps
✓ Libc provides syscall wrappers
Kernel Space
✓ Full CPU privilege (supervisor mode)
✓ Access all memory and hardware
✓ Handles interrupts and exceptions
✓ Manages processes and scheduling
✓ Runs device drivers
✓ Single crash → entire system panics

## Slide 5
Kernel Modules
What are Modules?
Loadable Kernel Modules (LKM) are object files (.ko) that can be loaded and unloaded into the kernel at runtime. Benefits: • No reboot to add drivers • Reduce kernel size • Load only what's needed Two types: • Built-in (y) → always loaded • Module (m) → loaded on demand
Module Commands
# List loaded modules: $ lsmod # Load a module: $ insmod mydriver.ko $ modprobe mydriver (loads dependencies too) # Remove a module: $ rmmod mydriver # Module info: $ modinfo mydriver.ko # Load at boot: echo "mydriver" >> /etc/modules-load.d/mydriver.conf

## Slide 6
Writing a Kernel Module
#include <linux/init.h> #include <linux/module.h> #include <linux/kernel.h> static int __init mydriver_init(void) { printk(KERN_INFO "mydriver: loaded\n"); return 0; // 0 = success, negative = error } static void __exit mydriver_exit(void) { printk(KERN_INFO "mydriver: unloaded\n"); } module_init(mydriver_init); module_exit(mydriver_exit); MODULE_LICENSE("GPL"); MODULE_AUTHOR("Student"); MODULE_DESCRIPTION("A simple driver example"); MODULE_VERSION("1.0"); // init: called when module is loaded (insmod/modprobe) // exit: called when module is unloaded (rmmod) // printk: kernel logging (not printf!) // Module metadata required for licensing

## Slide 7
Module Parameters
Code (mydriver.c)
static int blink_rate = 1000; static char *name = "mydriver"; module_param(blink_rate, int, 0644); MODULE_PARM_DESC(blink_rate, "Blink rate in ms"); module_param(name, charp, 0644); MODULE_PARM_DESC(name, "Device name"); // Types: int, long, short, uint, ushort // charp (string), bool, array
Usage
# Load with parameters: $ insmod mydriver.ko blink_rate=500 name="motor" # View parameters at runtime: $ cat /sys/module/mydriver/parameters/blink_rate 500 $ cat /sys/module/mydriver/parameters/name motor # View all: $ systool -v -m mydriver # Parameters are visible to all users when permissions are 0644

## Slide 8
Building Kernel Modules
Makefile
# Cross-compile module for ARM export ARCH=arm export CROSS_COMPILE=arm-linux-gnueabi- obj-m += mydriver.o all: make -C $(KERNEL_SRC) M=$(PWD) modules clean: make -C $(KERNEL_SRC) M=$(PWD) clean
Build Steps:
1. Build kernel first
$ make zImage modules dtbs
2. Point to kernel source
export KERNEL_SRC=/path/to/linux-6.1.50
3. Build module
$ make
4. Verify
$ file mydriver.ko → ELF 32-bit LSB relocatable, ARM
5. Deploy
$ scp mydriver.ko root@target:/lib/modules/$(uname -r)/

## Slide 9
Lab: Kernel Modules
Lab: Load/Unload Modules
$ insmod mydriver.ko [ 123.456789] mydriver: loaded $ insmod mydriver.ko blink_rate=500 name="mydevice" [ 234.567890] mydriver: loaded $ lsmod | grep mydriver mydriver 16384 0 $ cat /sys/module/mydriver/parameters/blink_rate 500 $ rmmod mydriver [ 345.678901] mydriver: unloaded $ dmesg | tail -5 [ 123.456789] mydriver: loaded [ 234.567890] mydriver: loaded [ 345.678901] mydriver: unloaded # Force remove (dangerous!): $ rmmod -f mydriver # Load with modprobe (reads /etc/modprobe.d/): $ modprobe mydriver

## Slide 10
Kernel Versioning & Source Tree
Version Format (6.1.50)
MAJOR.MINOR.PATCH[-EXTRA] 6 . 1 . 50 │ │ │ │ │ └─ Bug fixes, patches │ └─────── Backport fixes from │ newer kernels └──────────────── Major version (rarely changes) Longterm (LTS): 6.1.y maintained for 2+ Regular: 6.x.y maintained for ~6 months Check version: $ uname -r 6.1.50-rt15-v8+
Source Tree (Top-Level)
linux-6.1.50/ ├── arch/ ├── kernel/ │ ├── arm/ │ ├── sched/ │ ├── arm64/ │ ├── irq/ │ ├── x86/ │ └── fork.c │ └── riscv/ │ │ ├── drivers/ ├── mm/ │ ├── net/ ├── fs/ │ ├── mmc/ │ ├── ext4/ │ ├── i2c/ │ ├── ubifs/ │ └── gpio/ │ └── proc/ │ │ ├── net/ ├── include/ └── sound/ ├── init/ ├── ipc/ └── lib/

## Slide 11
Kernel Build Process
1
1. Get Source
git clone https://git.kernel.org/pub/scm/linux/kernel/git/stable/linux.git git checkout v6.1.50
2
2. Configure
make ARCH=arm <board>_defconfig make ARCH=arm menuconfig
3
3. Build
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabi- -j$(nproc)
4
4. Output
arch/arm/boot/zImage arch/arm/boot/dts/<board>.dtdtb drivers/**/*.ko
$ make -j4 zImage dtbs 2>&1 | tail CALL scripts/atomic-checks CALL scripts/checksyscalls.sh KERNEL arch/arm/boot/zImage DTC arch/arm/boot/dts/am335x-boneblack.dtb # zImage: compressed kernel # dtb: device tree blob $ ls -lh arch/arm/boot/ -rwxr-xr-x 3.2M zImage -rw-r--r-- 45K am335x-boneblack.dtb # Modules: $ make modules_install INSTALL_MOD_PATH=/tmp/rootfs $ ls /tmp/rootfs/lib/modules/6.1.50/ kernel/ modules.dep modules.alias

## Slide 12
Embedded Linux Design • Session 5 • Linux Kernel Overview
Kernel Configuration
defconfig & menuconfig
# Use board default config: $ make ARCH=arm bb.org_defconfig (creates .config from arch/arm/configs/) # Interactive configuration: $ make ARCH=arm menuconfig → Submenus for drivers, filesystems → Enable/disable features → Save → updates .config # Save minimal config: $ make ARCH=arm savedefconfig → Creates minimal defconfig → Only non-default values # Common options for embedded: CONFIG_EMBEDDED=y CONFIG_MODULES=y CONFIG_BLK_DEV_INITRD=y CONFIG_TMPFS=y
Key .config Entries
# Essential for embedded: CONFIG_ARCH_MULTI_V7=y CONFIG_ARCH_OMAP2PLUS=y CONFIG_SOC_AM33XX=y CONFIG_MMC=y CONFIG_MMC_OMAP_HS=y CONFIG_SERIAL_OMAP=y CONFIG_SERIAL_OMAP_CONSOLE=y CONFIG_I2C_OMAP=y CONFIG_SPI_OMAP24XX=y CONFIG_EXT4_FS=y CONFIG_TMPFS=y CONFIG_SQUASHFS=y CONFIG_UBIFS_FS=y CONFIG_IPV6=y CONFIG_NETFILTER=y # Module support: CONFIG_MODULES=y CONFIG_MODULE_UNLOAD=y CONFIG_MODVERSIONS=y

## Slide 13
Kernel Boot Process
zImage loaded
U-Boot loads zImage + DTB into memory decompresses kernel
stext()
Kernel entry point setup_arch() → init_cpu() Detect SoC, init MMU
start_kernel()
Core kernel init scheduler, interrupts, timers memory management
rest_init()
Last kernel thread calls kernel_init() → init process
init process
/sbin/init or first userspace Mount rootfs, start services
[ 0.000000] Booting Linux on physical CPU 0x0 [ 0.000000] Linux version 6.1.50-v8+ [ 0.000000] CPU: ARMv7 Processor [413fc082] [ 0.000000] Machine model: TI AM335x BBB [ 0.000000] Memory: 512MB = 512MB total [ 0.000000] Memory policy: Data cache writeback [ 0.000000] pinctrl core: initialized pinctrl subsystem [ 0.000000] NET: Registered protocol family 16 [ 0.001000] am335x_pinmux 44e10800.pinmux: registered [ 0.002000] gpio-mux ocp:pinctrl@44e10800: probed [ 1.234567] mmc0: SDHCI controller on 48060000.mmc [ 2.345678] EXT4-fs (mmcblk0p2): mounted filesystem [ 2.456789] VFS: Mounted root (ext4 filesystem) [ 2.567890] Run /sbin/init as init process

## Slide 14
Kernel Boot Arguments
bootargs (U-Boot → Kernel)
# Set in U-Boot environment: setenv bootargs "console=ttyO0,115200n8 root=/dev/mmcblk0p2 rootfstype=ext4 rootwait rw omap_wdt.early_enable=1" # console: serial console device + baud rate # root: root filesystem device # rootfstype: filesystem type # rootwait: wait for root device # rw: mount read-write
Common Parameters
root=/dev/mmcblk0p2 # SD card partition 2 root=/dev/ubi0:rootfs # UBIFS root root=/dev/nfs # NFS root (debug) rootfstype=ext4 rootfstype=squashfs # Read-only root console=ttyO0,115200n8 # OMAP UART0 console=ttyAMA0,115200 # ARM PL011 console=ttyS0,115200 # x86 serial rootwait # Wait for device ro # Read-only (for squashfs) quiet # Suppress boot messages init=/bin/sh # Debug: skip init panic=5 # Reboot after 5s on panic

## Slide 15
The init Process
What is init?
PID 1: the first userspace process Started by the kernel after boot Parent of all other processes Never exits (kernel panics if it does) Responsibilities: 1. Mount filesystems 2. Start system services 3. Handle orphans (reparenting) 4. Handle SIGCHLD signals 5. Shutdown/reboot handling Config locations: /etc/inittab (BusyBox init) /etc/systemd/ (systemd) cmdline: init=/bin/sh (emergency)
init Kernel Parameter
# Default init: /sbin/init → /lib/systemd/systemd # Override via bootargs: init=/bin/sh # Emergency shell init=/bin/bash # Bash as init path (debug) # View current init: $ readlink /sbin/init ../lib/systemd/systemd # Check PID 1: $ ps -p 1 PID 1 ? 00:00:01 systemd # Orphaned processes are reparented to init: $ ps -o pid,ppid,comm | grep init PPID 1 = owned by init

## Slide 16
systemd
systemd Concepts
systemd is the modern init system Replaced SysV init, Upstart Key concepts: • Units: services, sockets, timers, mounts • Targets: like runlevels (multi-user.target) • Journald: structured logging • Bus activation: on-demand startup Unit types: .service → daemons .socket → socket activation .timer → cron replacement .mount → filesystem mounts .target → group of units .device → device events (udev)
systemd Commands
# List all units: $ systemctl list-units # Service management: $ systemctl start myapp.service $ systemctl stop myapp.service $ systemctl restart myapp.service $ systemctl status myapp.service # Enable/disable at boot: $ systemctl enable myapp.service $ systemctl disable myapp.service # View logs: $ journalctl -u myapp.service $ journalctl -u myapp.service -f # Active targets: $ systemctl get-default multi-user.target $ systemctl set-default graphical.target

## Slide 17
systemd Unit File
# /etc/systemd/system/myapp.service [Unit] Description=My Embedded Application After=network.target sshd.service Wants=network-online.target Requires=sshd.d.service [Service] Type=simple ExecStartPre=/usr/bin/myapp-init.sh ExecStart=/usr/bin/myapp --config /etc/myapp/config.yaml ExecReload=/bin/kill -HUP $MAINPID Restart=on-failure RestartSec=5 WatchdogSec=30 # Environment: Environment=MYAPP_ENV=production EnvironmentFile=/etc/myapp/env # Security: User=myapp Group=myapp ProtectSystem=true NoNewPrivileges=true [Install] WantedBy=multi-user.target

## Slide 18
systemd vs BusyBox Init
Feature
systemd
BusyBox init
Service management
systemctl start/stop
/etc/init.d/ scripts
Dependencies
Built-in (After=, Requires=)
Manual scripting
Logging
journald (structured)
syslog only
Socket activation
Yes (on-demand startup)
No
Timer/cron
systemd timers
cron daemon
Parallel startup
Yes (dependency graph)
Sequential
Memory footprint
~10 MB
~1 MB
Complexity
High
Low
Best for
Complex systems, rich features
Small, simple systems

## Slide 19
/proc and /sys
/proc (procfs)
Process and kernel information Virtual filesystem (in RAM) Key entries: /proc/cpuinfo CPU info /proc/meminfo Memory usage /proc/interrupts Interrupt counters /proc/devices Registered devices /proc/modules Loaded modules /proc/cmdline Kernel cmdline /proc/version Kernel version Per-process (PID): /proc/<pid>/status Process status /proc/<pid>/fd/ Open file descriptors /proc/<pid>/maps Memory mappings
/sys (sysfs)
Device and driver information Virtual filesystem (in RAM) Key entries: /sys/class/ Device classes (net, gpio, input) /sys/devices/ Device tree /sys/bus/ Bus types (i2c, spi, usb) /sys/module/ Module parameters /sys/kernel/ Kernel settings Common uses: /sys/class/gpio/ GPIO control /sys/class/net/ Network interface info /sys/class/leds/ LED control /sys/class/thermal/ Thermal zones /sys/class/power_supply/ Battery info Files readable AND writable: $ echo 1 > /sys/class/leds/led0/brightness $ cat /sys/class/thermal/thermal_zone0/temp

## Slide 20
Kernel Logs & Debug
dmesg Commands
# View all kernel messages: $ dmesg # Follow new messages: $ dmesg -w # Clear buffer: $ dmesg -C # Human-readable timestamps: $ dmesg -t # no timestamps $ dmesg -H # human-readable $ dmesg -T # local time # Filter by level: $ dmesg -l err,warn $ dmesg --level=err # Filter by facility: $ dmesg -f kern $ dmesg -f daemon # Recent messages: $ dmesg | tail -100 $ journalctl -k # kernel messages via journald # USB thermometer: [ 5.678] usb 1-1: New USB device [ 5.789] usb 1-1: Product: TempSensor [ 5.890] input: TempSensor as /devices/.../input3
Log Levels (printk)
KERN_EMERG 0 System is unusable KERN_ALERT 1 Action must be taken immediately KERN_CRIT 2 Critical conditions KERN_ERR 3 Error conditions KERN_WARNING 4 Warning conditions KERN_NOTICE 5 Normal but significant KERN_INFO 6 Informational KERN_DEBUG 7 Debug-level messages # Default console loglevel: $ cat /proc/sys/kernel/printk 4 4 1 7 (current, default, minimum, boot-time-default) # Change at runtime: $ echo 8 > /proc/sys/kernel/printk (print everything to console) # In code: printk(KERN_INFO "value: %d\n", val);

## Slide 21
Common Pitfalls
⚠ Module version mismatch
Module compiled against different kernel → Rebuild module against running kernel
⚠ Module not unloading
Module in use or reference count > 0 → Check lsmod, stop dependent services
⚠ Wrong console= parameter
Serial console doesn't print kernel messages → Check baud rate, UART device name
⚠ Kernel panic on rootfs
Wrong root= device or rootfstype → Check bootargs, partition table
⚠ systemd service not starting
Missing dependency or wrong unit file → Check: systemctl status + journalctl

## Slide 22
Session Summary
Linux kernel is monolithic but supports loadable modules
Kernel modules (.ko) can be loaded/unloaded at runtime
Build kernel with defconfig + menuconfig for your board
Bootargs tell the kernel where rootfs lives (root=, console=)
systemd (rich features) vs BusyBox init (minimal footprint)