## Slide 1
Session 9: Debugging & Profiling
GDB, Tracing, Performance Analysis & Memory Management
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: Welcome to Session 9. Today we shift from building to observing and fixing. By the end of this session, you will be able to use GDB for remote debugging of embedded targets, profile system performance with perf and ftrace, trace system calls with strace, and identify memory leaks and OOM conditions. We will also cover why the observer effect matters and how to choose the right tool for the job. Expect hands-on time with kernel Oops analysis, perf stat, and memory leak detection.
Prerequisites: Sessions 6 (kernel architecture) and 7 (systems programming). Students should have GDB installed on their host.

## Slide 2
Learning Objectives
Use GDB for application debugging natively and remotely via gdbserver
Analyze postmortem core files and kernel Oops messages
Profile system performance with perf, ftrace, and LTTng
Trace system calls and library calls with strace
Detect memory leaks and diagnose out-of-memory conditions
Choose the right debugging and profiling tool for a given problem
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: These six objectives map directly to what embedded Linux engineers do daily. GDB remote debugging is not optional -- when your target has no keyboard or display, gdbserver over serial or TCP is the only way. Core file analysis lets you debug crashes that happened in the field. Profiling with perf is how you find the 5% of code consuming 80% of CPU. strace is the first command you run when a program silently fails. And memory debugging is critical when you have 64MB of RAM and a leak that eats 2MB per hour.

## Slide 3
GDB: The GNU Project Debugger
What is GDB?
S
o
u
r
c
e
-
l
e
v
e
l
d
e
b
u
g
g
e
r
f
o
r
C
,
C
+
+
,
a
n
d
o
t
h
e
r
c
o
m
p
i
l
e
d
l
a
n
g
u
a
g
e
s
D
e
b
u
g
r
u
n
n
i
n
g
p
r
o
g
r
a
m
s
,
e
x
a
m
i
n
e
c
o
r
e
f
i
l
e
s
,
s
t
e
p
t
h
r
o
u
g
h
k
e
r
n
e
l
c
o
d
e
C
o
m
m
a
n
d
-
l
i
n
e
i
n
t
e
r
f
a
c
e
b
y
d
e
f
a
u
l
t
;
m
a
n
y
G
U
I
s
a
v
a
i
l
a
b
l
e
(
G
D
B
T
U
I
,
V
S
C
o
d
e
,
D
D
D
)
Two Debugging Modes
N
a
t
i
v
e
:
G
D
B
r
u
n
s
o
n
t
h
e
s
a
m
e
m
a
c
h
i
n
e
a
s
t
h
e
t
a
r
g
e
t
p
r
o
g
r
a
m
E
m
b
e
d
d
e
d
/
R
e
m
o
t
e
:
G
D
B
r
u
n
s
o
n
h
o
s
t
,
g
d
b
s
e
r
v
e
r
o
n
t
a
r
g
e
t
,
c
o
n
n
e
c
t
v
i
a
T
C
P
o
r
s
e
r
i
a
l
Key Principle
A
l
w
a
y
s
c
o
m
p
i
l
e
w
i
t
h
-
g
(
o
r
-
g
g
d
b
)
t
o
i
n
c
l
u
d
e
d
e
b
u
g
s
y
m
b
o
l
s
O
p
t
i
m
i
z
e
d
c
o
d
e
(
-
O
2
,
-
O
3
)
m
a
k
e
s
d
e
b
u
g
g
i
n
g
h
a
r
d
e
r
-
-
u
s
e
-
O
g
f
o
r
d
e
b
u
g
b
u
i
l
d
s
S
t
r
i
p
d
e
b
u
g
s
y
m
b
o
l
s
f
r
o
m
p
r
o
d
u
c
t
i
o
n
i
m
a
g
e
s
t
o
s
a
v
e
s
p
a
c
e
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: GDB is the most widely used debugger in the Linux world. It has been around since 1986 and is still the primary tool for C and C++ debugging. For embedded Linux, the remote debugging mode is what matters. You compile your program on the host with debug symbols, copy it to the target, start gdbserver, and connect from the host.
In Yocto, you add 'dbg-pkgs' to produce packages with debug symbols. In Buildroot, enable BR2_ENABLE_DEBUG. The -ggdb flag produces information specifically for GDB, while -g is more portable. For embedded, always use -ggdb.
One critical debugging principle: never try to debug optimized code. The compiler reorders instructions, inlines functions, and eliminates variables. Use -Og which optimizes for debug experience.

## Slide 4
Preparing Code for Debugging
# Compile with debug symbols $ aarch64-none-linux-gnu-gcc -ggdb -o myapp myapp.c # Verify debug symbols are present $ file myapp myapp: ELF 64-bit LSB executable, ARM aarch64, version 1 (SYSV), dynamically linked, interpreter /lib/ld-linux-aarch64.so.1, with debug_info, not stripped <-- KEY: with debug_info $ readelf -S myapp | grep debug [27] .debug_info PROGBITS 0000000000000000 00003048 [28] .debug_abbrev PROGBITS 0000000000000000 00005021 [29] .debug_line PROGBITS 0000000000000000 00005110 # Compile flags comparison: # -g : Standard debug information # -ggdb : Extra GDB-specific information (recommended) # -Og : Optimize for debugging (since GCC 4.8) # -O0 : No optimization (easiest to debug, but not representative) # -O2/-O3 : Standard optimization (hard to debug) # For production: strip symbols into a separate file $ aarch64-none-linux-gnu-objcopy --only-keep-debug myapp myapp.debug $ aarch64-none-linux-gnu-strip --strip-debug myapp $ aarch64-none-linux-gnu-objcopy --add-gnu-debuglink=myapp.debug myapp
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: Students sometimes wonder why their breakpoints do not work or variables show as 'optimized out'. This slide shows the compilation pipeline. The -ggdb flag is specific to GCC and GDB -- it produces DWARF debug information that GDB can read.
The file command output is your quick check. If you see 'not stripped' and 'with debug_info', you are good. If you see 'stripped', you will not be able to use source-level debugging.
For production embedded systems, you strip the symbols from the binary on the but keep a copy of the unstripped version on the host. The --add-gnu-debuglink option lets GDB find the debug symbols from a separate file.

## Slide 5
Remote Debugging: gdbserver + cross-GDB
Target Side (embedded device)
Install gdbserver in rootfs (Buildroot: BR2_PACKAGE_GDBSERVER)
$ gdbserver :1234 ./myapp # Listen on TCP port 1234
$ gdbserver /dev/ttyS0 ./myapp # Or serial console
gdbserver loads program, sets breakpoint, waits for GDB
Controls execution of the target program
Translates memory/register reads to GDB remote protocol
Host Side (development machine)
Use cross-GDB from your toolchain
$ aarch64-none-linux-gnu-gdb ./myapp
(gdb) target remote 192.168.1.42:1234
(gdb) break main
(gdb) continue
(gdb) next / step / print var / backtrace
All normal GDB commands work transparently
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: This is the most important slide for embedded developers. You will rarely debug natively on the target. Instead, gdbserver runs on the embedded device and your cross-GDB runs on the host. The communication uses the GDB remote serial protocol over TCP or serial.
The key insight: GDB on the host knows about source code and debug symbols. gdbserver on the target knows about memory and registers. The remote protocol bridges them. When you type 'print x' in GDB, it sends a memory read request to gdbserver.
For network debugging, use 'target remote <ip>:<port>'. For serial, use a device path. The serial mode is common in early boot when the network is not up yet.

## Slide 6
Setting Up the Build System for Remote Debugging
Yocto Project
Add gdbserver to target image:
IMAGE_INSTALL:append = ' gdbserver'
Preserve debug symbols (prevent stripping):
INHIBIT_PACKAGE_STRIP = '1'
INHIBIT_SYSROOT_STRIP = '1'
Build and deploy SDK with GDB:
bitbake -c populate_sdk <image>
Run the SDK installer → get cross-GDB
Buildroot
Enable gdbserver in menuconfig:
Package Selection → Debugging, profiling → gdbserver
Enable GDB on host (for cross-debugging):
Same menu → gdb
No separation between build and app dev environments
Buildroot does not strip by default in debug builds
BR2_ENABLE_DEBUG = y
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: Yocto and Buildroot handle debug setup very differently. Yocto is more complex but more flexible -- you can install gdbserver into the target image and build an SDK that includes the cross-GDB. The INHIBIT_PACKAGE_STRIP variable prevents Yocto from stripping symbols, which it does by default to save space.
Buildroot is simpler: just enable gdbserver and gdb in the menus. Buildroot does not strip by default when BR2_ENABLE_DEBUG is set.
In both cases, you need the unstripped binary on the host for GDB to use. The stripped binary goes on the target.

## Slide 7
Core Files: Postmortem Debugging
# Enable core dumps on the target $ ulimit -c unlimited # Allow unlimited core size $ echo "/tmp/core.%e.%p" > /proc/sys/kernel/core_format # Trigger and capture a crash $ ./myapp Segmentation fault (core dumped) $ ls -lh /tmp/core.myapp.1234 -rw------- 1 root root 12M Jan 15 09:23 /tmp/core.myapp.1234 # Analyze the core file on the host with cross-GDB $ aarch64-none-linux-gnu-gdb ./myapp /tmp/core.myapp.1234 (gdb) bt #0 0x0000000000400568 in risky_function (ptr=0x0) at myapp.c:42 #1 0x00000000004005a4 in main () at myapp.c:87 (gdb) frame 0 (gdb) print ptr $1 = (int *) 0x0 (gdb) list myapp.c:42 40 void risky_function(int *ptr) { 41 // BUG: no null check! 42 *ptr = 42; ← Crash here 43 } # Key insight: core files capture the entire process state # at the moment of the crash -- memory, registers, stack
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: Core files are incredibly valuable in embedded because you often cannot attach a debugger in real-time. A device in the field crashes -- you retrieve the core file and analyze it on your host.
On many embedded systems, ulimit defaults to 0, meaning core dumps are disabled. You need to set it to unlimited in your startup scripts. The core_format proc entry lets you name cores with the executable name and PID for later identification.
The analysis workflow is identical to live debugging -- bt, frame, print, list. The only difference is that you cannot step forward. But you have the full state at the moment of the crash, which is usually enough.

## Slide 8
Debugging Kernel Code
kgdb (Kernel GDB)
Source-level kernel debugger over serial or Ethernet
Requires: CONFIG_KGDB=y in kernel config
Target connects to host GDB via kgdboc (kgdb over console)
echo ttyS0 > /sys/module/parameters/kgdboc
Then trigger: echo g > /proc/sysrq-trigger
GDB on host: can set breakpoints, inspect kernel memory
Useful for: driver debugging, oops analysis, boot failures
kdb (Built-in Kernel Debugger)
Self-hosted: no external dependencies
Simple command-line on serial console
Triggered via sysrq, oops, or breakpoint
Commands: md (memory display), bt (backtrace), go (continue)
Good for: quick checks, early boot, systems without GDB host
Limitation: no source-level debugging
Often used alongside printk for light debugging
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: Kernel debugging is a different world from application debugging. kgdb gives you full source-level debugging of the kernel, but it requires a serial or network connection to the host and CONFIG_KGDB built into the kernel. The target kernel stops and waits for GDB when you trigger it via sysrq.
kdb is lighter -- it is built into the kernel and accessible via serial console with no host needed. But it does not support source-level debugging. Many engineers use kdb for quick checks (is this function called? what is in this memory?) and kgdb for deep investigation.
For the course labs, we will trigger an intentional kernel oops and decode it, which is more practical than full kgdb setup for a classroom environment.

## Slide 9
Reading a Kernel Oops
# Trigger an oops for demonstration (DANGEROOD -- lab only!) # echo "hello" > /dev/null # safe way: use a test module # Sample Oops output (from serial console): Unable to handle kernel NULL pointer dereference at virtual address 00000000 pgd = c0004000 [00000000] *pgd=00000000 Internal error: Oops: 80000005 [#1] PREEMPT SMP ARM Modules linked in: my_driver CPU: 0 Not tainted 5.15.72-v7l #1 PC is at my_driver_write+0x14/0x30 [my_driver] LR is at vfs_write+0x128/0x260 pc : [<bf000014>] lr : [<c02a3b28>] psr: 60000013 # How to decode: # 1. PC (Program Counter) tells you WHERE it crashed # my_driver_write+0x14 = function + offset 0x14 bytes # 2. Use addr2line to find the source line: $ arm-none-linux-gnueabi-addr2line -e my_driver.ko -f -i my_driver_write+0x14 my_driver_write /home/dev/drivers/my_driver.c:87 # Or use GDB: $ arm-none-linux-gnueabi-gdb my_driver.ko (gdb) list *(my_driver_write+0x14) 85 static ssize_t my_driver_write(struct file *f, const char *buf, ...) { 86 // BUG: checking user buffer AFTER copy 87 copy_from_user(local_buf, buf, count); ← Oops here 88 if (count < 0 || count > MAX_BUF) 89 return -EINVAL;
Lab: Kernel Oops Analysis
Notes: Reading an Oops is a critical skill. When the kernel crashes, you get one shot at the output -- it is printed to the console and may scroll away. The Program Counter (PC) is the most important piece of information because it tells you exactly which instruction caused the crash.
The decode process: take the function name and offset from 'PC is at', then use addr2line with the unstripped kernel module or vmlinux to map it back to a source line. This requires keeping the unstripped vmlinux file on the host. In production, kernel symbols can be stored and matched later.
In the lab, students will intentionally trigger an oops using a buggy driver module and practice decoding it with addr2line. This is a real-world skill.

## Slide 10
GDB Command Cheat Sheet
Starting & Connecting
g
d
b
.
/
a
p
p
n
a
t
i
v
e
l
y
s
t
a
r
t
t
a
r
g
e
t
r
e
m
o
t
e
:
1
2
3
4
c
o
n
n
e
c
t
t
o
g
d
b
s
e
r
v
e
r
s
e
t
s
y
s
r
o
o
t
/
p
a
t
h
s
e
t
r
o
o
t
f
s
f
o
r
l
i
b
r
a
r
i
e
s
Breakpoints
b
r
e
a
k
m
a
i
n
a
t
f
u
n
c
t
i
o
n
b
r
e
a
k
f
i
l
e
.
c
:
4
2
a
t
l
i
n
e
w
a
t
c
h
v
a
r
o
n
w
r
i
t
e
r
w
a
t
c
h
v
a
r
o
n
r
e
a
d
i
n
f
o
b
r
e
a
k
p
o
i
n
t
s
l
i
s
t
a
l
l
d
e
l
e
t
e
2
r
e
m
o
v
e
b
r
e
a
k
p
o
i
n
t
#
2
Execution
c
o
n
t
i
n
u
e
(
o
r
c
)
r
u
n
t
o
n
e
x
t
b
r
e
a
k
p
o
i
n
t
n
e
x
t
(
o
r
n
)
s
t
e
p
o
v
e
r
s
t
e
p
(
o
r
s
)
s
t
e
p
i
n
t
o
f
i
n
i
s
h
r
u
n
u
n
t
i
l
f
u
n
c
t
i
o
n
r
e
t
u
r
n
s
u
n
t
i
l
l
i
n
e
r
u
n
u
n
t
i
l
l
i
n
e
n
u
m
b
e
r
Inspection
p
r
i
n
t
v
a
r
s
h
o
w
v
a
l
u
e
p
r
i
n
t
/
x
v
a
r
h
e
x
f
o
r
m
a
t
d
i
s
p
l
a
y
v
a
r
a
u
t
o
-
s
h
o
w
e
a
c
h
s
t
e
p
b
a
c
k
t
r
a
c
e
(
o
r
b
t
)
c
a
l
l
s
t
a
c
k
i
n
f
o
r
e
g
i
s
t
e
r
s
C
P
U
r
e
g
i
s
t
e
r
s
x
/
1
6
x
w
a
d
d
r
e
x
a
m
i
n
e
m
e
m
o
r
y
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: This is a reference slide -- students should screenshot it. In practice, the most commonly used GDB commands are: break, continue, next, step, print, backtrace, and info registers. Everything else is occasional.
A few tips that are not obvious:
- 'watch' is incredible for finding who changed a variable
- 'display' runs a print automatically after each step command
- 'set sysroot' is essential for cross-debugging to find shared library symbols
- In GDB TUI mode (Ctrl-X A), you see source code and registers simultaneously
Time for a quick live demo: start gdbserver on a target, connect from the host, set a breakpoint, and inspect a variable.

## Slide 11
The Observer Effect
Why Measurement Changes Behavior
Every probe costs CPU cycles
Profiling tools consume memory bandwidth
Tracing alters cache behavior (cache pollution)
Debug instrumentation adds code paths
Network debugging adds latency
Goal: minimize observer effect while gathering data
Rule: measure first, then instrument, then analyze
Symbol Tables and Compile Flags
Most tools need symbols to be useful
-g or -ggdb in compile flags
Some tools need special kernel options
CONFIG_FTRACE, CONFIG_PERF_EVENTS
CONFIG_KPROBES, CONFIG_UPROBES
May require building and deploying a new kernel
Trade-off: more info vs less representative results
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: This is a concept that many engineers overlook. When you attach a profiler to a program, you are changing its behavior. The profiler itself consumes CPU time, pollutes the cache, and may cause additional context switches. This means the profile you see is not exactly the profile of the unprofiled program.
The practical implication: use the least intrusive tool first. Start with 'top' or basic perf stat (which uses hardware counters and has near-zero overhead). Only move to more intrusive tools like function tracing when you need more detail.
For kernel tracing, you may need to rebuild the kernel with CONFIG_FTRACE and CONFIG_PERF_EVENTS. Plan for this in your development cycle.

## Slide 12
Profiling with perf
# perf is part of the kernel since 2.6.31 # Uses hardware performance counters (minimal overhead) # ─── Count events ─── $ perf stat ./myapp Performance counter stats for './myapp': 123.45 msec task-clock # 0.857 CPUs utilized 1,234 context-switches # 0.010 M/sec 5 cpu-migrations # 0.040 K/sec 123 page-faults # 0.996 K/sec 456,789,012 cycles # 3.700 GHz 234,567,890 instructions # 0.51 insn per cycle 45,678,901 branches # 370.020 M/sec 123,456 branch-misses # 0.27% of all branches # ─── Record call graph ─── $ perf record -g ./myapp $ perf report --stdio # Overhead Command Shared Object Symbol 45.23% myapp myapp [.] process_data 23.10% myapp myapp [.] read_sensor 12.34% myapp libc-2.31.so [.] memcpy 8.76% myapp myapp [.] calculate_average # ─── Profile specific events ─── $ perf record -e cache-misses ./myapp $ perf record -e branch-misses ./myapp # ─── Live system profiling ─── $ perf top # Like top, but per-function $ perf top -p <pid> # Profile specific process
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: perf is the single most useful profiling tool on Linux. It is part of the kernel source tree (tools/perf) and uses hardware performance counters that have near-zero overhead. On ARM, these counters are part of the PMU (Performance Monitoring Unit).
Start with 'perf stat' to get a quick overview: how many cycles, instructions, cache misses, page faults. The 'instructions per cycle' (IPC) metric is a quick health check -- below 1.0 means the CPU is stalling (usually on memory).
Then use 'perf record -g' to capture call graphs and 'perf report' to analyze them. The -g flag captures the call stack so you can see not just WHAT is slow but WHY.
perf top is like top but shows functions instead of processes. Great for finding CPU hogs on a running system.

## Slide 13
Function Tracing with ftrace
# ftrace is built into the kernel (since 2.6.27) # Mount debugfs (usually already mounted): $ mount -t debugfs none /sys/kernel/debug # ─── Available tracers ─── $ cat /sys/kernel/debug/tracing/available_tracers function function_graph nop # ─── Trace function calls ─── $ echo function > /sys/kernel/debug/tracing/current_tracer $ echo my_driver_write > /sys/kernel/debug/tracing/set_ftrace_filter $ echo 1 > /sys/kernel/debug/tracing/tracing_on # ... run your test ... $ echo 0 > /sys/kernel/debug/tracing/tracing_on $ cat /sys/kernel/debug/tracing/trace # ─── Function graph (shows call hierarchy + duration) ─── $ echo function_graph > /sys/kernel/debug/tracing/current_tracer $ cat /sys/kernel/debug/tracing/trace # CPU DURATION FUNCTION CALLS # | | | | | | | 0) | my_driver_write() { 0) 2.345 us | copy_from_user(); 0) 5.678 us | mutex_lock(); 0) + 12.345 us | } ← total time # ─── Trace events (lower overhead) ─── $ echo 1 > /sys/kernel/debug/tracing/events/sched/enable $ echo 1 > /sys/kernel/debug/tracing/events/irq/enable $ cat /sys/kernel/debug/tracing/trace_pipe # Live stream
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: ftrace is the kernel's built-in function tracer. It was created by Steven Rostedt to track down real-time scheduling latencies, which is why it is so good at measuring timing.
The function_graph tracer is particularly useful because it shows not just which functions were called, but how long each one took. This is invaluable for finding unexpected delays in driver code.
ftrace has some overhead when active, so use filters (set_ftrace_filter) to limit tracing to the functions you care about. The trace_pipe file gives you a live stream -- useful for watching events in real-time.
For production systems, ftrace can be configured at boot with kernel command line parameters so you can capture early boot traces.

## Slide 14
Advanced Tracing: LTTng & BPF
LTTng (Linux Trace Toolkit Next Generation)
Low-overhead kernel and userspace tracing
Three components: session daemon, consumer daemon, tracepoint probes
Designed for production systems (minimal overhead when not tracing)
Can trace across kernel + userspace boundary
Output: CTF (Common Trace Format) files
Analyze with Babeltrace or Trace Compass
Great for: multi-threaded apps, real-time systems
eBPF (Extended Berkeley Packet Filter)
Sandboxed VM running inside the kernel
Originally for network packet filtering (1992)
Now: general-purpose kernel tracing and monitoring
Tools: bpftrace, BCC (BPF Compiler Collection)
Can trace virtually any kernel or userspace event
Near-zero overhead when not actively tracing
Examples: opensnoop, execsnoop, biolatency
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: LTTng and eBPF represent the modern generation of tracing tools. LTTng was designed for production use -- it has near-zero overhead when not actively tracing, which means you can leave it installed in your production image and enable it when needed.
eBPF is the most significant addition to Linux tracing in the last decade. It lets you run small programs inside the kernel safely. Tools like bpftrace let you write one-liner tracing scripts: 'bpftrace -e 'tracepoint:syscalls:sys_enter_open { printf("%s %s\n", comm, str(args->filename)); }'' will trace every file open system call with the process name and filename.
For this course, we focus on ftrace and perf as the primary tools, but students should know LTTng and eBPF exist for more advanced use cases.

## Slide 15
strace & Valgrind
strace (System Call Tracer)
Captures all system calls made by a program
$ strace ./myapp # Trace all syscalls
$ strace -e open,read,write ./myapp # Filter
$ strace -p <pid> # Attach to running process
$ strace -c ./myapp # Summary counts
Use when: program fails silently, permission issues,
file not found, unexpected blocking
Low overhead, no recompilation needed
Valgrind (Memory Profiler)
Detects memory errors and leaks
$ valgrind --leak-check=full ./myapp
Finds: use-after-free, buffer overflows,
uninitialized reads, memory leaks
Also: cachegrind (cache profiling),
callgrind (call graph profiling)
High overhead (10-50x slower), use for testing only
Cannot run on cross-compiled ARM binaries directly
Run on host with qemu-arm or native ARM
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: strace is often the first tool I reach for when something is wrong and I do not know why. It requires no recompilation, no special setup. Just run your program under strace and watch what system calls it makes. If it is failing to open a file, you will see the open() call and its error code immediately.
The -c flag gives you a summary: how many of each syscall, how much time spent. This is a quick way to see if your program is I/O-bound (lots of read/write) or CPU-bound (few syscalls, lots of time in the kernel).
Valgrind is the gold standard for memory debugging. It catches errors that may not crash your program immediately but cause corruption later. The downside is massive slowdown (10-50x), so it is for testing, not production. For cross-compiled ARM code, you can use qemu-user to run the binary under Valgrind on the host.

## Slide 16
Poor Man's Profiler
# When you have GDB but no other tools # The idea: stop the program randomly and see what it's doing # 1. Attach to a running process $ gdb -p <pid> # 2. Take a backtrace (gdb) bt #0 0x7f3a in __poll () at poll.c:29 #1 0x4012 in main_loop () at app.c:156 #2 0x4089 in main () at app.c:234 # 3. Detach (program continues) (gdb) detach (gdb) quit # 4. Repeat 10-20 times # If you see the same function in most samples, # that's where the program spends its time # Automated version: $ for i in $(seq 1 20); do gdb -batch -ex "bt" -p <pid> 2>/dev/null sleep 1 done | sort | uniq -c | sort -rn # Sample output: 12 main_loop () at app.c:156 ← 60% of samples! 5 __poll () at poll.c:29 3 read_sensor () at sensor.c:42 # This is statistical sampling -- the law of large numbers # does the work. More samples = more accurate.
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: This is a technique from Brendan Gregg, one of the world's foremost performance engineers. It is surprisingly effective. The idea is simple: if you stop a program at random, the probability of seeing a particular function on the stack is proportional to how much time that function consumes.
If you take 20 samples and see main_loop() in 12 of them, main_loop() is consuming roughly 60% of the CPU time. This is the same principle that perf uses internally, but perf automates it with hardware timers.
The poor man's profiler is invaluable on minimal embedded systems where you may not have perf or ftrace available. If you have GDB (or even /proc/<pid>/stack), you can do statistical profiling.

## Slide 17
Choosing the Right Tool
Tool
What it measures
Overhead
When to use
GDB
Program state, execution flow
High (stops program)
Logic bugs, crashes, unexpected behavior
strace
System calls
Medium
Silent failures, permission issues, I/O problems
perf stat
Hardware counters
Very low
Quick performance overview, IPC, cache behavior
perf record
Call graph, hot functions
Low-Medium
Finding CPU bottlenecks, optimization targets
ftrace
Kernel function calls + timing
Medium-High
Kernel latency, driver timing, scheduling
LTTng
Kernel + userspace events
Low (when idle)
Production tracing, multi-threaded apps
eBPF/bpftrace
Any kernel/userspace event
Very low
Custom tracing, production monitoring
Valgrind
Memory errors, leaks
Very high (10-50x)
Memory bugs, buffer overflows, testing only
top
Per-process CPU/memory
Very low
Quick system overview, finding CPU/memory hogs
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: This comparison table is the practical takeaway from the profiling section. The key decision factors are: what do you need to measure, and how much overhead can you tolerate?
Start with the least intrusive tool. If top shows a process using 90% CPU, use perf record to find which function. If perf shows time in I/O, use strace to see which syscalls. If strace shows excessive read/write, use perf stat to check cache behavior. It is a funnel: broad measurement first, then targeted investigation.
For embedded systems, the constraint is often tool availability. perf and ftrace require kernel config options. strace and GDB are the most universally available.

## Slide 18
Lab: Profile a Misbehaving Application
1
1. Build the test application
cd /tmp && wget <course-server>/slowapp.c aarch64-none-linux-gnu-gcc -ggdb -O2 -o slowapp slowapp.c scp slowapp target:/tmp/
2
2. Initial observation
On target: /tmp/slowapp & On host: ssh target 'top' -- note CPU usage What process is consuming CPU? How much?
3
3. System call analysis
strace -cp <pid> Which syscalls are most frequent? Any unexpected patterns?
4
4. CPU profiling
perf record -g -p <pid> -- sleep 10 perf report --stdio Which functions are hottest? What is the call graph?
5
5. Fix and verify
The bug: unnecessary memory copy in the inner loop Fix: replace memcpy with pointer arithmetic Rebuild, redeploy, re-profile -- compare perf stat before/after
Lab: Profile a Misbehaving Application
Notes: This lab ties together the entire profiling section. Students work with a deliberately slow application and use the full tool chain: top for initial observation, strace for syscall analysis, perf for CPU profiling, and then fix the bug and verify.
The bug in slowapp.c is a classic: an unnecessary memcpy in a tight loop. Before the fix, perf report will show memcpy as the top consumer. After the fix, the CPU usage should drop dramatically.
Key teaching moment: show students the 'before' and 'after' perf stat side by side. The cycles count and IPC improvement make the value of profiling concrete.

## Slide 19
Virtual Memory Basics
How Linux Uses the MMU
Each process sees a full virtual address space
On 32-bit: 0x00000000 to 0xFFFFFFFF (4 GB)
Split: lower 3 GB = user space, upper 1 GB = kernel
Pages are 4 KB by default (configurable: 16 KB, 64 KB)
MMU translates virtual → physical via page tables
Page faults: kernel handles missing pages on demand
This is why malloc() succeeds even with 'no' physical memory
Process Memory Map
View with: cat /proc/<pid>/maps
Regions: text (code), data, bss, heap, shared libs, stack
Each region has permissions: r/w/x
Shared libraries mapped into multiple processes
mmap() regions for file-backed or anonymous mappings
Stack grows downward, heap grows upward
Use pmap <pid> for a readable summary
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: Virtual memory is the foundation of how Linux manages memory. Every process thinks it has a full 4 GB address space (on 32-bit). The MMU and page tables make this illusion work.
The key insight for embedded developers: malloc() does not allocate physical memory. It allocates virtual addresses. Physical pages are only assigned when the memory is actually accessed (demand paging). This is why you can malloc(1GB) on a system with 256 MB RAM -- until you touch all that memory.
The /proc/<pid>/maps file is incredibly useful for understanding how your program's memory is laid out. Show students this output for a running process.

## Slide 20
Kernel vs User Space Memory
Kernel Space
Not demand-paged: kmalloc() = real physical memory
Never swapped out or discarded
Allocated from a fixed pool (cannot grow dynamically)
kmalloc(): general purpose, physically contiguous
vmalloc(): virtually contiguous, not physically
Limited: typically 1 GB on 32-bit systems
Fragmentation is a real problem over time
User Space
Demand-paged: physical pages allocated on access
Can be swapped to disk (if swap is configured)
malloc() uses brk()/sbrk() for small allocations
malloc() uses mmap() for large allocations (>128 KB)
Copy-on-write: fork() shares pages until written
mlock() prevents swapping (important for RT)
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: The kernel/user space boundary is critical for embedded. Kernel memory is a fixed resource -- every kmalloc() reduces what is available for other kernel operations. If the kernel runs out of memory, the system panics. There is no OOM handling for kernel allocations.
User space memory is more flexible but has its own issues. malloc() uses two mechanisms: brk() extends the data segment for small allocations, and mmap() maps new pages for large ones. The 128 KB threshold is glibc's default (M_MMAP_THRESHOLD).
For real-time applications, mlock() is essential. It pins pages in physical memory so they cannot be swapped, eliminating page fault latency.

## Slide 21
Identifying Memory Leaks
# A memory leak: allocated memory that is never freed # Classic example: void process_data(void) { char *buf = malloc(1024); if (error_condition) return; ← LEAK: buf not freed on error path! // ... use buf ... free(buf); } # ─── Detection with Valgrind ─── $ valgrind --leak-check=full --show-leak-kinds=all ./myapp ==1234== HEAP SUMMARY: ==1234== in use at exit: 4,096 bytes in 4 blocks ==1234== total heap usage: 10 allocs, 6 frees ==1234== ==1234== 1,024 bytes in 1 blocks are definitely lost ==1234== at 0x4842200: malloc (vg_replace_malloc.c:309) ==1234== by 0x109237: process_data (myapp.c:45) ==1234== by 0x1093A1: main (myapp.c:89) # ─── Detection with mtrace (glibc) ─── #include <mcheck.h> int main(void) { mtrace(); // Start tracing // ... your code ... muntrace(); } $ MALLOC_TRACE=/tmp/mtrace.log ./myapp $ mtrace ./myapp /tmp/mtrace.log Memory not freed: ----------------- Address Size Caller 0x0000000000a4b010 0x400 at myapp.c:45 # ─── Detection with /proc ─── $ cat /proc/<pid>/status | grep VmRSS VmRSS: 24576 kB ← Resident set size (physical memory) # Watch this grow over time = likely leak
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: Memory leaks are especially dangerous in embedded systems because there is no one to restart the device when it runs out of memory. A leak of 1 KB per hour in a system with 64 MB RAM will crash the system in less than a year.
Valgrind is the most reliable detection tool. It tracks every malloc and free, and at exit reports exactly which allocations were not freed and where they were allocated. The --show-leak-kinds=all flag distinguishes 'definitely lost' (no pointer to the memory) from 'still reachable' (pointer exists but was not freed).
mtrace is lighter-weight -- it is built into glibc and requires only adding mtrace() and muntrace() calls. The mtrace command analyzes the log and reports unfreed blocks.
For long-running embedded systems, monitoring VmRSS over time is a simple leak detection strategy. If it grows without bound, you have a leak.

## Slide 22
Running Out of Memory (OOM)
Linux Overcommit Policy
Default: overcommit = heuristic (allow more than physical)
Most apps allocate more than they use (sparse arrays)
Works fine until everyone uses what they allocated
/proc/sys/vm/overcommit_memory: 0=heuristic, 1=always, 2=strict
Embedded systems: consider overcommit=2 (strict)
OOM Killer: last resort, kills largest/highest-score process
Score: based on memory usage, runtime, nice value
Preventing OOM Issues
Set memory limits: ulimit -v <KB> or setrlimit(RLIMIT_AS)
Monitor /proc/meminfo: MemFree, MemAvailable, SwapFree
Use mallopt(M_MMAP_THRESHOLD, ...) to control allocation strategy
Pre-allocate and pool memory at startup
Handle malloc() failures gracefully (always check return!)
For RT: mlock() critical pages to prevent page faults
Consider: cgroups memory controller for process isolation
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: The OOM killer is one of the most misunderstood parts of Linux memory management. Linux by default overcommits memory -- it lets processes allocate more than the system has. This works because most allocations are not fully used. But when processes actually touch all their allocated memory, the system runs out.
The OOM killer selects a process to kill based on a score. The score considers memory usage (higher = more likely to be killed), CPU time (longer = less likely), and nice value. You can adjust the score via /proc/<pid>/oom_score_adj.
For embedded systems, I recommend overcommit=2 (strict) so that malloc() fails instead of triggering the OOM killer. This lets your application handle the error gracefully. Always check malloc() return values -- this is not optional in embedded.

## Slide 23
mmap: Direct Hardware Register Access
# In embedded Linux, mmap is how you access hardware registers # from userspace (faster than ioctl for bulk access) # ─── Map physical memory into userspace ─── #include <sys/mman.h> #include <fcntl.h> int fd = open("/dev/mem", O_RDWR | O_SYNC); if (fd < 0) { perror("open /dev/mem"); return 1; } // Map a page of physical memory starting at 0x48000000 void *addr = mmap(NULL, getpagesize(), PROT_READ | PROT_WRITE, MAP_SHARED, fd, 0x48000000); // Physical address if (addr == MAP_FAILED) { perror("mmap"); return 1; } // Now access hardware registers directly! volatile uint32_t *reg = (uint32_t *)addr; uint32_t id = reg[0]; // Read register at offset 0 reg[1] = 0xDEADBEEF; // Write to register at offset 4 // Clean up munmap(addr, getpagesize()); close(fd); # ─── Key flags ─── # PROT_READ | PROT_WRITE - read/write access # MAP_SHARED - visible to other processes # MAP_PRIVATE - copy-on-write (changes not visible) # MAP_ANONYMOUS - no backing file (just memory) # O_SYNC - bypass cache (for device memory) # ─── Common uses ─── # - GPIO control via /dev/mem # - Shared memory between processes (MAP_SHARED | MAP_ANONYMOUS) # - Loading firmware into memory-mapped regions # - Zero-copy I/O with DMA buffers
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: mmap is one of the most powerful system calls in embedded Linux. It lets you map physical memory addresses into your process's virtual address space, giving you direct access to hardware registers from userspace.
The classic use case: accessing GPIO registers. On a typical SoC, GPIO control registers are at a known physical address (e.g., 0x48000000 for OMAP). By mmap'ing /dev/mem at that offset, you can read and write registers directly without going through a kernel driver.
Caveat: /dev/mem requires root access and is a security concern. Modern kernels restrict /dev/mem access (CONFIG_STRICT_DEVMEM). For production, use a proper kernel driver with mmap support. But for prototyping and debugging, /dev/mem is invaluable.
The volatile keyword is essential -- without it, the compiler may optimize away reads/writes to memory-mapped registers.

## Slide 24
Lab: Memory Leak Detection
1
1. Build the leaky application
cd /tmp && wget <course-server>/leaky.c gcc -ggdb -o leaky leaky.c ./leaky & # Run in background, note PID
2
2. Monitor memory growth
watch -n 1 'cat /proc/<pid>/status | grep VmRSS' Watch VmRSS grow over 30 seconds -- confirm the leak
3
3. Analyze with Valgrind
valgrind --leak-check=full ./leaky Note: which functions have unfreed allocations?
4
4. Fix the leak
Edit leaky.c: add free() before each early return Rebuild and re-run under Valgrind -- confirm 0 bytes leaked
5
5. Advanced: mtrace
Add mtrace()/muntrace() calls, rebuild Run with MALLOC_TRACE=/tmp/trace.log ./leaky Analyze with mtrace ./leaky /tmp/trace.log
Lab: Memory Leak Detection
Notes: This lab gives students hands-on experience with both Valgrind and mtrace. The leaky application has three leak paths: an early return after malloc, a loop that allocates without freeing on error, and a lost pointer (overwriting the last reference to allocated memory).
Step 2 (watching VmRSS) is important because it shows the real-world symptom of a leak: growing memory usage. In the field, this is often how leaks are first noticed.
Step 3 (Valgrind) shows the exact source locations. Students should see three definitely-lost blocks with the corresponding source lines.
Step 5 (mtrace) is optional but shows a lighter-weight alternative that can be used in production if Valgrind's overhead is too high.

## Slide 25
Debugging Workflow: A Systematic Approach
Reproduce
Can you trigger the bug reliably? If not, add logging and wait for it to recur
Observe
What are the symptoms? Crash, hang, wrong output? Check logs: dmesg, /var/log, serial console
Isolate
Narrow down: which process, which function? Use: top, strace, /proc/<pid>/maps
Instrument
Add targeted observation: GDB for logic, perf for performance, Valgrind for memory
Analyze
Examine the data: backtrace, profile report, memory leak report, Oops decode
Fix & Verify
Apply the fix, re-test, re-profile Confirm the bug is gone AND no regressions
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: This workflow slide ties the entire session together. Debugging is not random -- it is a systematic process. The most common mistake students make is jumping straight to GDB without first reproducing and observing. If you cannot reproduce the bug, you cannot verify the fix.
The 'Isolate' step is where tools like top and strace shine. They help you narrow down which process and which subsystem is involved before you invest time in detailed instrumentation.
The 'Fix & Verify' step is where I see the most bugs introduced. Students fix the symptom but not the cause, or they fix one thing and break another. Always re-run the full test suite after a fix.

## Slide 26
Quick Reference: What to Use When
Program crashes or segfaults
G
D
B
(
l
i
v
e
d
e
b
u
g
g
i
n
g
)
→
a
n
a
l
y
z
e
c
o
r
e
f
i
l
e
(
p
o
s
t
m
o
r
t
e
m
)
C
o
m
p
i
l
e
w
i
t
h
-
g
g
d
b
,
u
s
e
b
t
t
o
g
e
t
b
a
c
k
t
r
a
c
e
Program runs but produces wrong results
G
D
B
(
b
r
e
a
k
p
o
i
n
t
s
,
w
a
t
c
h
p
o
i
n
t
s
)
→
s
t
e
p
t
h
r
o
u
g
h
l
o
g
i
c
A
d
d
p
r
i
n
t
f
/
l
o
g
s
t
a
t
e
m
e
n
t
s
i
f
G
D
B
i
s
n
o
t
a
v
a
i
l
a
b
l
e
Program is slow or uses too much CPU
p
e
r
f
s
t
a
t
(
q
u
i
c
k
o
v
e
r
v
i
e
w
)
→
p
e
r
f
r
e
c
o
r
d
-
g
(
f
i
n
d
h
o
t
f
u
n
c
t
i
o
n
s
)
f
t
r
a
c
e
f
o
r
k
e
r
n
e
l
-
s
i
d
e
l
a
t
e
n
c
y
a
n
a
l
y
s
i
s
Program fails silently (no output, no crash)
s
t
r
a
c
e
(
c
h
e
c
k
s
y
s
c
a
l
l
s
)
→
l
o
o
k
f
o
r
e
r
r
o
r
c
o
d
e
s
(
e
r
r
n
o
)
C
h
e
c
k
:
o
p
e
n
(
)
,
r
e
a
d
(
)
,
w
r
i
t
e
(
)
,
c
o
n
n
e
c
t
(
)
f
a
i
l
u
r
e
s
Program uses too much memory over time
V
a
l
g
r
i
n
d
m
e
m
c
h
e
c
k
(
f
i
n
d
l
e
a
k
s
)
→
m
o
n
i
t
o
r
V
m
R
S
S
(
c
o
n
f
i
r
m
)
m
t
r
a
c
e
f
o
r
l
i
g
h
t
e
r
-
w
e
i
g
h
t
l
e
a
k
d
e
t
e
c
t
i
o
n
Kernel crashes or misbehaves
R
e
a
d
t
h
e
O
o
p
s
→
d
e
c
o
d
e
w
i
t
h
a
d
d
r
2
l
i
n
e
k
g
d
b
f
o
r
s
o
u
r
c
e
-
l
e
v
e
l
k
e
r
n
e
l
d
e
b
u
g
g
i
n
g
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: This is the 'cheat sheet' slide that students will photograph. It maps symptoms to tools. In practice, this is how experienced engineers think: 'my program crashed' → GDB; 'my program is slow' → perf; 'my program silently fails' → strace.
The key insight: start with the least intrusive tool that can answer your question. Do not start with GDB if strace can tell you the problem is a missing file. Do not start with ftrace if perf stat shows the problem is cache misses.
This slide also serves as a review of the entire session. Walk through each row and ask students: what would you see from this tool that tells you what is wrong?

## Slide 27
Session Summary
GDB: native and remote debugging, core files, kernel debugging with kgdb/kdb
perf: hardware counter profiling, call graph analysis, live system monitoring
ftrace: kernel function tracing, latency measurement, event tracing
strace: syscall tracing for quick diagnosis of silent failures
Valgrind: memory error detection, leak detection, cache profiling
Memory management: virtual memory, OOM handling, mmap for hardware access
Tool selection: start broad (top, strace), then targeted (GDB, perf, Valgrind)
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: Session 9 is one of the most practically valuable sessions in the course. These are the tools that embedded Linux engineers use every day. The key takeaway is not memorizing every GDB command or perf option -- it is knowing which tool to reach for and when.
In Session 10, we move to real-time systems. The debugging and profiling skills from today will be essential for measuring and verifying real-time behavior. Specifically, ftrace and perf are the primary tools for measuring scheduling latency, which is the core challenge in real-time Linux.

## Slide 28
Quiz & Assignment
Quiz (Canvas)
1
0
q
u
e
s
t
i
o
n
s
,
4
5
m
i
n
u
t
e
s
,
6
a
t
t
e
m
p
t
s
,
h
i
g
h
e
s
t
s
c
o
r
e
r
e
t
a
i
n
e
d
C
o
v
e
r
s
:
G
D
B
c
o
m
m
a
n
d
s
,
p
e
r
f
u
s
a
g
e
,
s
t
r
a
c
e
i
n
t
e
r
p
r
e
t
a
t
i
o
n
,
m
e
m
o
r
y
m
a
n
a
g
e
m
e
n
t
c
o
n
c
e
p
t
s
,
t
o
o
l
s
e
l
e
c
t
i
o
n
Assignment
1
.
S
e
t
u
p
r
e
m
o
t
e
d
e
b
u
g
g
i
n
g
:
c
r
o
s
s
-
c
o
m
p
i
l
e
a
t
e
s
t
p
r
o
g
r
a
m
,
r
u
n
g
d
b
s
e
r
v
e
r
o
n
t
h
e
t
a
r
g
e
t
,
c
o
n
n
e
c
t
f
r
o
m
h
o
s
t
G
D
B
,
s
e
t
a
b
r
e
a
k
p
o
i
n
t
,
i
n
s
p
e
c
t
a
v
a
r
i
a
b
l
e
2
.
P
r
o
f
i
l
e
t
h
e
t
e
s
t
p
r
o
g
r
a
m
w
i
t
h
p
e
r
f
s
t
a
t
a
n
d
p
e
r
f
r
e
c
o
r
d
3
.
S
u
b
m
i
t
:
s
c
r
e
e
n
s
h
o
t
o
f
G
D
B
s
e
s
s
i
o
n
+
p
e
r
f
r
e
p
o
r
t
o
u
t
p
u
t
Embedded Linux Design • Session 9 • Debugging, Tracing & Profiling
Notes: The assignment for this session is hands-on: students must demonstrate they can set up a complete remote debugging session and capture a profile. This is not optional -- these are the skills they will use in every embedded Linux job.
The quiz covers conceptual understanding: when to use which tool, what the output means, and the trade-offs between different approaches. It is open-book because in the real world, you look things up. What matters is knowing what to look for.