## Slide 1
Session 10: Real-Time Systems
Determinism, Latency, and the PREEMPT_RT Kernel
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: Welcome to the final session. Today we tackle real-time Linux -- one of the most nuanced topics in embedded systems. The key question: can Linux meet deadlines?
The answer is: yes, with the right configuration, but you need to understand what affects determinism and how to measure it. We will cover the PREEMPT_RT preemption model (now mainline since kernel 6.12!), sources of non-determinism, and how to measure scheduling latency with cyclictest and ftrace.
This session builds on everything from kernel architecture (session 6) through debugging and profiling (session 9). The lab at the end: measure latency on a real system.

## Slide 2
Learning Objectives
Define real-time computing: hard vs soft real-time, deadline, jitter
Identify sources of non-determinism in the Linux kernel
Understand the three preemption models and the PREEMPT_RT configuration
Explain threaded interrupts, priority inheritance, and rt-mutexes
Measure scheduling latency with cyclictest and interpret the results
Apply real-time tuning: CPU isolation, scheduling policy, memory locking
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: Real-time is about guarantees, not speed. A slow system that always meets its deadline is real-time. A fast system that occasionally misses is not.
PREEMPT_RT was fully merged into mainline Linux in version 6.12 (late 2024). This is a historic change -- for 20+ years, real-time support required a separate patch. Now it is a standard kernel configuration option.

## Slide 3
What Is Real-Time?
Hard vs Soft Real-Time
Hard real-time: MISSING a deadline is a system failure Examples: airbag controller, ABS brakes, pacemaker Requirement: worst-case latency must be bounded and acceptable Linux CANNOT guarantee hard real-time (no formal certification)
Soft real-time: missing a deadline degrades quality but is tolerable Examples: audio playback, video streaming, robot control Requirement: average latency low, jitter bounded Linux CAN provide soft real-time with proper tuning
Key Definitions
Deadline: the time by which a task MUST complete
Jitter: variation in response time (latency spread)
Latency: time from wake-up event to task execution
Determinism: system behaves predictably every time
Worst-case execution time (WCET): longest possible time
A real-time system is about GUARANTEES, not speed
A slow deterministic system > fast non-deterministic
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: The most important distinction: hard vs soft real-time. Linux is generally NOT suitable for hard real-time because it cannot provide formal worst-case guarantees. For that, you need a dedicated RTOS (FreeRTOS, VxWorks, QNX).
But Linux IS capable of soft real-time, which covers many embedded applications. With PREEMPT_RT and proper tuning, Linux can achieve sub-millisecond latencies.
Key insight: real-time is not about being fast. It is about being PREDICTABLE.

## Slide 4
Real-Time Scheduling Policies in Linux
SCHED_FIFO
F
i
r
s
t
I
n
,
F
i
r
s
t
O
u
t
r
e
a
l
-
t
i
m
e
p
o
l
i
c
y
T
a
s
k
r
u
n
s
u
n
t
i
l
i
t
s
l
e
e
p
s
,
i
s
p
r
e
e
m
p
t
e
d
b
y
h
i
g
h
e
r
-
p
r
i
o
r
i
t
y
R
T
t
a
s
k
,
o
r
e
x
i
t
s
N
o
t
i
m
e
s
l
i
c
i
n
g
a
m
o
n
g
s
a
m
e
-
p
r
i
o
r
i
t
y
t
a
s
k
s
P
r
i
o
r
i
t
y
r
a
n
g
e
:
1
(
l
o
w
)
t
o
9
9
(
h
i
g
h
)
SCHED_RR
R
o
u
n
d
-
R
o
b
i
n
r
e
a
l
-
t
i
m
e
p
o
l
i
c
y
L
i
k
e
S
C
H
E
D
_
F
I
F
O
b
u
t
w
i
t
h
a
t
i
m
e
q
u
a
n
t
u
m
(
d
e
f
a
u
l
t
:
1
0
0
m
s
)
S
a
m
e
-
p
r
i
o
r
i
t
y
t
a
s
k
s
t
a
k
e
t
u
r
n
s
P
r
i
o
r
i
t
y
r
a
n
g
e
:
1
(
l
o
w
)
t
o
9
9
(
h
i
g
h
)
SCHED_DEADLINE
E
a
r
l
i
e
s
t
D
e
a
d
l
i
n
e
F
i
r
s
t
(
E
D
F
)
s
c
h
e
d
u
l
i
n
g
E
a
c
h
t
a
s
k
d
e
c
l
a
r
e
s
:
r
u
n
t
i
m
e
,
p
e
r
i
o
d
,
d
e
a
d
l
i
n
e
S
c
h
e
d
u
l
e
r
p
i
c
k
s
t
h
e
t
a
s
k
w
i
t
h
e
a
r
l
i
e
s
t
d
e
a
d
l
i
n
e
B
e
s
t
f
o
r
m
u
l
t
i
m
e
d
i
a
,
p
e
r
i
o
d
i
c
c
o
n
t
r
o
l
l
o
o
p
s
A
v
a
i
l
a
b
l
e
s
i
n
c
e
L
i
n
u
x
3
.
1
4
Setting the policy
p
t
h
r
e
a
d
_
s
e
t
s
c
h
e
d
p
a
r
a
m
(
p
t
h
r
e
a
d
,
S
C
H
E
D
_
F
I
F
O
,
&
p
a
r
a
m
)
s
c
h
e
d
_
s
e
t
s
c
h
e
d
u
l
e
r
(
p
i
d
,
S
C
H
E
D
_
F
I
F
O
,
&
p
a
r
a
m
)
c
h
r
t
-
f
-
p
5
0
<
p
i
d
>
(
c
h
r
t
t
o
o
l
,
F
I
F
O
,
p
r
i
o
r
i
t
y
5
0
)
R
e
q
u
i
r
e
s
r
o
o
t
o
r
C
A
P
_
S
Y
S
_
N
I
C
E
c
a
p
a
b
i
l
i
t
y
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: SCHED_FIFO is the most commonly used real-time policy for embedded. A SCHED_FIFO task at priority 50 always runs before any SCHED_OTHER (normal) task.
Warning: a SCHED_FIFO task at priority 99 that never sleeps will lock out everything else on that CPU. Always design RT tasks to sleep or yield.
SCHED_DEADLINE uses EDF scheduling which theoretically provides 100% CPU utilization while meeting all deadlines, but is more complex to configure.

## Slide 5
Kernel Preemption Models
Standard Preemption Options
CONFIG_PREEMPT_NONE (No Forced Preemption) Kernel code runs to completion (no kernel preemption) Lowest overhead, highest latency Best for: throughput-bound servers
CONFIG_PREEMPT_VOLUNTARY (Voluntary Preemption) Explicit preemption points added to kernel code Reduces latency without major throughput impact Default for desktop/server kernels
CONFIG_PREEMPT (Fully Preemptible Kernel) Kernel code can be preempted at almost any point Lower latency, slightly higher overhead Best for: desktop, interactive systems
PREEMPT_RT (Real-Time Preemption)
CONFIG_PREEMPT_RT = y Most aggressive preemption: maximum kernel preemptibility Spinlocks converted to rt-mutexes (sleeping mutexes) Interrupt handlers run as kernel threads High-resolution timers (nanosecond precision)
HISTORIC: Merged into mainline Linux 6.12 (2024) No longer requires a separate patch! Available as a standard kernel config option
Yocto: add 'preempt-rt' to PREFERRED_PROVIDER_virtual/kernel Buildroot: Kernel → Preemption Model → Full RT
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: For over 20 years, PREEMPT_RT required a separate patch. In 2024, the core changes were merged into mainline kernel 6.12. This is a historic milestone.
What PREEMPT_RT does: converts spinlocks to rt-mutexes (sleeping mutexes with priority inheritance), runs interrupt handlers as kernel threads, and enables high-resolution timers. Result: the kernel can be interrupted almost anywhere.
For Yocto: select the preempt-rt kernel variant. For Buildroot: change the preemption model in kernel configuration.

## Slide 6
Understanding Scheduling Latency
What Is Scheduling Latency?
T
i
m
e
f
r
o
m
a
w
a
k
e
-
u
p
e
v
e
n
t
(
i
n
t
e
r
r
u
p
t
,
s
i
g
n
a
l
)
t
o
w
h
e
n
t
h
e
t
a
s
k
a
c
t
u
a
l
l
y
s
t
a
r
t
s
r
u
n
n
i
n
g
o
n
t
h
e
C
P
U
.
T
h
i
s
i
s
t
h
e
P
R
I
M
A
R
Y
m
e
t
r
i
c
f
o
r
r
e
a
l
-
t
i
m
e
p
e
r
f
o
r
m
a
n
c
e
.
Sources of Latency
1
.
H
a
r
d
w
a
r
e
:
i
n
t
e
r
r
u
p
t
c
o
n
t
r
o
l
l
e
r
d
e
l
a
y
(
m
i
c
r
o
s
e
c
o
n
d
s
)
2
.
I
n
t
e
r
r
u
p
t
h
a
n
d
l
i
n
g
:
t
i
m
e
t
o
r
u
n
I
S
R
/
t
h
r
e
a
d
e
d
I
R
Q
3
.
S
c
h
e
d
u
l
e
r
:
t
i
m
e
t
o
d
e
c
i
d
e
w
h
i
c
h
t
a
s
k
t
o
r
u
n
4
.
C
o
n
t
e
x
t
s
w
i
t
c
h
:
t
i
m
e
t
o
s
a
v
e
/
r
e
s
t
o
r
e
C
P
U
s
t
a
t
e
5
.
K
e
r
n
e
l
c
r
i
t
i
c
a
l
s
e
c
t
i
o
n
s
:
t
i
m
e
w
i
t
h
i
n
t
e
r
r
u
p
t
s
d
i
s
a
b
l
e
d
6
.
O
t
h
e
r
R
T
t
a
s
k
s
:
h
i
g
h
e
r
-
p
r
i
o
r
i
t
y
R
T
t
a
s
k
s
m
u
s
t
c
o
m
p
l
e
t
e
f
i
r
s
t
Typical Numbers (ARM Cortex-A, PREEMPT_RT, tuned)
B
e
s
t
c
a
s
e
(
i
d
l
e
s
y
s
t
e
m
)
:
5
-
2
0
m
i
c
r
o
s
e
c
o
n
d
s
T
y
p
i
c
a
l
(
l
i
g
h
t
l
o
a
d
)
:
2
0
-
1
0
0
m
i
c
r
o
s
e
c
o
n
d
s
W
o
r
s
t
c
a
s
e
(
h
e
a
v
y
I
/
O
+
b
a
c
k
g
r
o
u
n
d
)
:
1
0
0
-
1
0
0
0
+
m
i
c
r
o
s
e
c
o
n
d
s
W
i
t
h
o
u
t
P
R
E
E
M
P
T
_
R
T
:
w
o
r
s
t
c
a
s
e
c
a
n
b
e
1
0
+
m
i
l
l
i
s
e
c
o
n
d
s
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: Scheduling latency is the core metric for real-time systems. It is NOT the same as context switch time -- context switch is just one component.
These numbers are typical for an ARM Cortex-A72 (RPi4) class processor. The way to know YOUR system is to measure it with cyclictest.
The dramatic difference: without PREEMPT_RT, worst-case can exceed 10 ms (the old CONFIG_HZ tick period). With PREEMPT_RT: typically under 100 us.

## Slide 7
Priority Inheritance & rt-mutex
# Classic priority inversion problem: # T=0: Low-priority task (L) locks mutex # T=1: High-priority task (H) tries to lock mutex -> blocks # T=2: Medium-priority task (M) preempts L # T=3: M runs for a long time... # T=100: M finishes, L resumes, unlocks mutex # T=101: H finally runs # Result: H (highest priority) was delayed by M (lower priority)! # Linux solution: Priority Inheritance (PI) # When H blocks on mutex held by L, L temporarily inherits H's priority. # M cannot preempt L (L is now "high priority"). # L finishes quickly, unlocks, H runs immediately. # PREEMPT_RT: ALL spinlocks become rt-mutexes # rt-mutexes = sleeping mutexes with priority inheritance # No busy-waiting, bounded wait times # Tradeoff: slightly more overhead per lock/unlock # In code: pthread_mutexattr_setprotocol(&attr, PTHREAD_PRIO_INHERIT); pthread_mutexattr_settype(&attr, PTHREAD_MUTEX_RECURSIVE); pthread_mutex_init(&mtx, &attr); # Famous real-world case: Mars Pathfinder (1997) # Priority inversion caused system resets on Mars. # Fix: enable priority inheritance on the mutex.
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: Priority inheritance is critical for real-time. The Mars Pathfinder mission (1997) famously experienced this: a high-priority bus task was blocked by medium-priority communication tasks while a low-priority meteorology task held a shared mutex.
PREEMPT_RT converts ALL spinlocks to rt-mutexes, meaning ALL kernel locks support priority inheritance. This is a huge change from mainline where spinlocks busy-wait.

## Slide 8
Threaded Interrupt Handlers
Traditional Interrupt Handling
Interrupt arrives -> CPU jumps to ISR
ISR runs with interrupts DISABLED on this CPU
ISR must be very short (microseconds)
Deferred work goes to tasklet or workqueue
Problem: ISR disables ALL interrupts -> increases latency
Long ISR = longer interrupt-off periods = higher latency
No priority: ISR always wins over any task
Threaded Interrupts (PREEMPT_RT)
Interrupt handler runs as a SCHED_FIFO thread
Two parts: hard IRQ (quick check) + thread handler (full work)
Interrupt thread has configurable priority (e.g., SCHED_FIFO, priority 50)
RT tasks at priority 51+ will preempt the interrupt handler!
request_threaded_irq(irq, quick_check, thread_fn, flags, name, dev)
Result: interrupt handling no longer blocks real-time tasks
This is the single biggest latency reduction from PREEMPT_RT
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: Threaded interrupts are the single most impactful PREEMPT_RT change. In traditional Linux, interrupt handlers run with interrupts disabled -- NO task can run, not even your highest-priority RT task.
With threaded interrupts, the hard IRQ does minimal work. The actual processing happens in a kernel thread at a configurable priority. Your SCHED_FIFO priority 80 task will preempt the interrupt handler thread.
See interrupt threads in ps: '[irq/<number>-<name>]' as kernel threads.

## Slide 9
High-Resolution Timers
The Problem: Tick-Based Timers
Traditional Linux timer resolution = tick period (CONFIG_HZ)
CONFIG_HZ=100 (embedded default): 10 ms resolution
CONFIG_HZ=250 (desktop): 4 ms resolution
Task sleeping for 1 ms actually sleeps 4-10 ms!
nanosleep(1ms) -> wakes up at next tick boundary
High tick rate -> more timer interrupts -> more overhead
Resolution vs overhead trade-off
High-Resolution Timers (hrtimers)
hrtimers use hardware timers (not the periodic tick)
Resolution: nanoseconds (hardware dependent)
nanosleep(1ms) actually sleeps 1 ms (+/- a few microseconds)
nanosleep(100us) -> 100 us with PREEMPT_RT
Enabled by: CONFIG_HIGH_RES_TIMERS=y
Critical for: periodic control loops, precise timing
PREEMPT_RT enables tickless mode: kernel tick paused when no timers are pending (reduces jitter)
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: Timer resolution is a hidden source of jitter. With HZ=100, nanosleep(1ms) actually sleeps 0-10 ms (average 5 ms). hrtimers use the hardware timer directly, bypassing the tick system. Resolution: nanoseconds.
PREEMPT_RT enables tickless idle: the periodic tick is paused when no timers are pending. This eliminates a periodic source of jitter.

## Slide 10
Avoiding Page Faults in Real-Time Code
# Page faults: major source of non-determinism # First access to unmapped page -> fault -> kernel maps physical page # Time: microseconds to milliseconds (if swap involved) #include <sys/mman.h> int main(void) { // Lock current and future memory into RAM if (mlockall(MCL_CURRENT | MCL_FUTURE) == -1) { perror("mlockall"); return 1; } // All memory is now pinned. No page faults from here. } // Pre-fault the stack at startup: volatile char stack_touch[8192]; for (int i = 0; i < sizeof(stack_touch); i += 4096) stack_touch[i] = 0; // Pre-allocate and touch heap memory: void *buf = malloc(WORKING_SET_SIZE); if (buf) memset(buf, 0, WORKING_SET_SIZE); // Touch every page // Disable swapping on target: // swapoff -a // echo 0 > /proc/sys/vm/swappiness // Disable mmap in glibc (use sbrk instead): #include <malloc.h> mallopt(M_MMAP_THRESHOLD, 0);
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: Page faults are one of the easiest latency sources to eliminate entirely. mlockall(MCL_CURRENT | MCL_FUTURE) locks all current and future pages in RAM.
Pre-faulting the stack prevents page faults during deep function calls in the critical path. The volatile keyword prevents the compiler from optimizing away the access.
Your total working set must fit in RAM for mlockall to be viable.

## Slide 11
Interrupt Shielding & CPU Isolation
Interrupt Shielding
Redirect non-RT interrupts to specific CPUs
Keep RT CPUs free from non-critical interrupt handling
# Move all interrupts away from CPU 3 (RT CPU):
for irq in /proc/irq/*/smp_affinity; do
echo "0x7" > $irq # Allow CPUs 0,1,2 only
done
# Now CPU 3 handles no device interrupts
# Move specific IRQ to CPU 0:
echo 0 > /proc/irq/<num>/smp_affinity_list
CPU Isolation
Isolate a CPU from the Linux scheduler entirely
No kernel threads, no IRQs, no tasks on that CPU
# At boot (kernel command line):
isolcpus=3 # Isolate CPU 3
nohz_full=3 # No periodic tick on CPU 3
rcu_nocbs=3 # No RCU callbacks on CPU 3
# Pin RT task to isolated CPU:
taskset -c 3 ./rt-task
Result: your task runs on a dedicated CPU with minimal interruptions. Lowest possible latency.
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: CPU isolation is the most aggressive (and most effective) RT optimization. You dedicate one or more CPUs entirely to your real-time task.
isolcpus removes the CPU from the scheduler's available list. nohz_full disables the periodic tick. rcu_nocbs offloads RCU callback processing.
Downside: you lose a CPU for general-purpose work. Trade-off: one CPU contributes nothing to throughput but gives lowest possible latency.

## Slide 12
Other Sources of Non-Determinism
TLB Misses
T
r
a
n
s
l
a
t
i
o
n
L
o
o
k
a
s
i
d
e
B
u
f
f
e
r
:
c
a
c
h
e
f
o
r
v
i
r
t
u
a
l
-
>
p
h
y
s
i
c
a
l
m
a
p
p
i
n
g
M
i
s
s
:
w
a
l
k
p
a
g
e
t
a
b
l
e
s
(
m
e
m
o
r
y
a
c
c
e
s
s
,
m
i
c
r
o
s
e
c
o
n
d
s
)
M
i
t
i
g
a
t
i
o
n
:
u
s
e
h
u
g
e
p
a
g
e
s
(
2
M
B
/
1
G
B
)
t
o
r
e
d
u
c
e
T
L
B
p
r
e
s
s
u
r
e
e
c
h
o
2
0
>
/
p
r
o
c
/
s
y
s
/
v
m
/
n
r
_
h
u
g
e
p
a
g
e
s
CPU Frequency Scaling
D
V
F
S
c
h
a
n
g
e
s
C
P
U
c
l
o
c
k
s
p
e
e
d
d
y
n
a
m
i
c
a
l
l
y
F
r
e
q
u
e
n
c
y
c
h
a
n
g
e
-
>
t
i
m
i
n
g
i
n
s
t
a
b
i
l
i
t
y
d
u
r
i
n
g
t
r
a
n
s
i
t
i
o
n
M
i
t
i
g
a
t
i
o
n
:
s
e
t
g
o
v
e
r
n
o
r
t
o
'
p
e
r
f
o
r
m
a
n
c
e
'
e
c
h
o
p
e
r
f
o
r
m
a
n
c
e
>
/
s
y
s
/
d
e
v
i
c
e
s
/
s
y
s
t
e
m
/
c
p
u
/
c
p
u
0
/
c
p
u
f
r
e
q
/
s
c
a
l
i
n
g
_
g
o
v
e
r
n
o
r
Cache Contention
O
t
h
e
r
t
a
s
k
s
i
n
v
a
l
i
d
a
t
e
y
o
u
r
c
a
c
h
e
l
i
n
e
s
(
t
h
r
a
s
h
i
n
g
)
C
P
U
m
i
g
r
a
t
i
o
n
l
o
s
e
s
a
l
l
c
a
c
h
e
d
d
a
t
a
M
i
t
i
g
a
t
i
o
n
:
p
i
n
t
a
s
k
t
o
s
p
e
c
i
f
i
c
C
P
U
,
u
s
e
c
a
c
h
e
-
a
l
i
g
n
e
d
s
t
r
u
c
t
u
r
e
s
DMA
D
i
r
e
c
t
M
e
m
o
r
y
A
c
c
e
s
s
:
d
e
v
i
c
e
s
r
e
a
d
/
w
r
i
t
e
m
e
m
o
r
y
i
n
d
e
p
e
n
d
e
n
t
l
y
D
M
A
b
u
s
t
r
a
n
s
a
c
t
i
o
n
s
c
o
m
p
e
t
e
w
i
t
h
C
P
U
f
o
r
m
e
m
o
r
y
b
a
n
d
w
i
d
t
h
M
i
t
i
g
a
t
i
o
n
:
m
i
n
i
m
i
z
e
D
M
A
d
u
r
i
n
g
c
r
i
t
i
c
a
l
s
e
c
t
i
o
n
s
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: These are 'secondary' sources of jitter -- may not matter on lightly loaded systems but become significant under load.
CPU frequency scaling is often the easiest win. 'performance' governor locks CPU at max frequency -- more power, more predictable timing.
Huge pages (2 MB / 1 GB on ARM64) dramatically reduce TLB misses for data-intensive applications.

## Slide 13
Real-Time Tuning Checklist
Kernel Configuration
C
O
N
F
I
G
_
P
R
E
E
M
P
T
_
R
T
=
y
(
m
a
i
n
l
i
n
e
6
.
1
2
+
:
'
F
u
l
l
y
P
r
e
e
m
p
t
i
b
l
e
K
e
r
n
e
l
'
)
C
O
N
F
I
G
_
H
I
G
H
_
R
E
S
_
T
I
M
E
R
S
=
y
C
O
N
F
I
G
_
N
O
_
H
Z
_
F
U
L
L
=
y
(
t
i
c
k
l
e
s
s
o
n
i
s
o
l
a
t
e
d
C
P
U
s
)
C
O
N
F
I
G
_
H
Z
_
1
0
0
0
=
y
o
r
h
i
g
h
e
r
Boot Parameters
i
s
o
l
c
p
u
s
=
<
c
p
u
-
l
i
s
t
>
(
d
e
d
i
c
a
t
e
C
P
U
s
t
o
R
T
)
n
o
h
z
_
f
u
l
l
=
<
c
p
u
-
l
i
s
t
>
(
d
i
s
a
b
l
e
t
i
c
k
o
n
i
s
o
l
a
t
e
d
C
P
U
s
)
r
c
u
_
n
o
c
b
s
=
<
c
p
u
-
l
i
s
t
>
(
o
f
f
l
o
a
d
R
C
U
f
r
o
m
i
s
o
l
a
t
e
d
C
P
U
s
)
Runtime Configuration
C
P
U
g
o
v
e
r
n
o
r
:
p
e
r
f
o
r
m
a
n
c
e
(
d
i
s
a
b
l
e
D
V
F
S
)
M
e
m
o
r
y
:
m
l
o
c
k
a
l
l
(
)
i
n
R
T
c
o
d
e
,
s
w
a
p
o
f
f
-
a
I
n
t
e
r
r
u
p
t
s
:
m
o
v
e
t
o
n
o
n
-
R
T
C
P
U
s
v
i
a
s
m
p
_
a
f
f
i
n
i
t
y
S
c
h
e
d
u
l
e
r
:
S
C
H
E
D
_
F
I
F
O
,
a
p
p
r
o
p
r
i
a
t
e
p
r
i
o
r
i
t
y
Application Design
P
r
e
-
f
a
u
l
t
s
t
a
c
k
a
n
d
h
e
a
p
a
t
s
t
a
r
t
u
p
A
v
o
i
d
s
y
s
t
e
m
c
a
l
l
s
i
n
t
h
e
h
o
t
p
a
t
h
U
s
e
l
o
c
k
-
f
r
e
e
d
a
t
a
s
t
r
u
c
t
u
r
e
s
w
h
e
r
e
p
o
s
s
i
b
l
e
S
e
t
C
P
U
a
f
f
i
n
i
t
y
:
t
a
s
k
s
e
t
o
r
p
t
h
r
e
a
d
_
s
e
t
a
f
f
i
n
i
t
y
_
n
p
H
a
n
d
l
e
A
L
L
e
r
r
o
r
c
o
d
e
s
(
m
a
l
l
o
c
c
a
n
f
a
i
l
)
W
a
t
c
h
d
o
g
:
d
e
t
e
c
t
i
f
R
T
t
a
s
k
s
t
o
p
s
r
u
n
n
i
n
g
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: This is the practical checklist for making an embedded Linux system real-time. Each item addresses a specific source of non-determinism.
The watchdog entry is critical and often forgotten. A hung RT task is worse than one that misses a deadline.
In the lab, students will apply a subset of these tuning steps and measure the latency improvement at each stage.

## Slide 14
Measuring Latency with cyclictest
# cyclictest -- the standard RT latency measurement tool # Part of rt-tests: https://git.kernel.org/pub/scm/utils/rt-tests # Basic: measure sleep latency for 30 seconds $ cyclictest -t1 -p 80 -n -i 1000 -l 30000 # -t1: one thread # -p 80: SCHED_FIFO priority 80 # -n: use clock_nanosleep (high-resolution) # -i 1000: interval 1000 us (1 ms period) # -l 30000: 30000 loops (30 seconds) # Sample output: # T: 0 (12345) P:80 I:1000 C:30000 Min:8 Act:12 Avg:15 Max:89 # Min: best case Act: most recent # Avg: average Max: WORST CASE <- THIS MATTERS # Longer test (1 hour, 4 threads, all CPUs): $ cyclictest -t4 -p 90 -n -i 500 -l 7200000 -a # -a: pin each thread to different CPU # Verbose with histogram: $ cyclictest -t1 -p 80 -n -i 1000 -l 100 -v # Available in: # Buildroot: BR2_PACKAGE_RT_TESTS # Yocto: meta-oe recipe rt-tests
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: cyclictest is the standard tool for measuring RT latency. The concept is simple: create a high-precision timer, wake up, check how late you are, sleep again. The difference between expected and actual wakeup IS the scheduling latency.
The Max value is what matters for real-time. A system with Max=89us can meet a 100us deadline. A system with Max=150us cannot, even if average is 15us.
Run cyclictest for hours, not seconds. Worst-case latencies often appear only under specific conditions (heavy I/O, thermal throttling, rare kernel paths).

## Slide 15
Interpreting cyclictest Results
What Do the Numbers Mean?
Min: best-case latency (usually 1-10 us) System was idle, nothing to preempt
Avg: typical latency (usually 5-50 us) Normal load, cache warm
Max: worst-case latency (the critical number) Determined by longest non-preemptible section With PREEMPT_RT: typically 20-200 us Without PREEMPT_RT: can be 10+ ms
Spread (Max - Min) = jitter Low jitter = predictable system
Diagnosing Problems
Low Min, large Max: Background activity causes occasional delays Check: heavy I/O, network traffic, cron jobs
High Min (above 50 us): Systemic issue even at idle Check: CPU frequency scaling, BIOS, SMI
Periodic spikes: Something runs at regular intervals Check: kernel timers, RCU callbacks, workqueues Use ftrace to identify the culprit
Compare: PREEMPT_RT vs standard kernel Same workload, same hardware PREEMPT_RT should show 10-100x lower Max
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: Interpreting results is as important as collecting them. The Max value tells you whether you can meet your deadline. The spread tells you how predictable the system is.
For the lab, students will run cyclictest under different conditions: idle, with background I/O (stress-ng), and with CPU isolation. They will see how each tuning step reduces the Max latency.
A common mistake: running cyclictest for 30 seconds and declaring victory. Worst-case latencies may only appear after minutes or hours of operation.

## Slide 16
Using ftrace to Find Latency Sources
# When cyclictest shows high latency, ftrace tells you WHY # ─── Enable latency tracing ─── $ echo latency-format > /sys/kernel/debug/tracing/trace_options $ echo 1 > /sys/kernel/debug/tracing/tracing_on # ... run your workload ... $ cat /sys/kernel/debug/tracing/trace # Sample output showing a latency spike: # latency: 87 us # caller: __switch_to # preempt_count: 0x0 # need_resched: 0x1 # blocked_by: [irq/45-e1000] <-- interrupt handler blocked us! # ─── Trace specific latency events ─── $ echo 1 > /sys/kernel/debug/tracing/events/sched/sched_wakeup/enable $ echo 1 > /sys/kernel/debug/tracing/events/irq/irq_handler_entry/enable $ echo 1 > /sys/kernel/debug/tracing/events/irq/irq_handler_exit/enable $ cat /sys/kernel/debug/tracing/trace_pipe # Live stream # ─── Function graph tracer for detailed timing ─── $ echo function_graph > /sys/kernel/debug/tracing/current_tracer $ echo __schedule > /sys/kernel/debug/tracing/set_ftrace_filter $ cat /sys/kernel/debug/tracing/trace # ─── hist triggers (kernel 4.15+) ─── # Create a histogram of wakeup latencies $ echo 'hist:keys=lat.buckets=1000:vals=hitcount' > \ /sys/kernel/debug/tracing/events/sched/sched_wakeup_lat/trigger # ... run workload ... $ cat /sys/kernel/debug/tracing/events/sched/sched_wakeup_lat/hist
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: cyclictest tells you THAT you have latency. ftrace tells you WHY. This is the debugging workflow: measure first (cyclictest), then instrument (ftrace).
The latency-format option adds timing information to each trace entry. You can see exactly which function or interrupt handler caused the delay.
hist triggers (available since kernel 4.15) let you create histograms of latency events, which is perfect for understanding the distribution of delays over a long test run.

## Slide 17
Lab: Measure and Tune Real-Time Latency
1
1. Baseline measurement
Install rt-tests on target (Buildroot: BR2_PACKAGE_RT_TESTS) Run: cyclictest -t1 -p 80 -n -i 1000 -l 60000 Record: Min, Avg, Max latency
2
2. Add background load
In another terminal: stress-ng --cpu 4 --io 2 --timeout 60s Re-run cyclictest under load Compare: how much did Max latency increase?
3
3. Apply tuning
Set CPU governor to performance Isolate a CPU: isolcpus=3 (add to kernel cmdline, reboot) Pin cyclictest to isolated CPU: taskset -c 3 cyclictest ... Re-run under load
4
4. Measure improvement
Compare all three runs: baseline, loaded, tuned What was the Max latency in each case? What was the jitter (Max - Min)?
5
5. Analyze with ftrace (optional)
Enable sched_wakeup_lat tracing Identify the top 3 sources of latency on your system Document: what was the longest latency event and its cause?
Lab: Measure and Tune Real-Time Latency
Notes: This lab is the capstone of the real-time section. Students measure latency, add load, apply tuning, and measure again. The before/after comparison makes the value of each tuning step concrete.
Key teaching moment: show that CPU isolation has the biggest single impact. The isolated CPU has no competition -- cyclictest runs with minimal interference.
The ftrace step is optional for students who finish early. It shows them how to diagnose latency sources in production systems.

## Slide 18
PREEMPT_RT: What Changes in the Kernel
Spinlocks -> rt-mutexes
All kernel spinlocks become sleeping mutexes Supports priority inheritance No busy-waiting, bounded lock times
Threaded interrupts
Interrupt handlers run as SCHED_FIFO threads Configurable priority (default: 50) RT tasks at higher priority preempt IRQ threads
Preemptible kernel
Kernel code can be preempted almost anywhere Only minimal critical sections remain non-preemptible Dramatically reduces worst-case latency
High-resolution timers
Nanosecond-precision timers via hardware Tickless mode: no periodic tick when idle Precise sleep and wakeup for RT tasks
Priority inheritance
All mutexes support PI automatically Prevents priority inversion across the kernel Critical for multi-threaded RT applications
Result
Worst-case latency: 20-200 us (vs 10+ ms) Soft real-time capable for many applications Mainline since Linux 6.12 (2024)
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: This flow diagram summarizes the five key changes PREEMPT_RT makes to the kernel. Each change addresses a specific source of non-determinism.
The result: worst-case latency drops from 10+ milliseconds to 20-200 microseconds on typical ARM hardware. That is a 50-500x improvement.
And now that PREEMPT_RT is mainline, these benefits are available without any out-of-tree patches. Just select the right kernel configuration.

## Slide 19
When to Use (and Not Use) Real-Time Linux
Good Fit for RT Linux
Soft real-time requirements (deadlines > 100 us)
Audio/video processing, robotics, industrial control
Applications that need both RT and rich OS features
Network processing, IoT gateways, edge computing
Systems where occasional deadline misses are tolerable
Prototyping before committing to dedicated RTOS
When you need: networking, filesystems, drivers AND RT
Not a Good Fit
Hard real-time requirements (deadlines < 10 us)
Safety-critical systems (automotive, aerospace, medical)
Systems requiring formal WCET certification
Simple control loops (use bare-metal or small RTOS instead)
When a dedicated RTOS is already proven and certified
Systems where any single deadline miss is catastrophic
Consider: FreeRTOS, Zephyr, VxWorks, QNX for these cases
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: This is a pragmatic slide. Real-time Linux is not the answer for everything. For hard real-time and safety-critical systems, a certified RTOS is the right choice.
But for the growing class of embedded systems that need both real-time behavior AND rich OS features (networking, storage, web interfaces), RT Linux is increasingly the best option.
The trend in the industry is toward Linux for more applications, with RT capabilities closing the gap with traditional RTOSes.

## Slide 20
Session Summary
Real-time is about guarantees, not speed: deadline, jitter, determinism
PREEMPT_RT (mainline since 6.12): spinlocks->rt-mutexes, threaded IRQs, fully preemptible kernel
Scheduling policies: SCHED_FIFO, SCHED_RR, SCHED_DEADLINE for RT tasks
Sources of non-determinism: page faults, TLB misses, DVFS, cache contention, DMA
Tuning: mlockall(), CPU isolation, interrupt shielding, performance governor
Measurement: cyclictest for latency, ftrace for root cause analysis
Soft real-time capable: 20-200 us worst-case latency on ARM with proper tuning
Embedded Linux Design • Session 10 • Real-Time Systems
Notes: This is the final session summary for the course. The key takeaway: Linux CAN be real-time, but it requires understanding and deliberate configuration.
The PREEMPT_RT merge into mainline 6.12 is a game-changer. What required out-of-tree patches for 20 years is now a standard kernel option.
For the course project, students should apply the tuning checklist and measure the results. The combination of PREEMPT_RT + CPU isolation + mlockall() + performance governor gives the best results on embedded hardware.

## Slide 21
Course Wrap-Up: What We Built
Session 1-2: Foundation
E
m
b
e
d
d
e
d
L
i
n
u
x
c
o
n
c
e
p
t
s
,
t
o
o
l
c
h
a
i
n
s
,
b
o
o
t
l
o
a
d
e
r
s
,
c
r
o
s
s
-
d
e
v
e
l
o
p
m
e
n
t
s
e
t
u
p
Session 3-4: Building
B
u
i
l
d
r
o
o
t
a
n
d
Y
o
c
t
o
,
s
y
s
t
e
m
a
r
c
h
i
t
e
c
t
u
r
e
,
f
l
a
s
h
f
i
l
e
s
y
s
t
e
m
s
Session 5-6: Kernel
K
e
r
n
e
l
b
u
i
l
d
,
/
p
r
o
c
,
s
y
s
f
s
,
d
e
v
i
c
e
t
r
e
e
,
i
n
t
e
r
r
u
p
t
h
a
n
d
l
i
n
g
Session 7-8: Applications
P
r
o
c
e
s
s
e
s
,
t
h
r
e
a
d
s
,
I
P
C
,
e
m
b
e
d
d
e
d
P
y
t
h
o
n
,
D
o
c
k
e
r
d
e
p
l
o
y
m
e
n
t
Session 9-10: Observing & Tuning
G
D
B
,
p
r
o
f
i
l
i
n
g
,
t
r
a
c
i
n
g
,
m
e
m
o
r
y
m
a
n
a
g
e
m
e
n
t
,
r
e
a
l
-
t
i
m
e
s
y
s
t
e
m
s
The Big Picture
Y
o
u
n
o
w
h
a
v
e
t
h
e
s
k
i
l
l
s
t
o
b
u
i
l
d
a
c
u
s
t
o
m
e
m
b
e
d
d
e
d
L
i
n
u
x
s
y
s
t
e
m
f
r
o
m
s
c
r
a
t
c
h
:
t
o
o
l
c
h
a
i
n
→
b
o
o
t
l
o
a
d
e
r
→
k
e
r
n
e
l
→
r
o
o
t
f
s
→
a
p
p
l
i
c
a
t
i
o
n
→
d
e
b
u
g
→
p
r
o
f
i
l
e
→
o
p
t
i
m
i
z
e
f
o
r
r
e
a
l
-
t
i
m
e
.
Embedded Linux Design u'•' UCSC Extension u'•' Course Complete
Notes: This is the closing slide. We have covered the full embedded Linux development lifecycle: from cross-compilation and boot through kernel configuration, application development, debugging, profiling, and real-time optimization.
The course project ties it all together: students build a bootable RPi4 system from scratch, cross-compile applications, debug with GDB, profile with perf, and optionally tune for real-time.
Thank you for a great quarter. The skills from this course are directly applicable to embedded Linux roles in industry.

## Slide 22
Quiz & Assignment
Quiz (Canvas)
1
0
q
u
e
s
t
i
o
n
s
,
4
5
m
i
n
u
t
e
s
,
6
a
t
t
e
m
p
t
s
,
h
i
g
h
e
s
t
s
c
o
r
e
r
e
t
a
i
n
e
d
C
o
v
e
r
s
:
p
r
e
e
m
p
t
i
o
n
m
o
d
e
l
s
,
s
c
h
e
d
u
l
i
n
g
p
o
l
i
c
i
e
s
,
l
a
t
e
n
c
y
s
o
u
r
c
e
s
,
c
y
c
l
i
c
t
e
s
t
i
n
t
e
r
p
r
e
t
a
t
i
o
n
,
t
u
n
i
n
g
t
e
c
h
n
i
q
u
e
s
Final Assignment
1
.
B
u
i
l
d
a
P
R
E
E
M
P
T
_
R
T
k
e
r
n
e
l
f
o
r
y
o
u
r
t
a
r
g
e
t
(
Y
o
c
t
o
o
r
B
u
i
l
d
r
o
o
t
)
2
.
R
u
n
c
y
c
l
i
c
t
e
s
t
:
b
a
s
e
l
i
n
e
,
u
n
d
e
r
l
o
a
d
,
a
n
d
w
i
t
h
t
u
n
i
n
g
a
p
p
l
i
e
d
3
.
D
o
c
u
m
e
n
t
:
k
e
r
n
e
l
c
o
n
f
i
g
,
c
y
c
l
i
c
t
e
s
t
r
e
s
u
l
t
s
,
t
u
n
i
n
g
s
t
e
p
s
4
.
B
o
n
u
s
:
u
s
e
f
t
r
a
c
e
t
o
i
d
e
n
t
i
f
y
t
h
e
t
o
p
l
a
t
e
n
c
y
s
o
u
r
c
e
S
u
b
m
i
t
:
k
e
r
n
e
l
.
c
o
n
f
i
g
+
c
y
c
l
i
c
t
e
s
t
o
u
t
p
u
t
+
a
n
a
l
y
s
i
s
d
o
c
u
m
e
n
t
Embedded Linux Design u'•' UCSC Extension
Notes: The final assignment ties together the entire course. Students build a PREEMPT_RT kernel, measure latency, apply tuning, and document the results.
The bonus ftrace step is for students who want to go deeper. Identifying latency sources with ftrace is a production debugging skill.
This is the last assignment of the course. Good luck!