## Slide 1
Assignment 3: Build a Bootable Linux SD Card with Yocto Project
From source to SD card — build a complete Linux system for Raspberry Pi 4 using the Yocto Project.

## Slide 2
WHAT YOU'LL BUILD
Assignment Overview
Build a bootable Linux image for Raspberry Pi 4 — kernel, bootloader, userspace, and SD card image.
What You'll Build
Complete Linux root filesystem
Kernel, bootloader, and userspace via Yocto
Bootable SD card image (.wic.bz2)
Key Concepts Practiced
BSP layers and machine configuration
BitBake layer management
Image recipes and package groups
License flags for proprietary firmware

## Slide 3
STEP 1
Clone the Yocto Poky Distribution
Clone Poky and required layers. All layers must use the same release branch — mixing branches causes build failures.
Clone Poky (LTS: scarthgap)
cd ~/el
git clone -b scarthgap git://git.yoctoproject.org/poky.git
Clone Required Layers
cd ~/el/poky
git clone -b scarthgap \
git://git.openembedded.org/meta-openembedded
git clone -b scarthgap \
git://git.yoctoproject.org/meta-raspberrypi
Image recipes: rpi-test-image (X11, networking) · core-image-minimal (smaller) · rpi-basic-image (console only)

## Slide 4
STEP 2
Initialize the BitBake Build Environment
Source the environment script to set up BitBake, then register all required layers.
Initialize & Add Layers
cd ~/el/poky
source oe-init-build-env build-rpi
bitbake-layers add-layer \
../meta-openembedded/meta-oe (essential utilities)
bitbake-layers add-layer \
../meta-openembedded/meta-python (Python packages)
bitbake-layers add-layer \
../meta-openembedded/meta-networking (network tools)
bitbake-layers add-layer \
../meta-openembedded/meta-multimedia (optional )
bitbake-layers add-layer \
../meta-raspberrypi
Verify Layer Configuration
bitbake-layers show-layers
Confirms all layers are registered with matching priorities. Check this before starting any build.
build-rpi is your isolated build directory — safe to delete and recreate without affecting source layers.

## Slide 5
STEP 3
Configure the Build for Raspberry Pi 4
Edit build-rpi/conf/local.conf to set the target machine and enable headless boot features.
Target Machine
MACHINE = "raspberrypi4-64"
Selects the 64-bit BSP for Raspberry Pi 4.
Enable SSH
IMAGE_FEATURES +=
"ssh-server-openssh"
Critical for headless access after first boot.
License Flag
LICENSE_FLAGS_ACCEPTED =
"synaptics-killswitch"
Accepts the proprietary firmware license required by Raspberry Pi.
For other targets, use:
- Raspberry Pi 3: MACHINE = "raspberrypi3"
- Raspberry Pi 3 64-bit: MACHINE = "raspberrypi3-64"
To avoid re-downloading sources on rebuilds, add to conf/local.conf:
DL_DIR = "${HOME}/el/poky/downloads"
SSTATE_DIR = "${HOME}/el/poky/sstate-cache"

## Slide 6
STEP 4
Build the Image with BitBake
BitBake parses recipes, fetches sources, and compiles everything. Expect 30–90 minutes on a modern workstation.
Parse Recipes
Read metadata and resolve deps
Generate Image
Assemble rootfs and produce .wic.bz2
Compile & Package
Fetch sources, patch, build packages
BitBake moves through three phases automatically — parsing recipes, compiling all components, then assembling the final SD card image.
Run the Build
cd ~/el/poky/build-rpi
time bitbake rpi-test-image
Monitor Progress
tail -f tmp/log/bitbake-cookerdaemon.log
Locate Output
ls -l tmp/deploy/images/raspberrypi4-64/
After successful build, find your SD card image:
ls -l tmp/deploy/images/${MACHINE}/
Look for: rpi-test-image-raspberrypi4-64.rootfs.wic.bz2
Create directories:
mkdir -p ~/el/poky/downloads ~/el/poky/sstate-cache
Alternative images to consider:
- core-image-minimal (smaller, faster build)
- rpi-test-image (includes testing utilities)
- rpi-basic-image (basic Raspberry Pi image)

## Slide 7
STEP 5
Flash the Image to an SD Card
Decompress the .wic.bz2 image and write it to your SD card. bmaptool is faster and verifies integrity.
Decompress
cd ~/el/poky/build-rpi/\
tmp/deploy/images/raspberrypi4-64/
bunzip2 rpi-test-image-*.wic.bz2
Flash with dd
sudo dd if=rpi-test-image-*.wic \
of=/dev/sdX bs=4M \
status=progress
sync
Or use bmaptool
sudo bmaptool copy \
rpi-test-image-*.wic.bz2 \
/dev/sdX
Replace /dev/sdX with your actual SD card device. Double-check with lsblk — writing to the wrong device will overwrite data.

## Slide 8
STEP 6 · VERIFICATION
First Boot & Assignment Submission
Boot & Verify
Insert SD card, connect TTL serial (GPIO 14/15, pin 6 GND)
Power on, observe boot messages
Login as root (no password with debug-tweaks)
Run: uname -a — expect Linux raspberrypi4-64 … aarch64 GNU/Linux
Submit to Canvas (or in class)
uname -a output from booted system
Screenshot of TTL serial console during boot
Build log excerpt showing successful completion
Brief reflection (2–3 sentences): issues, build time, what you'd do differently