## Slide 1
Session 4: System Architecture
Storage, Memory, Boot, and Software Updates
UCSC Extension • Embedded Linux Design
Embedded Linux Design • Session 4 • System Architecture

## Slide 2
Today's Roadmap
Storage & Flash
Memory & Boot Chain
Software Updates
Prototyping with Raspberry Pi
System Design Case Study

## Slide 3
Storage Landscape
NAND Flash
Raw flash (managed by FTL) Used in: eMMC, SSD, USB drives Wear leveling required
NOR Flash
Execute-in-place (XIP) Used in: boot ROM, firmware Fast read, slow write
eMMC
Managed NAND + controller Used in: smartphones, embedded Standardized interface
SD Card
Removable managed NAND Used in: prototyping, cameras SPI or SDIO interface

## Slide 4
Flash Partitioning
Partition 1
1 MB
Partition 2
256 KB
Partition 3
8 MB
Partition 4
remaining
MBR vs GPT: MBR supports 4 primary partitions. GPT supports 128+ and includes redundancy.
# View partition table: $ fdisk -l /dev/mmcblk0 $ parted /dev/mmcblk0 print # Create partition (GPT): $ parted /dev/mmcblk0 mklabel gpt $ parted /dev/mmcblk0 mkpart primary ext4 1MiB 512MiB # Format: $ mkfs.ext4 -L rootfs /dev/mmcblk0p1

## Slide 5
Flash Filesystems
JFFS2
Journaling Flash FS v2 Raw NAND, wear leveling Small pages, slow mount
YAFFS2
Yet Another Flash FS Raw NAND, log-structured Fast mount, Linux-only
UBIFS
Unsorted Block Image FS On top of UBI layer Best for large NAND
ext4
Fourth Extended FS For managed flash (eMC, SD) Most common, journaling

## Slide 6
Wear Leveling & UBI
Why Wear Leveling?
NAND flash blocks wear out after ~10,000-100,000 erase cycles. Without wear leveling: Block 0: ████████████████ (worn out) Block 1: █ (barely used) Block 2: █ (barely used) With wear leveling: Block 0: ██████ (even) Block 1: ██████ (even) Block 2: ██████ (even) FTL (Flash Translation Layer) or UBI handles this automatically.
UBI Volume Management
UBI (Unsorted Block Image) sits between MTD and filesystem: ┌─────────────────────┐ │ UBIFS / ext4 │ ← Filesystem ├─────────────────────┤ │ UBI Volume │ ← Logical volumes ├─────────────────────┤ │ UBI Layer │ ← Wear leveling, bad block ├─────────────────────┤ │ MTD │ ← Memory Technology Device ├─────────────────────┤ │ Raw NAND │ ← Physical flash └─────────────────────┘ $ ubiattach /dev/ubi_ctrl -m 0 $ mount -t ubifs ubi0:rootfs /mnt

## Slide 7
Memory Layout
0x0000_0000
Boot ROM
64 KB
0x0001_0000
SRAM
128 KB
0x0003_0000
Peripherals
1 MB
0x8000_0000
DRAM
512 MB
0xA000_0000
Flash (XIP)
16 MB
ARM typical memory map. Addresses vary by SoC. Check your reference manual.

## Slide 8
Boot Chain: ROM → Linux
ROM Boot
SoC internal code Init DRAM, load SPL from flash/SD/USB
SPL
Secondary Program Loader Minimal U-Boot Init DRAM, load U-Boot
U-Boot
Full bootloader Load kernel + DTB Set bootargs, boot
Kernel
Linux kernel Init hardware Mount rootfs, start init
Init
init / systemd Start services System ready
U-Boot SPL 2023.04 (Oct 15 2023) DRAM: 512 MiB MMC: OMAP SD/MMC: 0 Loading Environment... OK Loading kernel from mmc 0:1... U-Boot 2023.04 (Oct 15 2023) Model: TI AM335x BeagleBone Black DRAM: 512 MiB NAND: 0 MiB MMC: OMAP SD/MMC: 0, OMAP SD/MMC: 1 Loading kernel... ## Flattened Device Tree blob at 88000000 Booting using the fdt blob at 0x88000000 Loading Kernel Image Starting kernel... [ 0.000000] Booting Linux on physical CPU 0x0 [ 0.000000] Linux version 6.1.50 [ 2.345678] VFS: Mounted root (ext4 filesystem).

## Slide 9
DRAM Initialization
Why DRAM Init Matters
DRAM must be configured before use: 1. Set up DRAM controller 2. Configure timing parameters 3. Run memory training 4. Test memory SRAM is used first (small, no init). SPL runs from SRAM, init DRAM, then loads U-Boot into DRAM. Timing parameters are board-specific: - CAS latency - Refresh rate - Bus width - Number of chip selects
SPL: The DRAM Enabler
SPL = Secondary Program Loader Stored in SRAM (no DRAM needed) Typical size: < 64 KB SPL responsibilities: 1. Initialize DRAM controller 2. Load U-Boot from storage 3. Jump to U-Boot in DRAM U-Boot SPL config: CONFIG_SPL=y CONFIG_SPL_DRAM_SUPPORT=y CONFIG_SPL_MMC_SUPPORT=y Board-specific dram_init(): board_init_f() → dram_init() → DDR PHY training → Memory test (optional)

## Slide 10
Software Update Strategies
A/B Partitioning
Two identical rootfs partitions Active + standby Atomic switch on update Rollback by switching back
Blue-Green
Two full system images Load balancer switches traffic Zero-downtime updates Common in cloud/edge
Canary
Gradual rollout Small % of devices first Monitor for errors Full rollout after validation
A/B Partition Diagram
Slot A (Active)
Kernel + Rootfs
Slot B (Standby)
Kernel + Rootfs (new version)
Bootloader selects active slot → Kernel boots

## Slide 11
Update Frameworks
SWUpdate
Open source, Lua scripts Multiple update formats A/B support, web UI Lightweight, flexible
Mender
Open source + commercial A/B updates, robust rollback Cloud management (Mender Server) Yocto and Buildroot support
RAUC
Robust Auto-Update Controller A/B with redundancy Bundle format with signatures Designed for Linux embedded

## Slide 12
OTA Update Flow
1
1. Check
Device polls server Checks for new version Downloads update bundle
2
2. Verify
Verify signature Check compatibility Validate bundle integrity
3
3. Write
Write to inactive slot Stream data to flash Progress indicator
4
4. Activate
Mark new slot as active Set bootloader flag Reboot
5
5. Boot & Verify
Boot new image Health check Rollback if failed

## Slide 13
Prototyping with Raspberry Pi
Raspberry Pi is the ideal prototyping platform for embedded Linux: Low cost, huge community, mainline kernel support, GPIO, and standard interfaces.
▸ Models: RPi 3B+, 4B, 5, Zero 2W
▸ SoC: Broadcom BCM2711/BCM2712
▸ RAM: 1-8 GB LPDDR4
▸ Boot: SD card, USB, network
▸ GPIO: 40-pin header, I2C, SPI, UART
▸ OS: Raspberry Pi OS, Ubuntu, Buildroot, Yocto

## Slide 14
Lab: Prototyping
Lab: RPi Setup
Hardware Setup
1. RPi 4B (2GB+ recommended)
2. MicroSD card (16GB+)
3. USB-C power supply (5V 3A)
4. USB-to-TTL serial cable (3.3V!)
5. Ethernet cable or WiFi
Serial Console Connection
# Find serial port: $ ls /dev/ttyUSB* # Connect (115200 8N1): $ screen /dev/ttyUSB0 115200 or $ minicom -D /dev/ttyUSB0 -b 115200 # Wiring (USB-to-TTL): RPi GPIO 14 (TX) → USB TTL RX RPi GPIO 15 (RX) → USB TTL TX RPi GND → USB TTL GND # WARNING: Do NOT connect VCC! # RPi is self-powered via USB-C

## Slide 15
Lab: Prototyping
Lab: RPi Boot & Debug
U-Boot 2023.04 (Oct 15 2023 - 12:34:56 +0000) Model: Raspberry Pi 4 Model B Rev 1.4 DRAM: 4 GiB MMC: mmcnr@7e300000: 1, mmc@7e340000: 0 Loading kernel from mmc 0:1... ## Flattened Device Tree blob at 02600000 Booting using the fdt blob at 0x02600000 Loading Kernel Image Starting kernel... [ 0.000000] Booting Linux on physical CPU 0x0 [ 0.000000] Linux version 6.1.50-v8
Essential Debug Commands:
# Kernel messages: $ dmesg | tail -50 # Device tree: $ ls /proc/device-tree/ # GPIO status: $ cat /sys/kernel/debug/gpio # Memory: $ free -h $ cat /proc/meminfo
# Storage: $ df -h $ lsblk $ fdisk -l # Network: $ ip addr $ ip route $ ping 8.8.8.8 # Processes: $ ps aux $ top # U-Boot env (from Linux): $ fw_printenv

## Slide 16
Lab: Prototyping
Lab: Cross-Compile & Deploy
1
1. Build on Host
Cross-compile with Buildroot/Yocto: $ make -j$(nproc) Output: zImage, rootfs.ext4, DTB
2
2. Flash SD Card
Write image to SD card: $ dd if=output/images/sdcard.img of=/dev/sdX bs=4M status=progress $ sync
3
3. Boot RPi
Insert SD card, power on Connect serial console Watch U-Boot → Kernel boot
4
4. Deploy App
Copy binary to target: $ scp myapp root@192.168.1.100:/usr/bin/ $ ssh root@192.168.1.100 ./myapp

## Slide 17
Case Study: IoT Gateway
Design an IoT gateway that collects sensor data from multiple sources, processes it locally, and uploads to the cloud.
Sensors
Temperature, humidity, motion I2C, SPI, UART interfaces
Processor
ARM Cortex-A53 512MB-1GB RAM eMMC + SD card
Connectivity
Ethernet, WiFi, BLE 4G/LTE optional MQTT to cloud
Software
Buildroot or Yocto Python + C applications OTA updates via Mender

## Slide 18
IoT Gateway: Storage Design
eMMC Partition Layout (8 GB)
boot
2 MB
env
256 KB
kernel
16 MB
rootfs_a
2 GB
rootfs_b
2 GB
data
remaining
Filesystem Choices:
rootfs_a / rootfs_b
ext4 with journaling Read-only rootfs option squashfs for read-only
data
ext4 with journaling Persistent across updates Separate mount point

## Slide 19
IoT Gateway: Boot Design
Power On
SoC reset vector Boot ROM executes
SPL
Init DRAM, MMC Load U-Boot from boot partition
U-Boot
Read bootcount Select active slot (A/B) Load kernel + DTB
Kernel
Init drivers Mount rootfs Start systemd
Systemd
Start services Network, MQTT, app Health check
U-Boot Environment (bootcmd)
# A/B slot selection: bootcount=0 bootlimit=3 active_slot=a # Load kernel from active slot: loadkernel=fatload mmc 0:${kernel_part} \ ${kernel_addr_r} zImage # Boot command: bootcmd=if test ${active_slot} = a; then \ setenv kernel_part 3; \ else \ setenv kernel_part 4; \ fi; run loadkernel; \ bootz ${kernel_addr_r} - ${fdt_addr_r} # Rollback on failure: altbootcmd=if test ${active_slot} = a; then \ setenv active_slot b; \ else \ setenv active_slot a; \ fi; saveenv; reset

## Slide 20
IoT Gateway: Update Design
OTA Update Flow
1. Mender server pushes update 2. Device downloads bundle 3. Write to inactive slot (B) 4. Reboot into slot B 5. Health check runs 6. If OK: mark B as active 7. If FAIL: rollback to slot A Key: data partition is NEVER touched during updates.
Mender Artifact
# mender-artifact format: update-image.mender ├── header.tar.gz │ ├── header-info │ └── headers/0000/ │ └── type-info ├── rootfs.ext4 └── version # Create artifact: $ mender-artifact write \ module-image \ -t raspberrypi4 \ -n gateway-v2.1 \ -f rootfs.ext4 \ -o update.mender

## Slide 21
Common Pitfalls
⚠ Wrong flash filesystem for raw NAND
Using ext4 on raw NAND without FTL → Use UBIFS or JFFS2 instead
⚠ No wear leveling
Writing frequently to same blocks → Flash wears out prematurely
⚠ Missing DRAM init
SPL doesn't configure DRAM correctly → U-Boot crashes immediately
⚠ No update rollback
OTA update bricks device → Always implement A/B with rollback
⚠ Data partition erased on update
User data lost after OTA → Keep data partition separate

## Slide 22
Session Summary
Choose flash type based on use case: eMMC for managed, raw NAND for custom
Use appropriate filesystem: UBIFS for raw NAND, ext4 for managed flash
A/B partitioning enables safe OTA updates with rollback
Raspberry Pi is ideal for prototyping embedded Linux systems
Separate data partition survives OTA updates

## Slide 23
References & Resources
Flash & Storage
▸ MTD subsystem: linux-mtd.infradead.org
▸ UBIFS documentation: linux-mtd.infradead.org/doc/ubifs.html
▸ eMMC spec: jedec.org/standards-documents
Software Updates
▸ Mender.io documentation: docs.mender.io
▸ SWUpdate: sbabic.github.io/swupdate
▸ RAUC: rauc.readthedocs.io
Prototyping
▸ Raspberry Pi documentation: rpi.com/documentation
▸ Bootlin training: bootlin.com/training
▸ elinux.org (Embedded Linux Wiki)
System Design
▸ Embedded Linux Conference (ELC) talks
▸ Yocto Project docs: docs.yoctoproject.org
▸ Buildroot manual: buildroot.org/downloads/manual