## Slide 1
Introduction
Outcomes: O1
Notes: In embedded systems, the operating system has to meet strict timing constraints, which is achieved by the use
of appropriate scheduling algorithms.
• However, a major problem arises, when the real-time tasks share resources.
Priority inversion could occur, which leads to possible loss/damage.
• Therefore, a basic understanding of real-time task scheduling algorithms and resource sharing protocols is
needed. In turn,
• POSIX-RT is the standardization of real-time operating systems.
Main Questions in this Chapter
What is an RTOS? Why RTOS?
Where is it getting used?
How is it different from a traditional OS?
Introduction to Realtime Linux https://www.youtube.com/watch?v=BKkX9WASfpI
_x000C__x000C_CHAPTER OVERVIEW
In This Chapter, We Will Discuss
1. Introduction
2. Embedded System
3. Real Time Systems
4. Cyber Physical Systems
5. Microcomputers
6. Cross-compilers
7. No Assignment
8. No Quiz
_x000C_Real-Time Systems “RT”
Real-time systems provide
• guaranteed worst-case response times to critical events, and
• acceptable average-case response times to noncritical events.
Embedded Systems “ES”
Embedded systems are computing systems that reside in a larger system.
Real-Time Embedded Systems (“RTES”)
Represents a class of Embedded Systems with constraints of Real-Time.
ES/RTES and Cyber Physical Systems “CPS”. See this URL.
ES/RTES and CPS are often interchangeably used. e.g. Adaptive Cruise Control Systems, Artificial Pancreas
• CPS integrates a continuous feedback loop and remediation/corrective measures.
• For predictability of response, given the “operating” constraints.
Reading & References
Introduction to Embedded Systems
https://www.youtube.com/watch?v=9Q-3c0gQcok
Notes are at https://drive.google.com/drive/folders/0B5jlwlXJI8pJZ1hObzV4VHJNREk
_x000C__x000C_An embedded system
• is built to control a specific function or a range of functions and
• is not designed to be programmed by an end user.
Embedded Systems
1. Evolved as replacement for analog & discrete logic-based boards
2. Finer Control & Improvement of Electro-Mechanical Performance
3. Intellectual Property Protection
An embedded operating system is an operating system for embedded computer systems. This type of
operating system is typically designed to be resource-efficient and reliable. Resource efficiency comes at
the cost of losing some functionality or granularity that larger computer operating systems provide, including
functions which may not be used by the specialized applications they run. Depending on the method used
for multitasking, this type of OS is frequently considered to be a real-time operating system, or RTOS.
https://en.wikipedia.org/wiki/Embedded_operating_system
https://www.embedded.com/getting-started-with-embedded-linux-part-twelve-application-
development/
_x000C__x000C_Inside an Embedded System
1. Cores
The main criteria for the processor is: can it provide the processing power needed to perform the
tasks within the system? This seems obvious but it frequently occurs that the tasks are either
underestimated in terms of their size and/or complexity or that creeping elegance expands the
specification to beyond the processor’s capability.
2. Memory
Is an important part of any embedded system design and is heavily influenced by the software design;
memory essentially performs two functions within an embedded system:
Persistent Storage for software and .
Storage for data such as program variables and intermediate results
3. IO
The main types of IO interfaces include:
• Binary Interfaces These are simple external pins whose logic state can be controlled by the
processor to either be a logic zero (off) or a logic one (on).
• Serial Interfaces These are interfaces that send or receive data in a serial mode.
_x000C__x000C_Examples
• Evolved From Microcontroller & Expanded Microcontroller
Microcontrollers can be considered as self-contained systems with a processor, memory and IO so
that in many cases all that is needed to use them within an embedded system is to add software.
Microcontrollers are usually available in several forms:
• Devices for prototyping or low volume production runs
Using volatile/non-volatile memory to allow software to be downloaded and saved.
• Devices for low to medium volume production runs
One time programmable or OTP use.
• Devices for high volume production runs
For high volumes, microcontrollers can be built with already programmed software.
• microcontroller families having parts supporting external expansion for memory and/or I/O bus
• Microprocessor Based
Microprocessor-based embedded systems originally took existing general-purpose processors and
constructed systems around them using external peripherals and memory.
• Board Based
Instead of having hardware being designed and built; an alternative is to use board-based systems as
provided by commodity hardware. The main advantage is the reduced work load and the availability
of ported software that can simply be utilised with very little effort. The disadvantages are higher cost
and in some cases restrictions in the functionality that is available.
_x000C_RTOS
• Characterized by defined response time to external stimuli
• Maximum defined time is more important than avg.
• typical industry accepted figures for context switches and interrupt response times are about
10 microseconds
The future of Preempt-RT
https://bootlin.com/blog/real-time-summit-2018/
_x000C__x000C_Task Swapping Method
The choice of scheduler algorithms can play an important part in the design of an embedded system and
can dramatically affect the underlying design of the software. There are many different types of scheduler
algorithm that can be used, each with either different characteristics or different approaches to solving the
same problem of how to assign priorities to schedule tasks.
choice of scheduler algorithms
• important part in the design of an embedded system and dramatically affects the underlying
design of the software
1. Time Slice
Time slicing can be used within an embedded system where time critical operations are not
essential. To be more accurate about its definition, it describes the task switching mechanism
and not the algorithm behind it although its meaning has become synonymous with both.
Time slicing works by making the task switching regular periodic points in time. This means that
any task that needs to run next will have to wait until the current time slice is completed or until
the current task suspends its operation. This technique can also be used as a scheduling
method as will be explained later in this chapter. The choice of which task to run next is
determined by the scheduling algorithm and thus is nothing to do with the time slice mechanism
itself. It just happens that many time slice-based systems use a round-robin or other fairness
scheduler to distribute the time slices across all the tasks that need to run.
_x000C_ total processing time needed to run all of them may be considerably less than the time provided
within a single time slot. This can be solved by artificially creating more context switch points by
getting each task to suspend after completion.
This may offer only a partial solution because a higher priority task may still have to wait on a
lower priority task to complete. With time slicing, the lower priority task cannot be preempted and
therefore the higher priority task must wait for the end of the time slice or the lower priority task to
complete.
3. Cooperative Multitasking (?)
While it is not applicable to real-time operating systems but, it has been included for reference.
The idea of co-operative multitasking is that the tasks themselves co-operate between
themselves to provide the illusion of multitasking. This is done by periodically allowing other tasks
or applications the opportunity to execute.
This requires programming within the application and the system can be destroyed by a single
rogue program that hogs all the processing power. This method is therefore not reliable enough
for most real-time embedded systems
_x000C_Choice of Scheduler Algorithms
• pre-emption is the first choice for embedded systems because of its better system response
• assignment of task priorities, is based on scheduler algorithms
1. Rate Monotonic Scheduling “RMS”
Rate monotonic scheduling (RMS) is an approach that is used to assign task priority for a pre-
emptive system in such a way that the correct execution can be guaranteed. It assumes that
task priorities are fixed for a given set of tasks and are not dynamically changed during
execution. It assumes that there are sufficient task priority levels for the task set and that the
task set models periodic events only. This means that an interrupt that is generated by a serial
port peripheral is modelled as an event that occurs on a periodic rate determined by the data
rate, for example. Asynchronous events such as a user pressing a key are handled differently.
The key policy within RMS is that tasks with shorter execution periods are given the highest
priority within the system. This means that the faster executing tasks can pre-empt the slower
periodic tasks so that they can meet their deadlines. The advantage this gives the system
designer is that it is easier to theoretically specify the system so that the tasks will meet their
deadlines without overloading the processor. This requires detailed knowledge about each task
and the time it takes to execute. This and its periodicity can be used to calculate the processor
loading.
_x000C__x000C_Priority Inversion
• a lower priority task can continue running despite there being a higher priority task active and
waiting to pre-empt.
• Can occur due to
1. Disabling interrupts
While in the interrupt service routine, all other interrupts are disabled until the routine has
completed. This can cause a problem if another interrupt is received and held pending. What
happens is that the higher priority interrupt is held pending in favour of the lower priority one —
albeit that it occurred first.
As a result, priority inversion takes place until interrupts are reenabled at which point the higher
priority interrupt will start its exception processing, thus ending the priority inversion.
One metric of an operating system is the longest period of time that all interrupts are disabled.
This must then be added to any other interrupt latency calculation to determine the actual
latency period.
_x000C__x000C_Cyber Physical Systems is the integration of
• Computational elements
• Physical environment
• Feedback Loop
For safe, reliable, predictable operation.
_x000C_Examples
• Adaptive Cruise Control Systems
• Artificial Pancreas
• Avionics
• Smart-Grid Power Systems
• Robotic Manufacturing Systems
_x000C_Design Methodology
• Mathematical Modeling
• Properties
• Verification Algorithms
• Applications
_x000C_DESIGN CONSIDERATIONS
Processing power: How fast of a microprocessor will be required?
Memory requirements: What types of RAM and NVM will be needed? how much?
Peripherals: What peripherals are required?
Reliability: Should the system be fail-proof? May it fail occasionally? What is the tolerable downtime?
Future upgrade: How will field upgrades be performed?
_x000C_SOFTWARE
DESIGN OBJECTIVES
Cross-Platform Development Process
Cross-Development Toolchain
Executable and Linking Format
Memory Mapping
_x000C_SOFTWARE
DESIGN OBJECTIVES
Cross-Platform Development Process
Cross-Development Toolchain
Executable and Linking Format
Memory Mapping
_x000C_PROGRAMMING LANGUAGE
Compiled vs Interpreted: Assembly, Classic C vs Java, Python.
Speed of Execution: Parallelism, Load Characteristics
_x000C_Cross-Development Toolchain
_x000C_ELF Linking View
_x000C_PREDEFINED HEADERS
_x000C_PREDEFINED HEADERS
_x000C_PREDEFINED HEADERS
_x000C_PREDEFINED HEADERS
_x000C_HARDWARE TERMS - REVIEW
Microprocessor Characteristics
Von Neumann and Harvard architectures
I/O Addressing
Endianness
Memory organization of some classic microprocessors
1. PIC18F8720
2. Intel 8086
3. Intel Pentium
4. Arm
_x000C__x000C_Von Neumann Architecture
1. Data and instructions (executable code) are stored in the same address space.
2. The processor interfaces to memory through a single set of address/data buses.
Harvard Architecture
1. Data and instructions (executable code) are stored in separate address spaces.
2. There are two sets of address/data buses between processor and memory.
Complex Instruction Set Computer (CISC)
1. runs “complex instructions“ where a single instruction may execute several low-level operations
Reduced Instruction Set Computer (RISC)
1. runs compact, uniform instructions where the amount of work any single instruction accomplishes is
reduced.
_x000C_Examples
• Evolved From Microcontroller & Expanded Microcontroller
• Microprocessor Based
• Board Based
_x000C_Whether integers are presented from left to right or right to left
1. Little-endian: the least significant byte stored at the lowest memory address
2. Big-endian: the most significant byte stored at the lowest memory address
_x000C_INTEL PENTIUM
_x000C_INTEL PENTIUM
_x000C_ARM926EJ-S
_x000C_ARM926EJ-S
memory mapping (8-bit memory)
_x000C_ARM926EJ-S
memory mapping (32-bit memory)
_x000C_Embedded Operating Systems https://en.wikipedia.org/wiki/Embedded_operating_system
• An embedded operating system is an operating system for embedded computer systems, typically
designed to be resource-efficient and reliable.
• Resource efficiency comes at the cost of losing some functionality or granularity that larger computer
operating systems provide, including functions which may not be used by the specialized applications
they run.
Depending on the method used for multitasking, this type of OS is frequently considered to be a real-time
operating system, or RTOS.
_x000C_and execute applications; implying that the system is only able to run a single application and subtasks
within it.
https://en.wikipedia.org/wiki/Embedded_operating_system
_x000C_Notes PREEMPT_RT A real-time preemption overview
1) Since kernel 2.6.24 in mainline Linux
2) Since kernel 2.6.25 in mainline Linux
3) Realtime-Preempt patches 2.6.24.7-rt15 or higher required
4) Since kernel 2.6.30 in mainline Linux
5) Not yet adapted to generic interrupt code
6) Since kernel 2.6.33 in mainline Linux
7) Since kernel 2.6.39 in mainline Linux
Through the use of the real-time Linux kernel patch PREEMPT_RT, support for full preemption of critical
sections, interrupt handlers, and "interrupt disable" code sequences can be supported. [75]
Partial mainline [76]
integration of the real-time Linux kernel patch already brought some functionality to the
kernel mainline.
Preemption improves latency, increases responsiveness, and makes Linux more suitable for desktop
and real-time applications. Older versions of the kernel had a so-called big kernel lock for synchronization
across the entire kernel, which was finally removed by Arnd Bergmann in 2011. [77]
Recommended reading
OSADL Project: Realtime Linux https://www.osadl.org/Realtime-Linux.projects-realtime-linux.0.html
These two articles by Paul E. McKenney are somewhat outdated (2005 and 2007); in consequence, some
details are no longer reflecting the current situation of the PREEMPT_RT patches, but the principle is still
the same.
"A realtime preemption overview" by Paul E. McKenney
"SMP and Embedded Real Time" by Paul E. McKenney
_x000C_https://en.wikipedia.org/wiki/Template:Linux_kernel_timeline
_x000C_What is an OS?
1.Controls all application interaction with hardware
2.Generally is the kernel
• Role of file system(s), libraries, and applications
3.Is always memory resident in kernel space
4.Interface is through system calls for user processes
_x000C_ REAL-TIME
Terms and Concepts
Real-time systems are classed as hard and soft
• Hard real-time systems must meet deadlines.
Response cannot be missed or ignored.
Otherwise there could be an impact to safety or criticality.
e.g. medical systems, military systems.
• Soft real-time systems can afford to miss some deadlines.
e.g. audio or video streaming
• Many RT systems are a mix – there are real-time expectations,
but there is a tolerance built into the system.
engine controls.
_x000C_Real-Time systems have 2 major requirements
1. Latency is the time required for servicing a request.
The request must be handled immediately, completely and uninterrupted.
e.g reading a bar code.
2. Jitter is the variance between the earliest and the latest time a task could be released relative to the
invocation of the task, in a given sample interval. Jitter is noise.
e.g. sensor data handling.
_x000C__x000C__x000C__x000C_RT Microkernel Architecture
• real-time Linux involve major patches to the existing systems
• RTLinux and RTAI linux are both micro-kernel patches.
• Linux kernel runs as a low priority task from micro-kernel
• micro-kernel interrupts Linux to run a real-time task.
• Supports POSIX 1003.1d
_x000C_Microkernel Architecture
_x000C_RT
Nanokernel/Picokernel Architecture
• Small footprint Kernel
• Offers hardware abstraction, but
• without system services.
_x000C_Quiz
None This Week
• Starts Next Chapter/Week
_x000C_Assignment
None This Week
• Starts Next Chapter/Week
_x000C_CHAPTER OVERVIEW
In This Chapter, We saw
1. Introduction
2. Embedded System
3. Real Time Systems
4. Cyber Physical Systems
5. Microcomputers
6. Cross-compilers
7. No Assignment
8. No Quiz
_x000C_Q&A

## Slide 2
Introduction
Outcomes: O1
Notes: Embedded Operating Systems
https://en.wikipedia.org/wiki/Embedded_operating_system
• An embedded operating system is an operating system for embedded computer systems, typically designed
to be resource-efficient and reliable.
• Resource efficiency comes at the cost of losing some functionality or granularity that larger computer
operating systems provide, including functions which may not be used by the specialized applications they
run.
Depending on the method used for multitasking, this type of OS is frequently considered to be a real-time
operating system, or RTOS.

## Slide 3
Free ?
Software is considered free when its license offers to all its users
the following four freedoms:
* Freedom to run the software for any purpose
* Freedom to study the software and to change it
¢ Freedom to redistribute copies
¢ Freedom to distribute copies of modified versions
These freedoms are granted for both commercial and non-commercial use
They imply the availability of source code, software can be modified and
distributed to customers
Good match for embedded systems!
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O1
Notes: Free Software Timeline
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Timeline_of_free_and_open-source_software
https://en.wikipedia.org/wiki/History_of_free_and_open-source_software
• 1983, Richard Stallman, GNU project and the free software concept.
gcc, gdb, glibc and other important tools
• 1991, Linus Torvalds, Linux kernel project, a Unix-like operating system kernel.
a completely free operating system, GNU/Linux with GNU software and many open-source components
• 1995, Linux is popular on server systems
• 2000, Linux is popular on embedded systems
• 2008, Linux is popular on mobile devices
• 2010, Linux is popular on phones
• 2012, Linux is available on cheap, extensible hardware: Raspberry Pi, BeagleBone Black

## Slide 4
Chapter Objectives
In This Chapter
¢ Overview of Embedded Linux Systems
¢ Introduction to Embedded Linux Systems
* Examples of Embedded Linux Systems
¢ Hardware for Embedded Linux Systems
* System Architecture of Embedded Linux Systems
* Environment for Embedded Linux Systems Development
* No Assignment
* Quiz
Outcomes: O1
Notes: CHAPTER OVERVIEW
In This Chapter, We Will Discuss
1. Overview of Embedded Linux Systems
What is this course about?
2. Introduction to Embedded Linux Systems
What are embedded systems?
3. Examples of Embedded Linux Systems
Some Examples.
4. Hardware for Embedded Linux Systems
Again, some examples.
5. System Architecture of Embedded Linux Systems
Overview
6. Environment for Embedded Linux Systems Development
Introduction.
7. No Assignment
8. Quiz

## Slide 5
Embedded Linux
use of
¢ Linux Kernel and
¢ Other various open-source components
in embedded systems.
* https://en.wikipedia.org/wiki/Embedded operating system
Outcomes: O1
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Starting out
Linux became viable for embedded systems around 1999.
It was when
• Axis https://www.axis.com first released their Linux driven network camera, and,
• TiVo https://business.tivo.com released their Digital Video Recorder (DVR).
Since then, Linux has become ever more popular in the embedded systems area; to the point that it is the
preferred operating system of choice for many classes of product.
Today, in 2021, there are more than 2 billion devices running Linux across many classes of product.
These include
• a large number of cellphones that run Android – which internally uses a Linux Kernel
• to hundreds of millions of set top boxes, smart TVs, Wi-Fi routers, as well as
• a very diverse range of devices such as vehicle diagnostics, weighing scales, industrial devices, and
medical monitoring units.

## Slide 6
So, why Embedded Linux?
Why ?
¢ Full Operating System support for complexities of modern usage.
¢ Strong OS Features
¢ Ported to a wide range of processor architectures
¢ Open Source
¢ Very active community
* Open Source licenses
https://en.wikipedia.org/wiki/Linux_on_embedded_systems
Build Path: RT
Notes: Why Linux?
• Provides Full Operating System support needed for complexities of handling modern usage.
e.g. today’s TV is not the same as the old analog sets.
- handle digital encrypted streams that need processing to handle images.
- connected to internet
- receive content from smartphones, tablets and home media servers
- used to play games
• Strong OS Features such as good scheduler, good network stack, good support for USB, Wi-Fi, Bluetooth,
many kinds of storage media, good support for multimedia devices and so on. It ticks all boxes.
• Ported to a wide range of processor architectures, including those that are commonly found on SoC
designs – ARM, MIPS, x86 and PowerPC.
• Open Source means freedom to get the source code and modify it.
A board support package can easily be created for a particular Soc board or device.
Easily add protocols, features and technologies missing from mainline source code, and,
remove features not needed to reduce memory and storage requirements.
Linux is flexible.
• Very active community – means Linux is up to date with current hardware, protocols and standards.
New release of the kernel every 8 to 10 weeks; with each release containing code from 1000+ developers.
• Open Source licenses guarantee access to the source code. There is no vendor tie-in.

## Slide 7
Advantages of Linux
key advantage is the re-use of components.
* Open-source model provides many components
* open-source components support hardware devices, a protocol, or a
feature in wide-spread use
* enable quick design and development of complex products with
existing components.
¢ Provides focus on the value addition of the product.
https://en.wikipedia.org/wiki/Linux_on_embedded_systems
Outcomes: O1
Build Path: RT
Notes: key advantage is the re-use of components.
• open-source model provides many components for standard features, from hardware support to network
protocols, to multimedia, to graphics, to cryptographic libraries, etc.
• once a hardware device, or a protocol, or a feature gets to wide-spread use, there’s a high chance that
open-source components will support it.
• enable quick design and develop of complex products with existing components.
There is no need to develop another operating system kernel, TCP/IP stack, USB stack or another
graphical toolkit library.
• Provides focus on the value addition of the product.

## Slide 8
Advantages of Linux ..2
Low Cost.
* duplicate on as many devices, free of cost.
* usage of only free software means cost of licenses is Zero.
* even development tools are free.
* allows for higher budget elsewhere — hardware, training etc.
https://en.wikipedia.org/wiki/Linux_on_embedded_systems
Notes: Low Cost.
• duplicate on as many devices, free of cost.
• usage of only free software means cost of licenses is zero.
• even development tools are free.
• allows for higher budget elsewhere – hardware, training etc.
Using Linux will not be free of cost.
It will still need substantial learning and engineering efforts to achieve the goals.

## Slide 9
Advantages of Linux ..3
Full control - over the software part of your system
source code availability
¢ for all components in system,
¢ with unlimited modifications, changes, tuning, debugging, optimization,
¢ with no time limits
¢ with no lock-in or dependency from a third-party vendor
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Outcomes: O1
Build Path: debug
Notes: Full control - over the software part of your system
source code availability
• for all components in system,
• with unlimited modifications, changes, tuning, debugging, optimization,
• with no time limits
• with no lock-in or dependency from a third-party vendor
avoid any non-open-source components when the system is designed and developed, though.

## Slide 10
Advantages of Linux ..4
Quality
* widely used on millions of systems
¢ higher quality than in-house development, or from proprietary vendors
so, design system with high-quality components at the very foundations.
https://en.wikipedia.org/wiki/Linux_on_embedded_systems
Outcomes: O1
Notes: Quality
• widely used on millions of systems
• higher quality than in-house development, or from proprietary vendors
so, design system with high-quality components at the very foundations.
Though, not all open-source components are of good quality, but most of the widely-used ones are.

## Slide 11
Advantages of Linux ..5
Community support
* developed by communities of developers and users
* better than traditional support
* provides high-quality support:
* directly contact the main developers of the component you are using.
* answer doesn’t depend what company you work for.
so, speeds up the resolution of problems when developing systems
https://en.wikipedia.org/wiki/Linux_on_embedded_systems
Build Path: RT
Notes: Community support
• developed by communities of developers and users
• better than traditional support
• provides high-quality support:
• directly contact the main developers of the component you are using.
• answer doesn’t depend what company you work for.
so, speeds up the resolution of problems when developing systems
but need to understand how the community works to properly use the community support possibilities

## Slide 12
Advantages of Linux ..6
Taking part into the community
* for bug reporting, test of new versions or features, patches that fix bugs or add
new features, etc.
* open-source components are usually not the core value of the product: it's the
interest of everybody to contribute back.
* a very motivating way of being recognized outside the company,
communication with others in the same field, opening of new possibilities, etc.
* allows the company to be recognized in the open-source community and
therefore get support more easily and be more attractive to open-source
developers
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Outcomes: O1
Build Path: RT
Notes: Taking part into the community
• for bug reporting, test of new versions or features, patches that fix bugs or add new features, etc.
• open-source components are usually not the core value of the product: it’s the interest of everybody to
contribute back.
• a very motivating way of being recognized outside the company, communication with others in the same
field, opening of new possibilities, etc.
• allows the company to be recognized in the open-source community and therefore get support more easily
and be more attractive to open-source developers

## Slide 13
So, when not to choose Linux?
Is Linux suitable for the project?
* problem being solved does not justify the complexities of an OS.
¢ does hardware do the job?
* have the right skills?
* need real-time handling?
* need regulatory approval (medical, automotive, aerospace etc)
https://en.wikipedia.org/wiki/Linux_on_embedded_systems
Mastering Embedded Linux Proagrammina By Frank Vasquez. Chris Simmonds (Packt— Publisher)
Build Path: RT
Notes: Is Linux suitable for the project?
• problem being solved does not justify the complexities of an OS.
Linux works well when the problem justifies the need for an OS.
It is especially good where connectivity, robustness and complex user interfaces are required.
• does hardware do the job?
Linux needs more resources compared to traditional RTOS’s such as VxWorks and QNX.
It needs atleast a 32-bit processor and lots of memory.
• have the right skills?
handling the early part of a project, board bring up, requires detailed knowledge of Linux and how it relates
to problem being solved. Also, when debugging and tuning the application, the results need to be
interpreted.
• need real-time handling?
Linux can handle many real-time activities so long as certain steps/details are followed.
More to follow in Ch10.
• need regulatory approval (medical, automotive, aerospace etc)
the burden of regulatory verification and validation may make some other OS a better choice.
even if Linux is chosen in these circumstances, it may make sense to get a commercially available
distribution from a company that has supplied Linux for similar, existing products, being built.

## Slide 14
Linux on embedded systems
Linux is found in embedded systems such as
* consumer electronics (set-top boxes, smart TVs, personal video recorders (PVRs),
* in-vehicle infotainment (IVI),
* network equipment (routers, switches, wireless access points (WAPs) or wireless
routers),
* machine control,
* industrial automation,
* navigation equipment,
* spacecraft flight software,
* medical instrumentation, and
* many, many more areas.
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Mastering Embedded Linux Programming Rv Frank Vasquez. Chris Simmonds (Packt — Publisher)
Outcomes: O1
Build Path: RT
Notes: Linux is found in embedded systems such as
• consumer electronics (set-top boxes, smart TVs, personal video recorders (PVRs),
• in-vehicle infotainment (IVI),
• network equipment (routers, switches, wireless access points (WAPs) or wireless routers),
• machine control,
• industrial automation,
• navigation equipment,
• spacecraft flight software,
• medical instrumentation, and
• many, many more areas.
Because of versatility, Linux kernel can be also found in mobile devices that are touchscreen-based embedded
devices, such as smartphones and tablets, personal digital assistants (PDAs) and portable media players.
This is a challenge for most learners because their computer experience is mainly based on GUI (Graphical
user interface) based interaction with the machine and high-level programming on the one hand and low-level
programming of small microcontrollers on the other hand. Further, the concept of command line interfaces is
widely unknown.
Source: https://en.wikipedia.org/wiki/Linux_on_embedded_systems

## Slide 15
Exploring the embedded systems of the future https://www.securitysa.com/63410n
Notes: Integration of Home Energy Management Systems (“HEMS”)
Embedded systems of the future will have interfaces that make use of the same kinds of speech and
movement recognition facilities available today in a range of home-based devices.

## Slide 16
Home Energy Management Systems: An Overview https://www.osti.gov/servlets/purl/1423114
Notes: 1. Device Monitoring and Control:
HEMS need to be able to monitor and control different devices and appliances in a home. Device
information can be available to the user via either a web interface or phone/tablet application. In its
simplest form, device control should be available to the user manually. If the management system supports
smart scheduling, control can be automatic. Moreover, control of devices can be remote or local.
2. Seamless Communication between Devices:
HEMS provide communication between different devices. Each device may operate on a different
communication technology, such as Wi-Fi, ZigBee, Z-Wave, CTA-2045 and others. The system should be
capable of providing a way to support communication between different devices regardless of their
supporting communication protocol.
3. Demand Response:
The basic requirement of the system for supporting DR is the ability to receive DR signals from a utility. For
better DR support, information for multiple homes in a community needs to be available, and the system
needs to be able to use an optimization method to intelligently respond to DR signals and allocate
resources to the homes efficiently.
4. Intelligence:
Most homeowners do not have any visibility or understanding of their energy usage, so they may not be
able to make appropriate decisions to reduce consumption. It is beneficial for HEMS to provide feedback to
the user and make some automatic adjustments if allowed by the user. To achieve the energy-saving goal
of HEMS, smart scheduling and optimization algorithms need to be incorporated into the systems.
5. Data Management:
In the smart grid era, information regarding energy usage can be provided at different granularities from a
wide variety of devices. HEMS should be capable of handling very large amounts of data efficiently.
6. Security and Privacy:
HEMS carry a lot of information regarding residents’ energy usage patterns and daily schedules. All this
information needs to be encrypted and secure, as does communication between various devices and
HEMS

## Slide 17
4 elements of embedded Linux
Every embedded Linux project must obtain, customize, and deploy
* Toolchain: compiler and tools needed for creating code for target.
* Bootloader: program to initialize the board and load Linux kernel.
* Kernel: manages the system resources and interface to hardware.
* Root FS: Container for libraries and programs that are needed once
the kernel completes initialization.
Mastering Embedded Linux Proarammina Bv Frank Vasquez. Chris Simmonds (Packt— Publisher)
Outcomes: O2, O3, O4
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Every embedded Linux project must obtain, customize, and deploy
• Toolchain: compiler and tools needed for creating code for target.
• Bootloader: program to initialize the board and load Linux kernel.
• Kernel: manages the system resources and interface to hardware.
• Root FS: Container for libraries and programs that are needed once the kernel completes initialization.
These 4 elements are offered as a package when a SoC or board is bought.
However, they may not be the best choice or offer the full value addition, expected.
- There is also the 5th element – that of, the application that enables the device to run and function.
This is where we look at two tools to automate the whole process: Yocto project and Buildroot.

## Slide 18
Roles and Expectations
Who writes open source?
How about 4 elements of embedded Linux? Who maintains them?
* Open-Source Community: Loose knit alliance of developers
from non-profit, for profit or academic institutions.
¢ Hardware Architects: Designers of the CPU.
They implement, or influence support for a CPU architecture.
* SoC Vendors: Take the kernel and toolchain from the architects and modify to
support their chips. They also create the reference boards.
* Board Vendors: Take the reference boards and design from the SoC Vendors
and build them into specific products.
« Linux Vendors: Offer Linux distributions that underwent strict regulatory
verification and validation across industry expectations/standards
Mastering Embedded Linux Programming Rv Frank Vasquez. Chris Simmonds (Packt — Publisher)
Outcomes: O1, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Roles and Expectations
• Open-Source Community: Loose knit alliance of developers from non-profit, for profit or academic
institutions.
• Hardware Architects: Designers of the CPU – implement, or influence support for a CPU architecture.
e.g. Arm/Linaro (Arm Cortex-A) , Intel (x86, x86_64), SiFive (RISC-V), IBM (PowerPC).
• SoC Vendors: Take the kernel and toolchain from the architects and modify to support their chips.
They also create the reference boards – designs used by board vendors to create development boards
and working products. e.g. Broadcom, Intel, Microchip, NXP, Qualcomm, TI, Xilinx and many others.
• Board Vendors: Take the reference boards and designs from the SoC Vendors and build them into
specific products. e.g. set-top boxes, cameras or create general purpose development boards.
An important category are the cheap development boards such as the Raspberry Pi and BeagleBoard
that have their own ecosystem of software and hardware.
• Linux Vendors: Offer Linux distributions that underwent strict regulatory verification and validation
across industry expectations/standards – such as medical, automotive, aerospace etc. Also, companies
such as Timesys, Wind River offer commercial Linux distributions.
These form a chain – meaning that there is no free choice of components.
The latest kernel from https://www.kernel.org cannot simply be taken;
usually, it does not have the support for the chip or board being used.
https://en.wikipedia.org/wiki/Embedded_operating_system

## Slide 19
Planning and Steps
Embedded Linux Development
Development Workflow
* Board Bring-Up: setup the development environment and create a working platform.
* System Design: decision about system architecture, storage of programs and data
* Applications Development: deploy Python applications, use Linux Process & Threads
* Optimization and Debug: trace, profile and debug in application and in kernel
Mastering Embedded Linux Proagrammina By Frank Vasquez. Chris Simmonds (Packt— Publisher)
Outcomes: O1, O2, O4
Build Path: cross-dev
AI Layer: L1-BuildAssistant
Notes: Development Workflow
• Board Bring-Up: setup the development environment and create a working platform.
• System Design: decision about system architecture, storage of programs and data
also, howo to divide work between kernel device drivers and applications; and, how to initialize the
system
• Applications Development: deploy Python applications, use Linux Process & Threads
how to deploy and package, how to effectively use Linux process and thread model, and how to manage
memory in a resource-constrained device.
• Optimization and Debug: trace, profile and debug – both, in application and in kernel

## Slide 20
Embedded Linux Development
using Open Source
Components are Open Source.
Consider
* What it means?
« Why Open-Source works the way it does?
* How it impacts the “often” proprietary embedded device created from it?
Mastering Embedded Linux Proagrammina By Frank Vasquez. Chris Simmonds (Packt— Publisher)
Notes: Components are Open Source.
Consider
• What it means?
• Why Open-Source works the way it does?
• How it impacts the “often” proprietary embedded device created from it?

## Slide 21
Licenses and
using Open Source
What does “free” mean when referencing Open Source?
* When you first hear of it, is it “nothing to pay”?
* Certainly, Open-Source guarantees using the software to develop and deploy, for free
* However, the important idea is that — there is the freedom and guarantee to obtain the
source, modify it in anyway needed and, then redeploy it.
* It is this guarantee or license that provides the right of use.
* In contrast, compare with
* freeware which permit copying of binaries, however, there is no access to source, or
* free for personal, non-commercial use.
Mastering Embedded Linux Proarammina Bv Frank Vasquez. Chris Simmonds (Packt— Publisher)
Outcomes: O4
Notes: Licenses and using Open Source
Open Source licenses are generally in two categories:
• copyleft licenses such as GPL – GNU Public License, and,
• permissive licenses such as BSD and MIT licenses.

## Slide 22
So, What are Permissive Licenses?
They permit
* modification of source code, and using in whichever way needed, so long as
* The terms of the license are not modified.
Mastering Embedded Linux Programming By Frank Vasquez. Chris Simmonds (Packt— Publisher)
Notes: Permissive Licenses have that one restriction, and except that
• permit any modifications
• permit any use

## Slide 23
And, What is GPL?
Are similar to permissive, in that, they too permit
* modification of source code, and using in whichever way needed,
however,
« they mandate the passing of the rights to obtain and modify the source to the users.
Mastering Embedded Linux Proagrammina By Frank Vasquez. Chris Simmonds (Packt— Publisher)
Outcomes: O1
Notes: GPL Licenses, similarly as well
• permit any modifications
• permit any use
However, with the requirement that
• the source code is freely available.
One option is to put the source code on a public server, and,
Another option is to offer it to end-users upon a written request
Further, GPL prohibits incorporating GPL code into proprietary programs.
If any way it is done, then, that would make the GPL apply to the whole – meaning that GPL and proprietary
programs cannot be combined.
In addition to the Linux Kernel,
• gcc collection,
• gdb, and
• many other similar tools
associated with the GNU project – all are covered by GPL.
Most standard libraries are licensed under GNU Lesser General Public License.
• this permits linking to them from proprietary programs, otherwise,
• if they are linked under GPL, then, as above, everything becomes GPL.
Then, there are issues too
• security
similar to the owner, an intruder can have to the system code.
• the defense to this is that, the images are signed by the vendor, so that unauthorized updates aren’t done.
But, that is an infringement of the owner’s rights to modify the software.

## Slide 24
Hardware Selection
What to look for when selecting hardware for an embedded Linux project.
« CPU Architecture — supported by kernel.
« Adequate Physical RAM
* non-volatile storage
+ Serial port for debug
* Initial Software loader
Mastering Embedded Linux Proagrammina By Frank Vasquez. Chris Simmonds (Packt— Publisher)
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: What to look for when selecting hardware for an embedded Linux project.
• CPU Architecture – supported by kernel.
• Adequate Physical RAM
• non-volatile storage
• Serial port for debug
• Initial Software loader

## Slide 25
Hardware Selection
for this class
Examples are intended to be generic.
However, for this class, please go with either
« Raspberry Pi 4
* Beaglebone Black, or
* QEMU
Mastering Embedded Linux Programming By Frank Vasquez. Chris Simmonds (Packt— Publisher)
Outcomes: O7
Notes: Hardware Selection for this class.
• Examples are intended to be generic.
please go with either
• Raspberry Pi 4, 3 or 3 model B.
Most popular ARM-based single board computer on the market
• Beaglebone Black, or
widely available and cheap development board that can be used for serious embedded programming
Though several years old, it is open source hardware – unlike Raspberry Pi; meaning that board designs
are freely available for anyone to build on top of the BeagleBone Black.
• QEMU
is a machine emulator that can be used to create a range of systems typical of embedded hardware.
Raspberry Pi 4,
• Beaglebone Black, or
• QEMU

## Slide 26
Hardware used
for this course
Raspberry PI 4 for assignments. (or 3 or 3B), or BeagleBoard Black or QEMU
¢ Broadcom BCM2711, Quad core Cortex-A72 (ARM v8) 64-bit Soc @ 1.5GH
¢ 2GB, 4GB or 8GB LPDDR4-3200 SDRAM (depending on model)
¢ Gigabit Ethernet, 2.4 & 5.0 GHz IEEE 802.11ac wireless, Bluetooth 5.0, BLE
¢ 2 USB 3.0 ports; 2 USB 2.0 ports.
* Micro-SD card slot
* standard 40 pin GPIO header (fully backwards compatible with previous boards)
¢ 2x micro-HDMI ports (up to 4kp60 supported)
Since most of you have already purchased
the Raspberry PI and USB-TTL cable
Development Environment:
Linux (Ubuntu)
Notes: Specs for Raspberry PI 4
https://www.raspberrypi.org/products/raspberry-pi-4-model-b/specifications/
• Broadcom BCM2711, Quad core Cortex-A72 (ARM v8) 64-bit SoC @ 1.5GHz
• 2GB, 4GB or 8GB LPDDR4-3200 SDRAM (depending on model)
• 2.4 GHz and 5.0 GHz IEEE 802.11ac wireless, Bluetooth 5.0, BLE
• Gigabit Ethernet
• 2 USB 3.0 ports; 2 USB 2.0 ports.
• Raspberry Pi standard 40 pin GPIO header (fully backwards compatible with previous boards)
• 2 × micro-HDMI ports (up to 4kp60 supported)
• 2-lane MIPI DSI display port
• 2-lane MIPI CSI camera port
• 4-pole stereo audio and composite video port
• H.265 (4kp60 decode), H264 (1080p60 decode, 1080p30 encode)
• OpenGL ES 3.1, Vulkan 1.0
• Micro-SD card slot for loading operating system and data storage
• 5V DC via USB-C connector (minimum 3A*)
• 5V DC via GPIO header (minimum 3A*)

## Slide 27
Quiz
Canvas
¢ 10 Questions
¢ 45 Mins
¢ 6 Attempts
¢ Highest Retained

## Slide 28
Assignment
1. None.
2. Make sure that you have the hardware unit for this class, for next
week.
AI Layer: L1-BuildAssistant

## Slide 29
Summary
In This Chapter
* Introduction
¢ Embedded Systems
* Real Time Systems
* Cyber Physical Systems
¢ Microcomputers
¢ Cross-compilers
* No Assignment/Quiz — this week.
Outcomes: O1, O2, O3
Build Path: cross-dev
AI Layer: L1-BuildAssistant
Notes: CHAPTER OVERVIEW
In This Chapter, We saw
1. Introduction
2. Embedded System
3. Real Time Systems
4. Cyber Physical Systems
5. Microcomputers
6. Cross-compilers
7. No Assignment/Quiz – this week.