## Slide 1
Toolchains & Bootloaders
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Toolchain https://en.wikipedia.org/wiki/Toolchain
• is the first element of embedded Linux, and is used to compile all the code to run on the device.
It is the starting point of the project.
• makes efficient use of hardware by using optimum instruction set for the processor.
• proper selection at an early stage has a profound impact on the final outcome.
Bootloader https://en.wikipedia.org/wiki/Bootloader
• is the second element of embedded Linux.
It is used to start the system and load the operating system kernel.
• control is passed from itself to the kernel using a data structure called a flattened device tree (FDT).
• e.g. U-Boot is a popular bootloader
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 2
Free ?
Software is considered free when its license offers to all its users
the following four freedoms:
¢ Freedomto run the software for any purpose
* Freedomto study the software and to change it
* Freedomto redistribute copies
* Freedom to distribute copies of modified versions
These freedoms are granted for both commercial and non-commercial use
They imply the availability of source code, software can be modified and
distributed to customers
Good match for embedded systems!
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O1
Notes: Free Software Timeline
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Timeline_of_free_and_open-source_software
https://en.wikipedia.org/wiki/History_of_free_and_open-source_software
• 1983, Richard Stallman, GNU project and the free software concept.
gcc, gdb, glibc and other important tools
• 1991, Linus Torvalds, Linux kernel project, a Unix-like operating system kernel.
a completely free operating system, GNU/Linux with GNU software and many open-source components
• 1995, Linux is popular on server systems
• 2000, Linux is popular on embedded systems
• 2008, Linux is popular on mobile devices
• 2010, Linux is popular on phones
• 2012, Linux is available on cheap, extensible hardware: Raspberry Pi, BeagleBone Black

## Slide 3
Chapter Objectives
In This Chapter
* Overview and Introduction to Toolchains
* Understanding and Building a Toolchain, linking and cross-compiling
¢ Overview and Introduction to Boot Loaders
* Introduction to boot sequence and
how boot loaders transfer control to kernel
¢ Device trees and U-Boot
* Assignment
* Quiz
Outcomes: O1, O2, O3, O4
Build Path: cross-dev
AI Layer: L1-BuildAssistant
Notes: CHAPTER OVERVIEW
In This Chapter, We Will Discuss
1. Overview and Introduction to Toolchains
What are Toolchains?
2. Understanding and Building a Toolchain, cross-compiling and linking.
types of toolchains, choosing C library, cross-compiling and linking.
3. Overview and Introduction to Boot Loaders
What are boot loaders? Why are they needed?
4. Introduction to boot sequence
how boot loaders transfer control to kernel.
5. System Architecture of Embedded Linux Systems
Overview
6. Device trees and U-Boot
Introduction to device trees and U-Boot
7. Assignment
8. Quiz

## Slide 4
Toolchain
¢ Aset of tools that compile source code into executables
¢ Includes a compiler, linker and runtime libraries
* to run ona falgel device
¢ Atoolchain remains constant throughout the life of a project.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
¢ https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Toolchain https://en.wikipedia.org/wiki/Toolchain
In software, a toolchain is a set of programming tools that create a software product, to run on a target device.
The tools forming a toolchain are executed consecutively so the output or resulting environment state of each
tool becomes the input or starting environment for the next one. However, the term is also used when referring
to a set of related tools that are not necessarily executed consecutively.
A simple software development toolchain consist of a compiler and linker, libraries, and a debugger.
e.g. a complex software product such as a video game needs tools for preparing sound effects, music,
textures, 3-dimensional models and animations, together with additional tools for combining these resources
into the finished product.
--
A toolchain
• is required to build the other three elements of the embedded Linux system – bootloader, kernel and root
filesystem.
• has to be able to compile code written in assembly, C and C++ since these are the languages used in the
base open source packages.

## Slide 5
Toolchain
definition
+ is the set of development tools available on a GNU/Linux system
+ that includes a compiler, linker and runtime libraries
+ that run on a system and generate code for the same system.
* target cannot contain the development tools needed on the target.
* target is too restricted in terms of resources such as storage or memory
* target is too slow compared to the development system
* so, tools are run on the development system, but generate code for target
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Toolchain
Outcomes: O1, O2, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Toolchain https://en.wikipedia.org/wiki/Toolchain
• is the set of development tools available on a GNU/Linux system
• that includes a compiler, linker and runtime libraries
• that run on a system and generate code for the same system.
• it is known as a native toolchain
However, on embedded systems, it is usually impossible to use native toolchain,
• target cannot contain the development tools needed on the target.
• target is too restricted in terms of resources such as storage or memory
• target is too slow compared to the development system
• so, tools are run on the development system, but generate code for target
• it is known as a cross-compiling toolchain

## Slide 6
Toolchain
machines used in build procedures
* Some terms
* build machine — where the toolchain is built
+ BBE machine — where the toolchain is executed, and binaries are generated
+ FBigel machine - where the binaries are executed
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides. pdf
https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: • Some terms
• build machine – where the toolchain is built
• host machine – where the toolchain is executed, and binaries are generated
• target machine – where the binaries are executed

## Slide 7
Toolchain
combinations of build procedures
* Some terms
* Native Build -— where the build, host and target are all for same architecture.
* Cross-Native Build — where build is on a different architecture,
while Host and Target are same
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides. pdf
https://en.wikipedia.org/wiki/Toolchain
Outcomes: O2, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Native Build
• All are same architecture
Cross-Native Build
• Build is on a separate architecture, as compared to host and target.
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf

## Slide 8
Toolchain
combinations of build procedures
* Some terms
* Cross Build — where the build and host are on same architecture,
while target is different
* Canadian Cross Build — where the Build, Host and Target are each
on a different architecture.
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides. pdf
https://en.wikipedia.org/wiki/Toolchain
Outcomes: O2, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Cross Build
• where the build and host are on same architecture, while target is different
• This is the most common scenario in embedded systems development.
Canadian Cross Build –
• where the Build, Host and Target are each on a different architecture.
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf

## Slide 9
Toolchain
components of toolchains
* components
* binutils
* kernel headers
* C/C++ compiler - @.g. gcc
* C/C++ libraries - e.g. glibc
* Debugger - e.g. gdb
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides. pdf
https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Binutils
is a set of tools to generate and manipulate binaries for a given CPU architecture
• as, the assembler, that generates binary code from assembler source code
• ld, the linker
• ar, ranlib, to generate .a archives (static libraries)
• objdump, readelf, size, nm, strings, to inspect binaries. Very useful analysis tools!
• objcopy, to modify binaries
• strip, to strip parts of binaries that are just needed for debugging (reducing their size).
GNU binutils is at https://www.gnu.org/software/binutils/
kernel headers
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
needed to compile C library and the applications
• available in <linux/...> and <asm/...> and a few other directories corresponding to include/uapi/ and in
arch/<arch>/include/uapi in the kernel sources
• extracted from the kernel sources using the headers_install kernel Makefile target.
programs never break existing when the kernel is upgraded.
• kernel to user space ABI is backward compatible .. ABI = Application Binary Interface - binary compatibility
otherwise, application systems would stick to older kernels.
• binaries generated with a toolchain using kernel headers older than a running kernel will work without
problem, but won’t be able to use the new system calls, data structures, etc.
programs never break existing when the kernel is upgraded.
• Similarly, binaries generated with a toolchain using kernel headers newer than the running kernel will work
only if they don’t use the recent features, otherwise they will break.
• updating the kernel will not break programs;
it’s usually fine to keep an old toolchain as long is it works fine for the project.
compiled programs and applications need to interact with the kernel and need kernel headers for
• available system calls and their numbers
• constant definitions
• data structures, etc.
C/C++ compiler
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
• GCC: GNU Compiler Collection
https://gcc.gnu.org/
• famous and ubiquitous
• compile C, C++, Ada, Fortran, Java, Objective-C, Objective-C++, Go, etc.
• generate code for a large number of CPU architectures, including x86, ARM, RISC-V, and many others.
• under the GPL license, libraries under the GPL with linking exception of LGPL.
• Clang / LLVM compiler
https://clang.llvm.org/
• increasingly popular and able to compile most programs
• offer better optimizations and makes errors easier to interpret.
• under MIT/BSD license type.
C library
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
provides C standard API for application development
• interface between the applications and the kernel
• essential component of a Linux system
• many several C libraries are available: glibc, uClibc, musl, klibc, newlib...
see https://www.etalabs.net/compare_libcs.html for a comparison – attached to the More Reading section
in this chapter.
C library decision must be made at cross-compiling toolchain generation time

## Slide 10
Toolchains for Linux
GCC
* Traditional base for toolchains for Linux
* Support for wide ranging architectures and operating systems, meaning
compatibility for existing code bases CLANG
* Now a viable alternative to the GNU GCC compiler.
* Faster compilation times and better diagnostics
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on embedded systems
Outcomes: O1, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Toolchains for Linux
• Traditionally toolchains for Linux were based on the GNU GCC compiler and components from the project.
It is still true as of today.
• Clang is newer and with faster compilation times. Also, it has better diagnostics.
• One major distinction is that GNU GCC has a GPL license, while LLVM has a BSD license.
Having said that,
• GNU GCC has support for wide ranging architectures and operating systems, meaning compatibility for
existing code bases, while,
• though it has taken time, the Clang compiler and the associated Low Level Virtual Machine project are now
a viable alternative, being able to compile all the components needed for embedded Linux. The Clang
compiler based approach will be covered later, in the course.
A standard GNU toolchain has:
• Binutils: a set of binary utilities including assembler and linker – available at
https://gnu.org/software/binutils
• GCC: GNU Compiler Collection – for C and other languages such as C++, Objective-C/C++, Java, Fortran,
Ada and Go .. all use a common backend that produces assembler code fed to GNU assembler.
• C library: POSIX based API that is the main interface to the kernel for applications. There are several libs.

## Slide 11
Types of Toolchains
Two types of toolchains.
* native - meaning same type of system as the program it generates.
* cross - meaning different type of system than the target.
Almost all embedded Linux development is done using a cross
development toolchain.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_embedded_ systems
Outcomes: O2, O3
Build Path: cross-dev
AI Layer: L1-BuildAssistant
Notes: Two types of toolchains.
• native - meaning same type of system as the program it generates.
• cross - meaning different type of system than the target.
Almost all embedded Linux development is done using a cross development toolchain.
• because embedded devices are not well suited to program development.
• they lack computing power, memory and storage
• More so, if the host and target architectures are same/similar.
It is not a good idea to copy over the binaries to the target, since host distribution updates will occur more
frequently than the target system distribution; or that the libraries on the target are optimized in a different
manner than the host.
• Sticking to a host distribution version is not a bad idea.
It ensures the golden rule .. that the target toolchain remains constant within the duration of a project.
• A better approach is to keep separate the host and target development environments, using a cross
toolchain.

## Slide 12
CPU Architectures
A toolchain has to be built for the target CPU.
¢ CPU architecture: ARM, MIPS, x86_64 etc
* Big- or little-endian: machine code is different for each especially since
some CPUs can operate in both modes.
* Floating point support: Not all embedded CPUs have hardware FPU,
so the toolchain has to be configured to support a software floating point
library.
¢ ABI-Application Binary Interface — calling convention for passing
parameters between function calls.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Outcomes: O1, O2, O3, O4, O7
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: A toolchain has to be built for the target CPU.
• CPU architecture: ARM, MIPS, x86_64 etc
• Big- or little-endian: machine code is different for each specially as some CPUs operate in either modes.
• Floating point support: Not all embedded CPUs have hardware FPU, so the toolchain must be configured
to support a software floating point library.
• ABI – Application Binary Interface – calling convention for passing parameters between function calls.
ABI is constant across a family of processors, however in ARM
• ABI from prior to 2000 was renamed to OABI - “Old ABI”
• Newer ABI since 2000, was also called EABI - “Extended ABI”; however, thereafter EABI split into two
depending on how floating point parameters are passed:
• Original EABI used general purpose registers in the integer format, while the
• Later EABI uses floating point registers for parameter passing. It is called EABIHF “EABI Hard Float”.
EABIHF is significantly faster since it removes the need for copying of the passed integer values in
registers into floating point registers.
• EABIHF is not compatible with CPUs that do not have a FPU; and so, a design decision is to be made,
since EABIHF is not compatible with the original EABI.

## Slide 13
Choosing a C library
C library -
* is a programming interface to Linux OS defined by POSIX.
* is implementation of the interfaces to the kernel for applications.
Even if programs are in Java or Python, the C library is to be eventually invoked.
* C Library can be bypassed; however, it is a lot of unnecessary trouble.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_embedded_ systems
Outcomes: O4
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: C library –
• is a programming interface to Linux OS defined by POSIX.
• is implementation of the interfaces to the kernel for applications.
Even if programs are in Java or Python, the C library is to be eventually invoked.
• C Library can be bypassed; however, it is a lot of unnecessary trouble.
Though there are many C Libraries to choose from, the main ones are:
glibc: standard GNU C libc library that is available under LGPL license 2.1. It is big and not very configurable,
however it is the most complete implementation of POSIX API.
musl: libc library that is newer and is available under MIT license. It is smaller and standards compliant
alternative to glibc. It is good for systems with limited RAM and storage.
uClibc-ng: is the C library for microcontroller architectures – Linux for CPU’s without MMUs that is licensed
under LGPL 2.1. uClibc-ng is a fork of the original uClibc. Not being used much unless using uClinux.
eglibc: variant of glibc for embedded systems. It is now obsolete, since the code base from eglibc was merged
back into glibc in glibc 2.20 – and so, eglibc is no longer maintained.

## Slide 14
Choosing a C library
glibc
glibc C library from the GNU project. License LGPL. https:/Avww.gnu.org/softwarellibc/
* on all GNU / Linux host systems —
performance, standards compliance and portability
* quite big for small embedded systems.
on armv7hf, version 2.31: libc: 1.5 MB, libm: 432 KB
source: https://toolchains.bootlin.com
* features not needed in embedded systems can be configured out
(merged from old eglibc project).
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on embedded systems
Outcomes: O1, O2, O3, O7
Build Path: cross-dev
AI Layer: L1-BuildAssistant
Notes: glibc C library from the GNU project. License LGPL. https://www.gnu.org/software/libc/
• on all GNU / Linux host systems –
performance, standards compliance and portability
• quite big for small embedded systems.
on armv7hf, version 2.31: libc: 1.5 MB, libm: 432 KB
source: https://toolchains.bootlin.com
• features not needed in embedded systems can be configured out
(merged from old eglibc project).

## Slide 15
Choosing a C library
uClibc-ng
uClibc-ng uClibc-ng continuation of old uClibc. License LGPL. https://uclibc-ng.org/
* for most embedded arch. incl. MMU-less ones (ARM Cortex-M, Blackfin, ...).
the only library supporting ARM noMMU.
* lightweight C library for small embedded systems — high configurability
* features may be implemented later than on glibc (real-time, floating-pt ops etc).
* no guaranteed binary compatibility.
need to recompile applications when the library configuration changes.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on embedded systems
Outcomes: O1, O4, O7
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: uClibc-ng uClibc-ng continuation of old uClibc. License LGPL. https://uclibc-ng.org/
• for most embedded arch. incl. MMU-less ones (ARM Cortex-M, Blackfin, ...).
the only library supporting ARM noMMU.
• lightweight C library for small embedded systems – high configurability
• features may be implemented later than on glibc (real-time, floating-pt ops etc).
• no guaranteed binary compatibility.
need to recompile applications when the library configuration changes.
• Size on armv7hf, version 1.0.34: libc: 712 KB,
source: https://toolchains.bootlin.com

## Slide 16
Choosing a C library
mus! C library
mus! C library. License MIT. httos://www.must-libe.org/
* lightweight, fast and simple library for embedded systems
* great at making small static executables
* supported by build systems such as Buildroot and Yocto Project
and, used by the Alpine Linux lightweight distribution
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Outcomes: O1
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: musl C library. License MIT. https://www.musl-libc.org/
• lightweight, fast and simple library for embedded systems
• great at making small static executables
• supported by build systems such as Buildroot and Yocto Project
and, used by the Alpine Linux lightweight distribution
• Size on armv7hf, version 1.2.0: libc: 748 KB,
source: https://toolchains.bootlin.com.

## Slide 17
Choosing a C library
some other smaller C libraries
Several other smaller C libraries have been developed,
but none of them have a goal of allowing compilation of large existing applications
typically very small static executables
only relatively simple programs, and
in very small root filesystems.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on embedded systems
Outcomes: O1, O4, O6
Build Path: toolchain
Notes: Several other smaller C libraries have been developed,
but none of them have a goal of allowing compilation of large existing applications
• typically, very small static executables
• only relatively simple programs, and
• in very small root filesystems.
Some choices:
• Newlib, https://sourceware.org/newlib/
maintained by Red Hat,
used mostly in Cygwin, in bare metal and in small POSIX RTOS.
• Klibc, https://en.wikipedia.org/wiki/Klibc
from the kernel community,
designed to implement small executables for use in an initramfs at boot time.

## Slide 18
Choosing a C library
how to?
C library
So, how to select
* If using uClinux then go with uClibc-ng, else
* If < 32MB storage then use mus! libc, else
* Use glibc
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_embedded_ systems
Build Path: toolchain
Notes: C library
So, how to select
• If using uClinux then go with uClibc-ng, else
• If < 32MB storage then use musl libc, else
• Use glibc
The choice of the C library limits the choice of toolchain,
since not all pre-built toolchains support all C libraries.
Size Tests run with gcc 10.0.2 toolchains for armv7-eabihf
• using small static executables - compile statically a hello.c program, and strip
• With musl 1.2.0: 9,084 bytes
• With uclibc-ng 1.0.34 21,916 bytes.
• With glibc 2.31: 431,140 bytes
• compile statically BusyBox 1.32.1, and strip
• With musl 1.2.0: 1,176,744 bytes
• With uclibc-ng 1.0.34 : 1,251,080 bytes.
• With glibc 2.31: 1,852,912 bytes
• Compiling with shared libraries will mostly eliminate size differences.

## Slide 19
Choosing a C library
how to?
General Advice
start developing and debugging applications with glibc,
« itis the most standard solution.
* if everything works, and if there are size constraints,
try to compile the app and then the entire filesystem with uClibc or musl.
* if not, it could be because of missing features in the C library.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Outcomes: O1, O4, O6
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: General Advice
start developing and debugging applications with glibc,
• it is the most standard solution.
• if everything works, and if there are size constraints,
try to compile the app and then the entire filesystem with uClibc or musl.
• when making static executables, musl is an easier choice in terms of licensing.
the binaries are smaller too.
• if not, it could be because of missing features in the C library.
Also, static executables built with some C library could be used in a system with a different C library.

## Slide 20
GNU prefix
GNU uses a prefix to the name of each tool in a toolchain
* Identifies combination that was used to generate that component
* e.g. x86_64-linux-gnu, mipsel-unknown-linux-gnu
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: GNU uses a prefix to the name of each tool in a toolchain
• Identifies combination that was used to generate that component
e.g. x86_64-linux-gnu, mipsel-unknown-linux-gnu
• It consists of a tuple of 3 or 4 parts
• CPU: such as ARM, MIPS, x86_64.
further if a CPU has both endian modes, they are differentiated by
el - for little-endian, and
eb - for big-endian
e.g. mipsel and armeb
• Vendor: provider of toolchain.
e.g. buildroot, poky or unknown. Sometimes it is left out altogether.
• Kernel: for now, always Linux.
• OS: name for userspace C library – gnu or musl an alternative C standard library for Linux.
https://en.wikipedia.org/wiki/Musl
sometimes ABI is appended – so examples are gnueabi, gnueabihf, musleabi or musleabihf
e.g.
• x86_64-linux-gnu Indicates CPU of x86-64, kernel of Linux and userspace library of GNU
• mipsel-unknown-linux-gnu Indicates CPU of MIPS with little endian mode, an unknown vendor of
toolchain, a Linux kernel and a userspace library of GNU

## Slide 21
Toolchain
Options
Considerations
° ABI
¢ Floating Point support
* CPU optimization flags
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Outcomes: O1, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Considerations when building a toolchain
• Define ABI “Application Binary Interface” for generating binaries needs to be defined
ABI defines the calling conventions (how function arguments are passed, how the return value is passed,
how system calls are made) and the organization of structures (alignment, etc.)
All binaries in a system are typically compiled with the same ABI, and the kernel must understand this ABI.
On ARM, two main ABIs: OABI and EABI. Today everybody uses EABI
On MIPS, several ABIs: o32, o64, n32, n64 https://en.wikipedia.org/wiki/Application_Binary_Interface
• Floating point support
Some processors have a floating point unit, while others do not.
e.g., many ARMv4 and ARMv5 CPUs do not have a FPU. Since ARMv7, a VFP unit is mandatory.
With an FPU, the toolchain should generate hard float code, in order to use FP instructions directly
Else, for processors without a floating point unit, two solutions
• Generate hard float code and rely on kernel to emulate the floating point instructions. This is very slow.
• Generate soft float code, so that instead of generating floating point instructions, calls to a user space
library are generated
Decision is taken at toolchain configuration time

## Slide 22
Toolchain
Obtaining one
3 choices
* find a ready-built toolchain
* generate using an embedded build tool, or
* create one
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on embedded systems
Outcomes: O1, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: 3 choices
• find a ready-built toolchain
• generate using an embedded build tool, or
• create one
A prebuilt cross toolchain is attractive since it only has to be downloaded and installed; however, the
dependency on the configuration of the toolchain or the person or tool that built it.
Most likely, it will be:
• From a SoC or board vendor: since most vendors offer a Linux toolchain.
• From a consortium providing support for a given architecture: e.g. Linaro with pre-built toolchain for ARM
architecture.
• From a 3rd party Linux tool vendor, such as Mentor Graphics, Timesys or MontaVista.
• From the cross-tool packages of the Linux distro: Debian has packages for cross compiling ARM, MIPS and
PowerPC.
• From a binary SDK from an embedded build tool: Yocto Project and examples at yoctoproject.org
The main thing to decide is whether the prebuilt toolchain meets the requirements.
• Does it use the preferred C library?
• Does provider provide updates for security fixes and bugs? If so, whether directly or upstream? How often?
If either above is no, then consider creating your own.
However, even that is not easy. To build from scratch, look at Cross Linux from Scratch https://trac.clfs.org, for
step-by-step instructions on how to create each component.

## Slide 23
Building a Toolchain
Community support
* developed by communities of developers and users
* better than traditional support
* provides high-quality support:
* directly contact the main developers of the component you are using.
* answer doesn’t depend what company you work for.
so, speeds up the resolution of problems when developing systems
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Outcomes: O1, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Community support
• developed by communities of developers and users
• better than traditional support
• provides high-quality support:
• directly contact the main developers of the component you are using.
• answer doesn’t depend what company you work for.
so, speeds up the resolution of problems when developing systems
but need to understand how the community works to properly use the community support possibilities

## Slide 24
What is crosstool-NG?
Set of scripts and makefiles for generating cross-developmenttoolchains
* originally called crosstool, and developed by Dan Kegel
¢ in 2007, Yann Morin used it to create the next generation of crosstool
the most convenient way to create a standalone cross toolchain from source.
because of crosstool-NG, building own toolchain is a valid and viable option.
+ https://bootlin.com/doc/training/lembedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_embedded_ systems
Outcomes: O1, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Set of scripts and makefiles for generating cross-development toolchains
• originally called crosstool, and developed by Dan Kegel
• in 2007, Yann Morin used it to create the next generation of crosstool
the most convenient way to create a standalone cross toolchain from source.
because of crosstool-NG, building own toolchain is a valid and viable option.

## Slide 25
Installing crosstool-NG
Simple Steps
1. Install a native toolchain and some build tools on the host machine.
2. Get the current release from the crosstool-NG. The class uses version 1.24.0
Do not run as root..
The prefix=${PWD} option means that the programs are installed under the
current directory. It avoids the need for root permissions, etc.
Outcomes: O2, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant

## Slide 26
Toolchain
Utilities
Community support
* developed by communities of developers and users
* better than traditional support
* provides high-quality support:
* directly contact the main developers of the component you are using.
* answer doesn’t depend what company you work for.
so, speeds up the resolution of problems when developing systems
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Outcomes: O1, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Community support
• developed by communities of developers and users
• better than traditional support
• provides high-quality support:
• directly contact the main developers of the component you are using.
• answer doesn’t depend what company you work for.
so, speeds up the resolution of problems when developing systems
but need to understand how the community works to properly use the community support possibilities

## Slide 27
Toolchain
Build Utilities
utilities
* crosstool-ng
Also, root filesystem build tools that construct a cross-compiling toolchain
* Buildroot
¢ PTXdist
* OpenEmbedded/ Yocto Project
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Outcomes: O1, O2, O3, O6
Build Path: cross-dev
AI Layer: L1-BuildAssistant
Notes: Crosstool-ng
• Rewrite of the older Crosstool, with a menuconfig-like configuration system
• Feature-full: supports uClibc, glibc and musl, hard and soft float, many architectures
• Actively maintained https://crosstool-ng.github.io/
Many root filesystem build systems also allow the construction of a cross-compiling toolchain
Buildroot Makefile-based. Can build glibc, uClibc and musl based toolchains, for a wide range
of architectures. Use make sdk to only generate a toolchain. https://buildroot.org
PTXdist Makefile-based, maintained mainly by Pengutronix.
It only supports uClibc and glibc (version 2021.03 status) https://www.ptxdist.org/
OpenEmbedded / Yocto Project
A featureful, but more complicated build system
http://www.openembedded.org/
https://www.yoctoproject.org/

## Slide 28
Toolchain
crosstool-ng
usage
* Installation either local or system-wide
* list and load Sample Configurations
* modify configuration
* build
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Linux_on_ embedded systems
Outcomes: O1, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: crosstool-ng
• Installation of Crosstool-NG can be done system-wide, or just locally in the source directory.
For local installation:
./configure --enable-local
make
make install
• Sample configurations for various architectures are available in samples, they can be listed using
./ct-ng list-samples
• To load a sample configuration
./ct-ng <sample-name>
• To adjust the configuration
./ct-ng menuconfig or ./ct-ng nconfig (according to your preference)
• To build the toolchain
./ct-ng build
-

## Slide 29
What is a Bootloader?
2nd element of embedded Linux
* starts the system and loads the OS
https://en.wikipedia.org/wiki/Bootloader
Outcomes: O1
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Bootloader
• 2nd element of embedded Linux
• starts the system and loads the OS

## Slide 30
What does a Bootloader do?
Two main jobs, as earlier
¢ starts the system and loads the OS
At startup, system is in a very minimal state -
* No DRAM controller yet, no RAM memory
* No NAND flash or MMC controller yet, no storage subsystem access
Typically, the only resources accessible are
* a single CPU core, and
* Some on-chip static memory and the boot ROM
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: What does a Bootloader do?
At startup, system is in a very minimal state –
• No DRAM controller yet, no RAM memory
• No NAND flash or MMC controller yet, no storage subsystem access
Typically, the only resources accessible are
• a single CPU core, and
• some on-chip static memory and the boot ROM
System bootup consists of several phases of code, each bringing more of the system into operation.
The final step of the bootloader is to load the kernel into RAM and create an execution environment for it.
The interaction between bootloader and kernel is architecture-specific, but, at high-level it has to pass a pointer
• to a structure containing configuration information on the hardware, and
• to pass a pointer to the kernel command line
The kernel command line is provided a text string that determines the boot settings at startup.
A secondary function of the command line interface is to provide a maintenance mode for updating the boot
configurations, loading new boot images into memory and, if needed run diagnostics.
It may need access/setup over a serial console for embedded systems.
Once kernel has started executing, the bootloader is no longer needed and the memory can all be reclaimed.

## Slide 31
The boot sequence
Introduction
In earlier times, it was a simpler model.
The bootloader
* was in non-volatile memory - usually NOR flash memory at the time
* was located at the reset vector of the processor
e.g. Oxffffffic - with a jump instruction to the start of the bootloader code.
* would then continue running in NOR flash
to initialize physical RAM — DRAM, and copy itself into there.
* then loaded the kernel from flash memory to transfer control to it.
Today, the boot sequence is a complex multi-stage procedure.
Outcomes: O1, O4
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: The boot sequence.
In earlier times, it was a simpler model.
• was in non-volatile memory - usually NOR flash memory at the time
• was located at the reset vector of the processor
e.g. 0xfffffffc - with a jump instruction to the start of the bootloader code.
• would then continue running in NOR flash
to initialize physical RAM – DRAM, and copy itself into there.
• then loaded the kernel from flash memory to transfer control to it.
Today, the boot sequence is a complex multi-stage procedure.
1st Step. Load from ROM.
2nd Step. Secondary Program Loader - SPL
3rd Step. Third Stage Program Loader - TPL

## Slide 32
The boot sequence
Phase 1 — Load from ROM
ROM
* needed due to absence of reliable external memory. known as ROM code.
* proprietary since it is loaded into SoC chip when chip is manufactured.
* no open source equivalent.
* can only use SRAM - Static RAM; since it does not need memory controller ..
meaning no DRAM yet, since it is device specific
https://en.wikipedia.org/wiki/Bootloader
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Load from ROM
• needed due to absence of reliable external memory. known as ROM code.
• proprietary since it is loaded into SoC chip when chip is manufactured.
• no open source equivalent.
• can only use SRAM – Static RAM; since it does not need memory controller ..
meaning no DRAM yet, since it is device specific
Most SoC designs have a small amount SRAM – from 4k to several 100k.
ROM Code
• loads a small chunk of code from pre-programmed locations into the SRAM
• As an example,
TI OMAP and Sitara chips try to load code
- from the first few pages of NAND flash memory, or
- from flash memory connected through a SPI – serial peripheral interface, or,
- from the first sectors of an MMC device - say an eMMC or SD card, or,
- from a file named MLO on the first partition of an MMC device.
If all these fail, then it tries reading as
- a byte stream from the Ethernet,
- USB, or
- UART – usually provided for loading code during manufacture rather than normal, routine operations.
• Most SoC have ROM that operates similarly.
oad from ROM
• at the end, jumps to the beginning of SPL.
In SoCs where the SRAM is not large enough to load a full bootloader such as U-Boot, there is an
intermediate loader stage called the Secondary Program Loader “SPL”.

## Slide 33
The boot sequence
Phase 2 — Secondary Program Loader
SPL - Secondary Program Loader sets up
* the memory controller and
* essential parts of system
in preparation for loading the TPL - Third Stage or Tertiary Program Loader.
SPL
* is limited by the size of the SRAM
* reads the instructions from the list of devices like the ROM code
using the pre-programmed offsets from the start of a flash device.
* prints version information and progress messages to the console.
* does not allow for any user interaction.
Build Path: bootloader
Notes: SPL - Secondary Program Loader sets up
• the memory controller and
• essential parts of system
in preparation for loading the TPL - Third Stage or Tertiary Program Loader.
SPL
• is limited by the size of the SRAM
• reads the instructions from the list of devices like the ROM code
using the pre-programmed offsets from the start of a flash device.
• prints version information and progress messages to the console.
• does not allow for any user interaction.
• may be open source e.g. TI x-loader and Atmel AT9IBootstrap, or
may be proprietary and provided by the manufacturer as a binary.
If the SPL has filesystem drivers built into it, then it can read from well-known filesystems
for files such as u-boot.img from a storage disk/partition.
Sequence and Steps
• From bootup, the execution sequence jumps to the SPL from the ROM code.
• SPL executes within the SRAM
• at the end of the 2nd phase - SPL loads TPL into the DRAM, and then
• the execution sequence jumps to the TPL.

## Slide 34
The boot sequence
Phase 3 - Third Stage Program Loader
TPL - Third Stage or Tertiary Program Loader
* loads kernel into DRAM
* sets up FDT and initramfs
in preparation for system bootup.
TPL usually
* is a full bootloader such as U-Boot
* permits a simple command line user interface that
* performs maintenance tasks such as
- loading new boot and kernel images into flash storage, and,
- loading and booting a kernel.
\https://en.wikipedia.org/wiki/Bootloader
Outcomes: O6
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: TPL – Third Stage or Tertiary Program Loader
• loads kernel into DRAM
• sets up FDT and initramfs
in preparation for system bootup.
--
TPL usually
• is a full bootloader such as U-Boot
• permits a simple command line user interface that
• performs maintenance tasks such as
- loading new boot and kernel images into flash storage, and,
- loading and booting a kernel.
--
Sequence and Steps
• From bootup, the execution sequence now jumps to the TPL from the SPL code.
• TPL executes within the DRAM
• at the end of the 3rd phase - TPL loads kernel into the DRAM, and then
an FDT and/or the initial RAM disk could be appended, if needed
• so that the kernel is in memory waiting to be started, and,
• the execution sequence jumps to the kernel.
Embedded bootloaders
• Usually disappear from memory once the kernel is up and running,
• Since they have no further part in the operations of the system.
TPL hands over the control of the boot process to the kernel.

## Slide 35
The boot sequence
Last Stage — Moving from bootloader to kernel
Bootloader - provides basic information to kernel, such as
* machine number to identify type of SoC
used on PowerPC and ARM systems without FDT
* details of hardware detected thus far
- size and location of Physical RAM, and
- CPU clock speed
¢ kernel command line
* location and size of device tree binary
* location and size of initial RAM disk called initramfs.
https://en.wikipedia.org/wiki/Bootloader
Outcomes: O6, O7
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Bootloader - provides basic information to kernel, such as
• machine number to identify type of SoC
used on PowerPC and ARM systems without FDT
• details of hardware detected thus far
- size and location of Physical RAM, and
- CPU clock speed
• kernel command line
is an ASCII text string that is used at bootup e.g. name of device that contains the root filesystem.
• location and size of device tree binary
• location and size of initial RAM disk called initramfs.
--
The root filesystem
• is commonly provided as a RAM disk, and, if so,
• is the responsibility of the bootloader to load the RAM disk image into memory
We’ll see creating the root filesystems later in this course.

## Slide 36
The boot sequence
Last Stage - Why Device Tree?
Why Device Tree -
The basic information provided to kernel, on earlier slide, is
* architecture dependent, and
* very limited
meaning that the bulk of it
* is discovered at runtime or
* hard-coded into kernel as platform data.
The widespread use of platform data, meant that
each board had to have the kernel configured/modified for it.
A better way was needed — and, that is the device tree.
https://en.wikipedia.org/wiki/Bootloader
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Why Device Tree?
--
The basic information provided to kernel, on earlier slide, is
• architecture dependent, and
• very limited
meaning that the bulk of it
• is discovered at runtime or
• hard-coded into kernel as platform data.
The widespread use of platform data, meant that each board had to have the kernel configured/modified for it.
A better way was needed - and, that is the device tree.
• The move away from A tags started in Feb 2013 – in Linux 3.8.
• Today almost all ARM systems use device tree to gather information about the specifics of the hardware
platform, meaning that a single kernel binary can be run on a wide range of these platforms.

## Slide 37
Device Tree
Introduction
Device Tree
* common on PowerPC and ARM
* flexible way of defining hardware components in a system.
* static data
* usually loaded by bootloader and passed to kernel, or
have device tree in kernel image for boot loaders that can not load them.
https://en.wikipedia.org/wiki/Bootloader
Outcomes: O1, O7
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Device Tree
• common on PowerPC and ARM
• flexible way of defining hardware components in a system.
• static data
• usually loaded by bootloader and passed to kernel, or
have device tree in kernel image for boot loaders that can not load them.
• derived from Sun Microsystems bootloader called Openboot – that was then
• formalized as Open Firmware spec IEEE standard IEEE1275-1994.
• first used in PowerPC-based Mac, and then
• used for the PowerPC Linux port
• subsequently adapted on a larger scale for the ARM Linux implementation, and
• on a much lesser extent by MIPS, MicroBlaze and other architectures.
See https://www.devicetree.org

## Slide 38
Device Tree
Basics
Device Tree
* hierarchical representation
* as a tree, of
+ hardware components in a system
* begins with root node - represented by /
* followed by subsequent nodes representing the hardware of the system.
Device Tree Source files
* large number found in arch/$ARCH/boot/dts, and a
* smaller number found in U-Boot Source code found in arch/$ARCH/dts
https://en.wikipedia.org/wiki/Bootloader
Outcomes: O1
Build Path: bootloader
AI Layer: L1-BuildAssistant
{
compatible = “ti,am33xx";
#address-cells = <1>;
#size-cells = <1>;
cpus {
#address-cells = <1>;
#size-cells = <0>;
cpu@0 {
compatible = "arm,cortex-a9";
device_type = “cpu”;
reg = <0>;
};
cpu@1 {
compatible = "arm,cortex-a9";
device_type = “cpu”;
reg = <1>;
};
};
memory@0x80000000 {
device_type = “memory”;
reg = <0x80000000 0x20000000> /* 512 MB */
};
Notes: Device Tree
• hierarchical representation
• as a tree, of
• hardware components in a system
• begins with root node - represented by /
• followed by subsequent nodes representing the hardware of the system.
Device Tree Source files
• large number found in arch/$ARCH/boot/dts, and a
• smaller number found in U-Boot Source code found in arch/$ARCH/dts.
Each node has a name and contains properties, in the form
name = value

## Slide 39
Device Tree
reg property
reg property
* consists of 0 or specify two values
real physical address and size/length of range
* represents range of units in a register space
* written as 32-bit integers called cells
in previous example, it refers to a single bank of memory starting at
0x80000000 for a length of 0x20000000
https://en.wikipedia.org/wiki/Bootloader
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: reg property
• consists of 0 or specify two values
real physical address and size/length of range
• represents range of units in a register space
• written as 32-bit integers called cells
in previous example, it refers to a single bank of memory starting at
0x80000000 for a length of 0x20000000
It becomes more complex when address or size cannot be represented as 32-bit quantities.
For e.g. on a device with 64-bit addressing - two cells are needed for each:
reg = <0x00000000 0x80000000 0x00000000 0x80000000>
Also, the number of cells required is held in #address-cells and #size-cells, higher up in the hierarchy.
So, to understand the reg property, there has to be a lookback for the #address-cells and #size-cells.
If there is none, then the default is 1 for each.
CPUs have addresses as well.
In a quad core device the cpus are addressed as 0,1,2,3 – one-dimensional array.
So, the #address-cells = <1> and #size-cells = <0> in the cpus node, while in the child node cpu@0 reg = <0>

## Slide 40
Device Tree
labels
* there could be multiple representations of hierarchy between components
e.g data connection, but they could be connected to
- an interrupt controller,
- a clock source, and/or
- a voltage regulator.
* to express these connections
- a label can be added to a node, and then,
- the label can be referenced from other nodes
* these labels are also known as phandles.
https://en.wikipedia.org/wiki/Bootloader
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: labels
• there could be multiple representations of hierarchy between components
e.g data connection, but they could be connected to
- an interrupt controller,
- a clock source, and/or
- a voltage regulator.
• to express these connections
- a label can be added to a node, and then,
- the label can be referenced from other nodes
• these labels are also known as phandles.

## Slide 41
Device Tree
include
* Since a lot of hardware is common between SoCs of same family and
boards using the same SoC
* common sections can go into include files, with the .dtsi extension
* layering provides flexibility and reduces the need for duplicated code.
https://en.wikipedia.org/wiki/Bootloader
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: include
• Since a lot of hardware is common between SoCs of same family and boards using the same SoC
• common sections can go into include files, with the .dtsi extension
• layering provides flexibility and reduces the need for duplicated code.

## Slide 42
Device Tree
compiling
* bootloader and kernel need a binary representation of device tree, so
* itneeds to be compiled with the device tree compiler dtc, and,
* it results in a .dtb file - device tree binary/blob
https://en.wikipedia.org/wiki/Bootloader
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: include
• bootloader and kernel need a binary representation of device tree, so
• it needs to be compiled with the device tree compiler dtc, and,
• it results in a .dtb file - device tree binary/blob
example
• copy of dtc in Linux source in scripts/dtc/dtc
• also, available as a package on many Linux distributions
• use it to compile a simple device tree – without #include
$ dtc simpledts-1.dts –o simpledts-1.dtb
DTC: dts->dts on file “simpledts-1.dts”
dtc
• does not give helpful error messages and
• makes no checks other than the basic syntax, so
• debugging typos can be a pain.
We’ll get into more on device trees in a later chapter.
Like the kernel,
• the bootloader can use a device tree to initialize an embedded SoC and peripherals.
• such a device tree is super important when loading the kernel from a mass storage device such as flash.

## Slide 43
U-Boot
embedded Linux supports many boot loaders
U-Boot
* supports a good number of processor architectures, and,
* supports many individual boards and devices
* has been around for a long time, and
* has a good community for support.
* started as an open-source bootloader for embedded PowerPC boards
* then ported to ARM boards and then to other architectures — MIPS, SH, etc
* hosted and maintained by Denx Software Engineering
* See https://www.denx.de/wiki/U-Boot
https://en.wikipedia.org/wiki/Bootloader
Outcomes: O2, O7
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: embedded Linux supports many boot loaders
U-Boot
• supports a good number of processor architectures, and,
• supports many individual boards and devices
• has been around for a long time, and
• has a good community for support.
• started as an open-source bootloader for embedded PowerPC boards
• then ported to ARM boards and then to other architectures – MIPS, SH, etc
• hosted and maintained by Denx Software Engineering
• See https://www.denx.de/wiki/U-Boot

## Slide 44
Building U-Boot
Get the source code, by
* either git clone,
* Or, a tarball
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Get the source code, by
• either git clone,
• Or, a tarball
There are more than 1000 configuration files for common development boards and devices in the configs/
directory.
• while the filenames are descriptive, there is
• more descriptive information in the per-board README files in the board/ directory
As an example, for the BeagleBone Black,
• there is a likely configuration file named configs/am335x_evm_defconfig, and the
• The text “the binary produced by this board supports … Beaglebone Black” in the board’s README file for
the am335x chip board/ti/am335x/README
• With this, building U-Boot for a Beaglebone Black is simple.
• Inform U-Boot of the prefix for the cross compiler using the CROSS_COMPILE make variable, and then
• Selecting the configuration file for make [board]_defconfig
• The results of the compilation are files named
• u-boot : an ELF object format file suitable for use with a debugger.
• u-boot.map : symbol table
• u-boot.bin : U-Boot in raw binary format suitable for running on the device
• u-boot.img : this is the u-boot.bin file with a U-Boot header added so that it can be uploaded to a running
copy of U-Boot.

## Slide 45
Installing U-Boot
Installing U-Boot for the first time requires external setup:
* Using a hardware debug interface such as JTAG, to load a copy of the U-
Boot directly into RAM and get it running. From there it can be copied to the
flash memory.
* Using a built-in boot ROM, that can be used to read boot code from external
sources such as SD cards, serial interfaces or USB mass storage. This is the
case with the an335x chip in the Beaglebone Black.
* Using an SD card reader to write the images to the card.
There are two types:
- external readers that plug into a USB port, or the
- internal SD reader found on many laptops
Outcomes: O7
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Installing U-Boot for the first time requires external setup:
• Using a hardware debug interface such as JTAG, to load a copy of the U-Boot directly into RAM and get it
running. From there it can be copied to the flash memory.
• Using a built-in boot ROM, that can be used to read boot code from external sources such as SD cards,
serial interfaces or USB mass storage. This is the case with the an335x chip in the Beaglebone Black.
• Using an SD card reader to write the images to the card.
There are two types:
- external readers that plug into a USB port, or the
- internal SD reader found on many laptops
• The lsblk command is a useful tool for finding out which device has been allocated.

## Slide 46
Using U-Boot
Some of the common tasks used with U-Boot include:
* Creating and modifying variables from the U-Boot command line.
* Formatting the boot image
* Loading images
* Booting Linux, and
* Automating the boot with U-Boot scripts
Build Path: bootloader
Notes: Some of the common tasks used with U-Boot include:
• Creating and modifying variables from the U-Boot command line.
Using setenv to create/modify and printenv command to print
• Formatting the boot image
since U-Boot does not have a filesystem, it tags blocks of information with a 64byte header to track the
contents; this is done using the mkimage command line tool that comes with the u-boot-tools package on
Ubuntu, or created by running make tools from within the U-Boot source tree as tools/mkimage
• Loading images
the MMC driver handles the loading of the images from removable storage such as SD card or a network.
• Booting Linux, and
the bootm command starts the Linux kernel image running
• Automating the boot with U-Boot scripts
U-Boot stores the sequence of commands n environment variables.
If the special variable called bootcmd contains a script it is run at power-up.

## Slide 47
Porting U-Boot
to a new board
Steps include:
Build Path: bootloader

## Slide 48
Summary Notes
* Toolchains.
¢ Bootloaders.
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant

## Slide 49
Quiz
Canvas
* 10 Questions
° 45 Mins
* 6 Attempts
¢ Highest Retained

## Slide 50
Assignment
1. Setup toolchain for your target
use example provided
in the zip file.
2. Compile hello.c or the hello.cpp — for the target.
3. Submit output of xcc.sh from the 1a directory.
Outcomes: O2, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Assignment
1.Setup toolchain
use example 1 for rpi4,
then, for your target
2. Run “time make” – using
either
example 1a for rpi4,
example 1b for rpi3B+, or
example 1c for rpi3B
from the zip file.
3.Compile hello.c and the hello.cpp – for the target.
show the output of the file command
a) file hello-c (say using *bcc -o hello-c hello.c)
b) file hello-cpp (say using *g++ -o hello-cpp hello.cpp)

## Slide 51
Summary
In This Chapter
* Overview of Embedded Linux Systems
* Introduction to Embedded Linux Systems
* Examples of Embedded Linux Systems
¢ Hardware for Embedded Linux Systems
* System Architecture of Embedded Linux Systems
¢ Environment for Embedded Linux Systems Development
* NoAssignment
* Quiz
Outcomes: O1
Notes: CHAPTER OVERVIEW
In This Chapter, We saw
1. Overview of Embedded Linux Systems
2. Introduction to Embedded Linux Systems
3. Examples of Embedded Linux Systems
4. Hardware for Embedded Linux Systems
5. System Architecture of Embedded Linux Systems
6. Environment for Embedded Linux Systems Development
7. No Assignment
8. Quiz