## Slide 1
Buildroot and Yocto Project
AI Layer: L1-BuildAssistant
Notes: Selecting a Build System https://en.wikipedia.org/wiki/Toolchain
• The elements of embedded Linux are getting discussed step by step,
• how to build a toolchain, and
• a bootloader, and,
• While in later chapters, we will discuss
• a kernel, and
• a root filesystem
• As they are combined into a basic embedded Linux system.
Sure - There are a lot of steps!
• Fortunately, the process can be simplified by automating it as much as possible.
We will look at how embedded build systems help and look Buildroot and the Yocto Project.
• Both are complex and flexible tools, and it would require an entire book to describe how they work in full.
• In this chapter, we get to see the general ideas behind build systems.
A simple device image is built to get an overall feel of the system, and then get to make some changes
Topics include
• Comparing build systems
• Distributing binaries
• Introducing Buildroot
• Introducing the Yocto Project
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 2
Chapter Objectives
In This Chapter
¢ Comparing Build Systems
¢ Distributing Binaries
* Buildroot
* Yocto Project
* Assignment
° Quiz
AI Layer: L1-BuildAssistant
Notes: CHAPTER OVERVIEW
In This Chapter, We Will Discuss
1. Comparing Build Systems
What are Build Systems?
2. Distributing Binaries
types.
3. Buildroot
Overview and Getting Started with Buildroot
4. Yocto Project
Overview and Getting Started with Yocto Project
5. Assignment
6. Quiz
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 3
Comparing Build systems
* RYO process — Roll Your Own
painful
waste of time, with
likelihood of an unmaintainable system
* Only override/benefit is, it it is
truly innovative, or has a
customized approach to taking up bare minimum memory.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
* https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: • Roll Your Own - RYO process
painful
waste of time, with
likelihood of an unmaintainable system
• Only override/benefit is, it it is
truly innovative, or has a
customized approach to taking up bare minimum memory.
The idea of a build system is to automate all the steps, where
a build system should be able to build, from upstream source code, some or all of the following:
• A toolchain
• A bootloader
• A kernel
• A root filesystem
Building from upstream source code is important for a number of reasons.
• It means that there is the peace of mind to rebuild at any time, without external dependencies.
• It also means that the source code is available for debugging, and also that to meet the license
requirements to distribute the code to users where necessary.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 4
Binaries
distros
«RPM
* stands for Redhat Package Manager
* and, is used in Red Hat, SUSE, Fedora, and other distributions based on them.
* DEB
* stands for Debian package manager
* and, is used in Debian and Debian-derived distributions, including Ubuntu and Mint
* also, there is a lightweight format specific to embedded devices known as the Itsy
package format or IPK, which is based on DEB.
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: • RPM
• stands for Redhat Package Manager
• and, is used in Red Hat, SUSE, Fedora, and other distributions based on them.
• DEB
• stands for Debian package manager
• and, is used in Debian and Debian-derived distributions, including Ubuntu and Mint
• also, there is a lightweight format specific to embedded devices known as the Itsy package format or
IPK, which is based on DEB.
The ability to include a package manager on the device is one of the big differentiators between build systems.
a package manager on the target device provides an easy path to deploy/update new/existing packages.

## Slide 5
Buildroot
Introduction
current versions of Buildroot, build
* a toolchain,
* a bootloader,
¢ akernel, and
* aroot filesystem.
Outcomes: O1, O3, O6
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: current versions of Buildroot, build
1. a toolchain,
2. a bootloader,
3. a kernel, and
4. a root filesystem.
It uses GNU Make as the principal build tool.
• good online documentation at https://buildroot.org/docs.html
• The Buildroot user manual at https://buildroot.org/downloads/manual/manual.html.

## Slide 6
Buildroot
Background
Buildroot
* one of the first build systems,
* began as part of uClinux/uClibc projects for generating a small root fs for testing,
* became a separate project in late 2001 and continued to evolve through to 2006
* since 2009, it has developed rapidly, adding support for glibc-based toolchains and
a greatly increased number of packages and target boards.
Outcomes: O2, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Buildroot
1. one of the first build systems,
2. began as part of uClinux/uClibc projects for generating a small root fs for testing,
3. became a separate project in late 2001 and continued to evolve through to 2006
4. since 2009, it has developed rapidly, adding support for glibc-based toolchains and a greatly increased
number of packages and target boards.
OpenWrt http://wiki.openwrt.org forked from Buildroot around 2004.
• The primary focus of OpenWrt is to produce software for wireless routers, and so the package mix is
oriented toward the networking infrastructure.
• It also has a runtime package manager using the IPK format so that a device can be updated or upgraded
without a complete reflash of the image.
• However, today, Buildroot and OpenWrt have diverged to such an extent that they are now almost
completely different build systems. Packages built with one are not compatible with the other.

## Slide 7
Buildroot
Stable releases and long-term support
Buildroot
stable releases four times a year,
in February, May, August, and November.,
* marked by Git tags of the form
<year>.02, <year>.05, <year>.08, and <year>.11
Build Path: RT
AI Layer: L1-BuildAssistant
Notes: Buildroot
1.stable releases four times a year,
in February, May, August, and November.,
2.marked by Git tags of the form
<year>.02, <year>.05, <year>.08, and <year>.11
Periodically, a release is marked for long-term support (LTS), which means that there will be point releases to
fix security and other important bugs for 12 months after the initial release.
The 2017.02 release was the first to receive the LTS label.

## Slide 8
Buildroot
Installing
Buildroot
install Buildroot
* either by cloning the repository
* or downloading a tar archive.
Outcomes: O4
AI Layer: L1-BuildAssistant
Notes: Buildroot
install Buildroot
1. either by cloning the repository
2. or, downloading an archive.
As an example of obtaining version 2021.05.1 - latest stable version at the time of writing:
$ git clone git://git.buildroot.net/buildroot –b 2021.05.1
$ cd buildroot
The equivalent TAR archive is available at https://buildroot.org/downloads .
Install all packages listed in System requirements section at
https://buildroot.org/downloads/manual/manual.html

## Slide 9
Buildroot
Configure
Buildroot
* uses the kernel Kconfig/Kbuild mechanism
* configure from scratch directly using make menuconfig (xconfig or gconfig), or
* choose from one of the100+ configurations of dev boards and the QEMU emulator
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Buildroot
1. uses the kernel Kconfig/Kbuild mechanism
2. configure from scratch directly using make menuconfig (xconfig or gconfig), or
3. choose from one of the100+ configurations of dev boards and the QEMU emulator.
They are stored in the configs/ directory.
Use make listdefconfigs to list all the default configurations.
To build a default configuration to run on the Arm QEMU emulator:
$ cd buildroot
$ make qemu_arm_versatile_defconfig
$ make
Note.
make in Buildroot does not use the “-j” option to control the parallelism of jobs to run.
Instead, Buildroot determines and makes use of the CPUs by itself.
To limit the number of jobs run make menuconfig and look under Build options.
The build will take several minutes - up to an hour or more, depending on the host system and internet
connectivity speed.

## Slide 10
Buildroot
Configure .. 2
Buildroot
* as earlier, build could take up to an hour
* download of about 200 MB and consumes about 4 GB of disk.
* when complete, two new directories are seen
© dil: contains archives of the upstream projects that Buildroot has built.
* output/: contains all intermediate and final compiled resources.
Outcomes: O4
AI Layer: L1-BuildAssistant
Notes: Buildroot
1. as earlier, build could take up to an hour
2. download of about 200 MB and consumes about 4 GB of disk.
3. when complete, two new directories are seen
• dl/: contains archives of the upstream projects that Buildroot has built.
• output/: contains all intermediate and final compiled resources.
further. Output contains the following hierarchy:
▪ build/: the build directory for each component.
▪ host/: contains tools required by Buildroot to run on host, including executables of
toolchain in output/host/usr/bin.
▪ images/: most important of all since it contains the results of the build.
Depending on selection when configuring, there will be a bootloader, a kernel,
and one or more root filesystem images.
▪ staging/ a symbolic link to sysroot of the toolchain. In that sense, staging as name of the
link is confusing since it does not point to a staging area.
▪ target/: staging area for the root directory.
It cannot be use it as a root filesystem directly as it stands because file ownership
and permissions are not set correctly. Buildroot uses a device table, as earlier, to
set ownership and permissions when fs image is created in the image/ directory.

## Slide 11
Buildroot
Running on Raspberry Pi
On a Raspberry Pi
steps for configuring and building a bootable image for the Raspberry Pi
$ cd buildroot
$ make clean
$ make raspberrypi4_64_defconfig
$ make
Outcomes: O7
AI Layer: L1-BuildAssistant
Notes: Buildroot
steps for configuring and building a bootable image for the Raspberry Pi
$ cd buildroot
$ make clean
$ make raspberrypi4_64_defconfig
$ make
When the build finishes, the image is written to a file named output/images/sdcard.img.
The post-image.sh script and the genimage-raspberrypi4-64.cfg configuration file used to write the
image file are both located in the board/raspberrypi/ directory.
Next, write the sdcard.img onto a microSD card and boot it on the Raspberry Pi 4.
Confirm that the Pi 4 booted successfully by plugging it in and observing that the network activity lights blink.

## Slide 12
Buildroot
Running for the BBB
For BBB
$ cd buildroot
$ make clean
$ make beaglebone_defconfig
$ make
AI Layer: L1-BuildAssistant
Notes: BBB
1. creating a directory to store changes for the nova board:
$ mkdir -p board/EL/me
2. clean the artifacts from any prior build
$ make clean
3. select the configuration for the BeagleBone
$ make beaglebone_defconfig

## Slide 13
Buildroot
Running for the QEMU
On the QEMU
Using sample configurations in the board/ directory, which contains custom
configuration files and information about installing the results on the target
e.g. for ARM use board/qemu/arm-versatile/readme.txt,
Outcomes: O2, O7
AI Layer: L1-BuildAssistant
Notes: On the QEMU
Using sample configurations in the board/ directory, which contains custom configuration files and information
about installing the results on the target
e.g. for ARM use board/qemu/arm-versatile/readme.txt,
If qemu-system-arm is already installed,
$ qemu-system-arm -M versatilepb -m 256 \
-kernel output/images/zImage \
-dtb output/images/versatile-pb.dtb \
-drive file=output/images/rootfs.ext2,if=scsi,format=raw \
-append "root=/dev/sda console=ttyAMA0,115200" \
-serial stdio -net nic,model=rtl8139 -net user
When QEMU boots up, kernel boot messages appear in the same Terminal window below the QEMU cmd,
followed by a login prompt.
• Log in as root, with no password.
• QEMU also launches a black window, in addition to the one with the kernel boot messages.
It is there to display the graphics frame buffer of the target.
In this case, the target never writes to the framebuffer, which is why it appears black.
To close QEMU, either press Ctrl + Alt + 2 to get to the QEMU console and then type quit, or just close the
framebuffer window.

## Slide 14
Buildroot
Running for a custom BSP
to create a Board Support Package (BSP)
Using versions of U-Boot and Linux from following chapters,
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: custom BSP
Using sample configurations in the board/ directory, which contains custom configuration files and information
about installing the results on the target
e.g. for ARM use board/qemu/arm-versatile/readme.txt,
The recommended places to store changes are as follows:
board/<organization>/<device>: has patches, binary blobs, extra build steps, conf files for Linux, U-Boot, etc.
configs/<device>_defconfig: contains the default configuration for the board.
package/<organization>/<package_name>: contains any additional packages for this board.
1. creating a directory to store changes for the nova board:
$ mkdir -p board/EL/me
2. clean the artifacts from any prior build
$ make clean
3. select the configuration for the BeagleBone, say for e.g.
$ make beaglebone_defconfig

## Slide 15
Buildroot
License Compliance
* Buildroot is based on open source software,
as are the packages it compiles.
¢ At some point during the project, check the licenses
by running the following:
$ make legal-info
AI Layer: L1-BuildAssistant
Notes: Buildroot.
1. Buildroot is based on open source software, as are the packages it compiles.
2. At some point during the project, check the licenses by running the following:
$ make legal-info
The information is gathered into output/legal-info/.
There are summaries of the licenses used to compile the host tools in host-manifest.csv and, on the target, in
manifest.csv. There is more information in the README file and in The Buildroot user manual.

## Slide 16
Yocto Project
Introduction
current versions of Buildroot, build
* a toolchain, a bootloader, a kernel, and a root filesystem.
And, Yocto Project is a more complex beast than Buildroot.
* it builds toolchains, bootloaders, kernels, and root filesystems as above,
* and it can generate an entire Linux distribution with binary packages that
can be installed at runtime.
Outcomes: O1, O3, O6
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: current versions of Buildroot, build
1. a toolchain, a bootloader, a kernel, and a root filesystem.
And, Yocto Project is a more complex beast than Buildroot.
1. it builds toolchains, bootloaders, kernels, and root filesystems as above,
2. and, it can generate an entire Linux distribution with binary packages that can be installed at runtime.
The build process is
• structured around groups of recipes, similar to Buildroot packages
• but written using a combination of Python and shell script.
The Yocto Project includes a task scheduler called BitBake that produces whatever is configured, from the
recipes.
There is plenty of online documentation at https://www.yoctoproject.org.

## Slide 17
Yocto Project
Background
need to understand background first, for making sense of the Yocto Project.
* it began as part of OpenEmbedded project in 2003
¢ Around 2005, a fork that was called Poky — rhymes with hockey, was created.
It had a more conservative choice of packages for releases that were stable over time
* In 2008 Intel bought over, and
* In 2010 transferred over Poky Linux to the Linux Foundation when they formed the
Yocto Project.
* Since 2010, the common components of OpenEmbedded and Poky were combined
into a separate project known as OpenEmbedded Core, or OECore.
Outcomes: O4
Build Path: RT
Notes: background of the Yocto Project.
1. it began as part of OpenEmbedded project
OpenEmbedded grew out of many projects to port Linux to handheld computers, and was the build system
for handheld computers e.g.Sharp Zaurus and Compaq iPaq - from about 2003
Then, other developers began to use/develop it for devices running embedded Linux, and continues to be
developed today.
The OpenEmbedded project created a set of binary packages using the compact IPK format, which could
then be combined in various ways to create a target system and be installed on the target at runtime.
It did this by creating recipes for each package and using BitBake as the task scheduler. It was, and is very
flexible. By supplying proper metadata, it can create an entire Linux distribution to any custom specification.
One that is fairly well-known is the Ångström Distribution, but there are many others as well.
2. Around 2005, a fork that was called Poky – rhymes with hockey, was created.
in 2005, Richard Purdie at OpenedHand, created a fork of OpenEmbedded, which had a more conservative
choice of packages, and created releases that were stable over a period of time.
He named it Poky - after a Japanese snack - rhyme with hockey.
Although Poky was a fork, OpenEmbedded and Poky continued to run alongside each other, sharing
updates and keeping the architectures more or less in step

## Slide 18
Yocto Project
Background .. 2
Yocto Project combines several components:
* OE-Core: core metadata, that is shared with OpenEmbedded.
¢ BitBake: task scheduler, that is shared with OpenEmbedded and others.
* Poky: the reference distribution.
¢ Documentation: This is the user's manuals and developer's guides for each
component.
* Toaster: This is a web-based interface to BitBake and its metadata.
Notes: Yocto Project combines several components:
1. OE-Core: This is the core metadata, and is shared with OpenEmbedded.
2. BitBake: This is the task scheduler, and is shared with OpenEmbedded and other projects.
3. Poky: This is the reference distribution.
4. Documentation: This is the user's manuals and developer's guides for each component.
5. Toaster: This is a web-based interface to BitBake and its metadata.
The Yocto Project provides a stable base, which can be used as-is or can be extended using meta layers.
Many SoC vendors provide BSPs for their devices
• in this way. Meta layers can also be used to create extended or just different build systems.
• Some are open source, such as the Ångström Distribution, while others are commercial, such as
MontaVista Carrier Grade Edition, Mentor Embedded Linux, and Wind River Linux.
• TheYocto Project has a branding and compatibility testing scheme to ensure that there is interoperability
between components; and therefore, there are the statements such as "Yocto Project compatible" on
various web pages.
• think of the Yocto Project as the foundation of a whole sector of embedded Linux, as well as being a
complete build system on its own.

## Slide 19
Yocto Project
So, what is ina name? Why call it Yocto?
Yocto is 10 -4
* to indicate that it could build very small Linux systems
Outcomes: O1
AI Layer: L1-BuildAssistant
Notes: Yocto is 10 -24
• as compared to a micro that is 10 -6 or, an Ångström that is 10 -10
• also, distinguish from Ångström Distribution, which is based on OpenEmbedded.
As above, an Ångström that is 10 -10 – huge as compared to a yocto!
1. to indicate that it could build very small Linux systems
2. although, to be fair, so can other build systems

## Slide 20
Yocto Project
Stable releases and long-term support
Yocto Project
stable releases
* supported for 12 months after the release
* two times a year,
in April, and October.
long-term support
* supported supported for 24 months after the release
* every two years
Build Path: RT
Notes: Yocto Project
1.stable releases two times a year,
in April, and October.
principally known by their code names
• but it is useful to know the version numbers of the Yocto Project and Poky as well
Here is a list of some of the six recent releases:
Code name Release date Yocto version Poky version
• Gatesgarth October 2020 3.2 24
• Dunfell April 2020 3.1 23
• Zeus October 2019 3.0 22
• Warrior April 2019 2.7 21
• Thud November 2018 2.6 20
• Sumo April 2018 2.5 19
The stable releases are supported with security and critical bug fixes for the current release cycle and the next
cycle. In other words, each version is supported for 12 months after the release.
In addition, Dunfell is the first LTS release of Yocto.
The LTS designation means that Dunfell will receive defect fixes and updates for an extended period of 2 years
Consequently, the plan going forward is to choose an LTS release of the Yocto Project every 2 years.

## Slide 21
Yocto Project
Installing
install Yocto Project
* by cloning the repository
AI Layer: L1-BuildAssistant
Notes: install Yocto Project
• choosing the code name as the branch
• and, clone the repository
.
Installing the Yocto Project
To install the Yocto Project, choosing the code name as the branch, say dunfell, and, clone the repository.
$ git clone -b dunfell git://git.yoctoproject.org/poky.git
• It is good practice to run git pull periodically to grab the latest bug fixes and security patches from the
remote branch.
• Read the Compatible Linux Distribution and Build Host Packages sections of the Yocto Project Quick Build
guide - https://www.yoctoproject.org/docs/current/brief-yoctoprojectqs/briefyoctoprojectqs.html.
• Make sure that the essential packages for the Linux distribution are installed on the host computer.

## Slide 22
Yocto Project
Configure
Yocto Project
* uses the kernel Kconfig/Kbuild mechanism
* configure from scratch directly using make menuconfig (xconfig or gconfig), or
* choose from one of the100+ configurations of dev boards and the QEMU emulator
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Configure Yocto Project
1. Begin by sourcing a script to set up the environment:
$ source poky/oe-init-build-env
This creates a working directory for you named build/ and makes it the current directory.
All of the configuration, as well as any intermediate and target image files, are put in this directory.
You must source this script each time you want to work on this project.
Alternatively, to choose a different working directory by adding it as a parameter to
oe-init-build-env; for example:
$ source poky/oe-init-build-env build-rpi4
$ source poky/oe-init-build-env build-rpi3B+
$ source poky/oe-init-build-env build-rpi3B
$ source poky/oe-init-build-env build-bbb
$ source poky/oe-init-build-env build-qemuarm
This will put you into the build-xxx/ directory.
This way, there can be several build directories, each for a different project:
choose which one you want to work with through the parameter that's passed to oe-init-buildenv.

## Slide 23
Yocto Project
Configure .. 2
Yocto Project
* as earlier, build could take up to an hour
* download of about 200 MB and consumes about 4 GB of disk.
* when complete, two new directories are seen
© dil: contains archives of the upstream projects that Buildroot has built.
* output/: contains all intermediate and final compiled resources.
Outcomes: O4
AI Layer: L1-BuildAssistant
Notes: Buildroot
Initially, the build directory contains only one subdirectory named conf/,
which contains the following configuration files for this project:
local.conf: This contains a specification of the device you are going to build and the build environment.
bblayers.conf: This contains the paths of the meta layers you are going to use.
For now, just need to set the MACHINE variable in conf/local.conf to qemuarm by removing the comment
character (#) at the start of this line:
e.g.
MACHINE ?= "qemuarm"

## Slide 24
Yocto Project
Build
Building Yocto Project
* to perform the build, run BitBake
+ indicating which root filesystem image to create
Outcomes: O6
Build Path: rootfs
AI Layer: L1-BuildAssistant
Notes: Building Yocto Project
1. to perform the build, run BitBake
2. Indicating which root filesystem image to create
Some common images are as follows:
core-image-minimal: a small console-based system useful for tests and as the basis for custom images.
core-image-minimal-initramfs: This is similar to core-image-minimal but built as a ramdisk.
core-image-x11: This is a basic image with support for graphics through an X11 server and the xterminal
Terminal app.
core-image-full-cmdline: This console-based system offers a standard CLI experience and full support for the
target hardware.
By giving BitBake the final target, it will work backward and build all the dependencies first, beginning with the
toolchain.
For now create a minimal image to see how it works:
$ bitbake core-image-minimal

## Slide 25
Yocto Project
Build .. 2
Building Yocto Project
* to perform the build, run BitBake
+ indicating which root filesystem image to create
Outcomes: O6
Build Path: rootfs
AI Layer: L1-BuildAssistant
Notes: Building Yocto Project .. 2
1. build will take several hours, even with several CPU cores and lots of RAM
2. downloads about 10 GB of source code, and, consumes about 40 GiB of disk space.
When it is complete, there will be several new directories in the build directory, including
• downloads/, which contains all the source downloaded for the build, and
• tmp/, which contains most of the build artifacts.
further, in tmp/:
• work/: This contains the build directory and the staging area for the root filesystem.
• deploy/: This contains the final binaries to be deployed on the target:
• deploy/images/[machine name]/: Contains the bootloader, the kernel and the root filesystem images
ready to be run on the target.
• deploy/rpm/: This contains the RPM packages that make up the images.
• deploy/licenses/: This contains the license files that are extracted from each package.
When the build is done, the finished image can be used to boot.

## Slide 26
Yocto Project
Running the QEMU target
On the QEMU
* source oe-initbuild-env, then run
* rungemu gemuarm
Outcomes: O2, O7
AI Layer: L1-BuildAssistant
Notes: On the QEMU
When a QEMU target is built using the Yocto Project, an internal version of QEMU is generated.
It removes the need to install the QEMU package for the distribution, and avoids version dependencies.
A wrapper script named runqemu is used to run this version of QEMU.
Therefore,
1. source oe-initbuild-env, then run
2. runqemu qemuarm
The QEMU has been configured with a graphic console so that the login prompt appears in a black
framebuffer.
Log in as root, without a password.
• To close QEMU, close the framebuffer window.
• To launch QEMU without the graphic window, add nographic to the command line:
$ runqemu qemuarm nographic
• In this case, close QEMU using the key sequence Ctrl + A and then x.
The runqemu script has many other options.
Type runqemu help for more information.

## Slide 27
Yocto Project
Layers
* metadata for the Yocto Project is structured into layers
* each layer has a name beginning with meta
* core layers of the Yocto Project are as follows:
* meta: the OpenEmbedded core and contains some changes for Poky.
¢ meta-poky: metadata specific to the Poky distribution.
* meta-yocto-bsp: contains the BSPs for machines that Yocto Project supports.
Notes: Layers
1. metadata for the Yocto Project is structured into layers
2. each layer has a name beginning with meta
• core layers of the Yocto Project are as follows:
• meta: metadata for OpenEmbedded core and contains some changes for Poky.
• meta-poky: metadata specific to the Poky distribution.
• meta-yocto-bsp: contains the BSPs for machines that Yocto Project supports.
• BitBake searches for recipes is stored in <build directory>/conf/bblayers.conf and, by default, includes all
three layers mentioned in the preceding list.
• Because of structuring recipes and other configuration data, it is very easy to extend and add new layers.
• Additional layers are available from SoC manf., Yocto Project itself, and several independent contributors.
• A useful list of layers is at http://layers.openembedded.org/layerindex/
• some examples:
• meta-qt5: Qt 5 libraries and utilities
• meta-intel: BSPs for Intel CPUs and SoCs
• meta-raspberrypi: BSPs for the Raspberry Pi boards
• meta-ti: BSPs for TI Arm-based SoCs
• Adding a layer is simply copying the meta directory to a suitable location and adding it to bblayers.conf.
• Make sure that you read the REAMDE file withiin each layer to see what dependencies it has on other
layers, as well as which versions of the Yocto Project it is compatible with.

## Slide 28
Yocto Project
Bitbake and recipes
A look at recipes next and show
* how to create a customized image and
* how to create a package
BitBake processes metadata of several different types, including the following:
Recipes: Files ending in .bb. contain information about building a unit of software
Append: Files ending in .bbappend. override or extend some details of a recipe.
Include: Files ending in .inc. information that is common to several recipes
Classes: Files ending in .bbclass. common build information
Configuration: Files ending in .conf. define various configuration variables
AI Layer: L1-BuildAssistant
Notes: Bitbake and recipes
A look at recipes next and show
1. how to create a customized image and
2. how to create a package
BitBake processes metadata of several different types, including the following:
• Recipes: Files ending in .bb. contain information about building a unit of software
including how to get a copy of the source code, the dependencies of other components, and
how to build and install it.
• Append: Files ending in .bbappend. override or extend some details of a recipe.
A bbappend file appends instructions to the end of a recipe (.bb) file of the same root name.
• Include: Files ending in .inc. information that is common to several recipes.
The files may be included using the include or require keywords. The difference is that require
produces an error if the file does not exist, whereas include does not.
• Classes: Files ending in .bbclass. common build information
for example, how to build a kernel or how to build an autotools project. The classes are inherited
and extended in recipes and other classes using the inherit keyword.
The classes/base.bbclass class is implicitly inherited in every recipe.
• Configuration: Files ending in .conf. define various configuration variables
They define various configuration variables that govern the project's build process.

## Slide 29
Yocto Project
Customizing images via local.conf
to add a package to an image during development or tweak it in other ways, use
IMAGE_INSTALL_append =" strace helloworld"
Further, changes are possible via EXTRA_IMAGE_FEATURES
Build Path: debug
AI Layer: L1-BuildAssistant
Notes: Customizing images via local.conf
to add a package to an image during development or tweak it in other ways, use
IMAGE_INSTALL_append = " strace helloworld"
Further, changes are possible via EXTRA_IMAGE_FEATURES
As a short list to provide an idea of the features that can be enabled:
• dbg-pkgs: installs debug symbol packages for all the packages installed in the image.
• debug-tweaks: allows root logins without passwords and other changes that make development easier.
• package-management: installs package management tools and preserves package manager database.
• read-only-rootfs: This makes the root filesystem read-only..
• x11: installs the X server.
• x11-base: installs the X server with a minimal environment.
• x11-sato: installs the OpenedHand Sato environment.
many more features that can be added in this way.
• look at the Image Features section of the Yocto Project Reference Manual at
https://www.yoctoproject.org/docs/latest/ref-manual/ref-manual.html ,
• and also see meta/classes/core-image.bbclass.

## Slide 30
Yocto Project
Writing an image recipe
local.conf: problem with making changes to local.conf is that it is local
image recipe: to create an image that is to be shared with other developers or to be
loaded onto a production system, then put the changes into an image recipe.
Notes: Writing an image recipe – Deep dive
local.conf: problem with making changes to local.conf is that it is local
image recipe: to create an image that is to be shared with other developers or to be loaded onto a production
system, then put the changes into an image recipe.
• An image recipe contains instructions about how to create the image files for a target, including the
bootloader, the kernel, and the root filesystem images.
• By convention, image recipes are put into a directory named images, so to get a list of all the images that
are available - use this command:
$ ls meta*/recipes*/images/*.bb
e.g. the recipe for core-image-minimal is in meta/recipes-core/images/core-image-minimal.bb
• A simple approach is to take existing image recipe and modify it with statements similar to that in local.conf.
e.g. image that is the same as coreimage-minimal but includes helloworld program and the strace
it is a two-line recipe file, which includes (using the require keyword) the base image and add the packages
put the image in a directory named images, so add the novaimage-bb recipe with the following content to
meta-nova/recipeslocal/images:
require recipes-core/images/core-image-minimal.bb
IMAGE_INSTALL += “ helloworld strace“
• Now, remove the IMAGE_INSTALL_append line from the local.conf and build it using this:
$ bitbake nova-image

## Slide 31
Yocto Project
Creating an SDK
SDK
* create a standalone toolchain that other developers can install, without a full
installation of the Yocto Project.
* the toolchain should include development libraries and header files for all the
libraries installed on the target
* easy - use the populate_sdk task for any image
$ bitbake -c populate_sdk nova-image
Outcomes: O2, O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Creating an SDK – Deep dive
1. create a standalone toolchain that other developers can install, without a full installation of the Yocto Project.
2. the toolchain should include development libraries and header files for all the libraries installed on the target
3. easy - use the populate_sdk task for any image
$ bitbake -c populate_sdk nova-image
4. result is a self-installing shell script in tmp/deploy/sdk:
poky-<c_library>-<host_machine>-<target_image> <target_machine>-toolchain-<version>.sh
e.g. for the SDK built with the nova-image recipe, it is this:
poky-glibc-x86_64-nova-image-cortexa8hf-neonbeaglebone-yocto-toolchain-3.1.5.sh
5. for a basic toolchain with just C and C++ cross compilers, the C library, and header files, run this instead:
$ bitbake meta-toolchain
6. To install the SDK, just run the shell script.
The default install directory is /opt/poky, but the install script allows changing this
7. To make use of the toolchain, first, source the environment and set up the script:
$ source /opt/poky/3.1.5/environment-setupcortexa8hf-neon-poky-linux-gnueabi
8. Note: The environment-setup-* script for the SDK is not compatible with the oe-init-build-env script.

## Slide 32
Yocto Project
License
License
* The Yocto Project insists that each package has a license.
* Acopy of the license is placed in
tmp/deploy/licenses/[package name]
for each package as it is built.
Outcomes: O4
Notes: License
1. The Yocto Project insists that each package has a license.
2. A copy of the license is placed in
tmp/deploy/licenses/[package name]
for each package as it is built.

## Slide 33
Summary Notes
¢ Buildroot.
* Yocto Project.
Further reading
¢ The Buildroot user manual, Buildroot Association:
http://buildroot.org/downloads/manual/manual.html
* Yocto Project documentation, Yocto Project:
https://www.yoctoproject.org/documentation
¢ Embedded Linux Development Using the Yocto Project Cookbook, by
Alex Gonzalez
Outcomes: O4
AI Layer: L1-BuildAssistant
Notes: 1. Buildroot.
Buildroot is simple and quick, making it a good choice for fairly simple traditional embedded Linux..
2. Yocto Project.
The Yocto Project is more complex and flexible.
Even though there is good support throughout the community and industry for the Yocto Project, the tool still
has a very steep learning curve. It can take several months to become proficient with Yocto, and even then,
it will sometimes do things that aren't expected.
3. Both the Yocto Project and Buildroot provide point releases for about 1 year after the initial release, and the
Yocto Project now offers long term support for at least 2 years.
4. In either case, you will find yourself having to maintain your release yourself; otherwise, you will be paying
for commercial support. The third possibility, ignoring the problem, should not be considered as an option!
Further reading
The Buildroot user manual, Buildroot Association:
http://buildroot.org/downloads/manual/manual.html
Yocto Project documentation, Yocto Project:
https://www.yoctoproject.org/documentation
Embedded Linux Development Using the Yocto Project Cookbook, by Alex González

## Slide 34
Quiz
Canvas
¢ 10 Questions
¢ 45 Mins
¢ 6 Attempts
¢ Highest Retained

## Slide 35
Assignment
1. Setup buildroot for your target
example 2/2a/2b for rpi4/rpi3B+/rpi3B
in the zip file.
2. Copy to SD Card and boot up the Rpi.
3. Submit screenshot of the build and run.
Outcomes: O2, O7
AI Layer: L1-BuildAssistant
Notes: Assignment
1. Setup buildroot for your target
example 2/2a/2b for rpi4/rpi3B+/rpi3B
in the zip file.
2. Copy to SD Card and boot up the Rpi.
3. Submit screenshot of the build and run.

## Slide 36
Summary
In This Chapter
¢ Overview of Embedded Linux Systems
* Introduction to Embedded Linux Systems
¢ Examples of Embedded Linux Systems
¢ Hardware for Embedded Linux Systems
* System Architecture of Embedded Linux Systems
* Environment for Embedded Linux Systems Development
* No Assignment
* Quiz
Outcomes: O1
Notes: CHAPTER OVERVIEW
In This Chapter, We saw
1. Overview of Embedded Linux Systems
2. Introduction to Embedded Linux Systems
3. Examples of Embedded Linux Systems
4. Hardware for Embedded Linux Systems
5. System Architecture of Embedded Linux Systems
6. Environment for Embedded Linux Systems Development
7. No Assignment
8. Quiz