## Slide 1
System Architecture
Flash Memory — Devices and fs
Notes: Design Decisions to be made before development starts
being able to make informed decisions concerning
• the storage of programs and data,
• how to divide work between kernel device drivers and applications, and
• how to initialize the system.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 2
Chapter Objectives
In This Chapter
¢ Selecting hardware for Embedded Linux
* Storage Strategy — flash memory, fs for flash memory
* Assignment
° Quiz
Notes: CHAPTER OVERVIEW
In This Chapter, We Will Discuss
1. Selecting hardware for Embedded Linux
2. Storage Strategy – flash memory, fs for flash memory
3. Assignment
4. Quiz
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 3
Selecting hardware for
embedded Linux
° First is a CPU architecture that is supported by the kernel
* Second is a reasonable amount of RAM
*Third — is non-volatile storage, usually flash memory
«Fourth is a serial port is very useful, preferably UART-based
° Fifth is loading software when starting from scratch
e.g. load from JTAG interface, or boot code
directly from removable media, especially SD and micro SD
cards, or serial interfaces such as UART or USB.
Outcomes: O6, O7
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: CPU architecture
• First, a CPU architecture that is supported by the kernel—unless the plan is to add a new architecture.
• Looking at the source code for Linux 5.4, there are 25 architectures, each represented by a sub-directory in
the arch/ directory. They are all 32- or 64-bit architectures, most with an MMU, but some without.
• The ones most often found in embedded devices are Arm, MIPS, PowerPC, and x86, each in 32 and 64-bit
variants, all of which have memory management units (MMUs).
• There is another group that doesn't have an MMU and that runs a subset of Linux known as microcontroller
Linux or uClinux. These processor architectures include ARC (Argonaut RISC Core), Blackfin, MicroBlaze,
and Nios.
Reasonable amount of RAM
• 16 MiB is a good minimum, although it is quite possible to run Linux using half that.
• It is even possible to run Linux with 4 MiB if the trouble is taken to optimize every part of the system.
It may even be possible to get lower, but there comes a point at which it is no longer Linux.
non-volatile storage, usually flash memory
• 8 MiB is enough for a simple device such as a webcam or a simple router.
• As with RAM, a workable Linux system can be created with less storage if really needed, but the lower you
go, the harder it becomes.
• Linux has extensive support for flash storage devices, including raw NOR and NAND flash chips, and
managed flash in the form of SD cards, eMMC chips, USB flash memory, and so on.
a serial port is very useful, preferably UART-based.
• It does not have to be fitted on production boards, but makes board bring-up, debugging, and development
much easier
interface for loading software when starting from scratch
• Many microcontroller boards are fitted with a Joint Test Action Group (JTAG) interface for this purpose.
• Modern SoCs also have the ability to load boot code directly from removable media, especially SD and
micro SD cards, or serial interfaces such as UART or USB.
• In addition, there are interfaces to the specific bits of hardware your device needs to get its job done.
• Mainline Linux comes with open source drivers for many thousands of different devices, and there are
drivers (of variable quality) from the SoC manufacturer and from the OEMs of third-party chips that may be
included in the design, but remember the commitment and ability of some manufacturers.
• As a developer of embedded devices, quite a lot of time is spent evaluating and adapting third-party code, if
it is already there, or liaising with the manufacturer if not.
• Finally, there is the requirement to write the device support for interfaces that are unique to the device or
find someone to do that.

## Slide 4
Storage Strategy
* mass storage options for embedded devices
* have a great impact on the rest of the system
* for robustness, speed, and methods used for in-field updates.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
+ https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Most devices employ flash memory in some form or another.
• Flash memory is less expensive now, as storage capacities have increased to the tens of gigabytes.
One objective is to understand
• technology behind flash memory, as well as
• how different memory organization strategies affects the
• low-level driver software that manages it e.g. the Linux memory technology device (MTD) layer.
For each flash technology, there are different choices of fs.
Need look at
• fs often found on embedded devices and a summary of choices for each type of flash memory,
• techniques that make the best use of flash memory and presenting a coherent storage strategy.
Ubuntu
• provides packages for most tools needed to create and format various filesystems.
To install the tools on an Ubuntu 20.04 LTS system, use:
• $ sudo apt install e2fsprogs genext2fs mtd-utils squashfs-tools util-linux
• The mtd-utils package includes mtdinfo, mkfs.jffs2, sumtool, nandwrite, and the UBI command-line tools.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 5
Storage Options
Why Storage? What are the options
¢ NOR flash
* NAND flash memory
* Managed flash memory
* Hard drives
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
* https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Storage options
• Embedded devices need storage that is is physically compact, consuming little power,robust, and reliable
over a lifetime of perhaps tens of years.
• Most often, this means solid-state storage.
Solid-state storage was introduced some years ago with ROM, but for the past 20 years, it was with an
underlying flash memory.
Meanwhile, there were several generations of flash memory, from NOR to NAND to managed flash eMMC
The following are the options:
• NOR flash is expensive, reliable and can be mapped into the CPU address space, which means it allows to
execute code directly from flash. NOR flash chips are low capacity, ranging from a few MB to about a GB.
• NAND flash is much cheaper than NOR and is available in higher capacities, from 10s of MB to 10s of GB.
However, it needs a lot of hardware and software support to turn it into a useful storage medium.
• Managed flash consists of NAND flash chips, with a additional controller to handle complexities of flash
memory and provide a hardware interface similar to that of a hard disk. It removes complexity from the
driver software and insulates system designers from frequent changes in flash technology. SD cards,
eMMC chips, and USB flash drives are in this category. Almost all current generations of smartphones and
tablets have eMMC storage, and this trend is likely to progress with other categories of embedded devices.
• Hard drives are seldom found in embedded systems. However, one exception is digital video recording in
set-top boxes and smart TVs, where a large amount of storage is needed with fast write times..
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 6
Storage Options
NOR Flash
NOR flash
* erase blocks and erase cycles
* maps into CPU address space - including reset vector and bootloader
* Hard drives
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
¢ https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: NOR Flash
erase blocks and erase cycles
• memory cells in NOR flash chips are arranged into erase blocks of, around, 128 KiB. erasing a block sets all
bits to 1 - one word at a time (8, 16, or 32 bits, depending on data bus width). Each erase cycle damages
memory cells slightly, and after a number of cycles, the erase block is unreliable and is unusable anymore.
The maximum number of erase cycles is given in the data sheet for the chip and is usually in the range of
100K to 1M.
maps into CPU address space - including reset vector and bootloader
• The chip is mapped into CPU address space, meaning that code is executed directly from NOR flash.
It includes the bootloader code as it needs no initialization beyond hardwiring the address mapping.
SoCs that support NOR flash have a default memory mapping encompassing the reset vector of the CPU.
Further, the kernel, and even the root fs, can be located in flash memory, avoiding need to copying them
into RAM, in a technique known as eXecute In Place, or XIP. It creates devices with small memory footprint
Common Flash Interface - CFI
• CFI is a standard register-level interface supported by all modern NOR flash chips.
The CFI is described in standard JESD68 https://www.jedec.org/ .
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 7
Storage Options
NAND Flash
NAND flash
* much cheaper than NOR flash and has a higher capacity
* SLC, MLC and TLC
* erase blocks and erase cycles
* does not map into CPU address space
* ECC
* OOB for ECC, Bad Blocks, Filesystem metadata
* Need for a flash controller
* ONFI
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
* https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3, O6
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: NAND Flash
SLC, MLC and TLC
• First generation NAND chips stored one bit per memory cell known as a single-level cell (SLC) organization.
• Then, came two bits per cell in multi-level cell (MLC) or three bits per cell in trilevel cell (TLC) chips.
• With increase in number of bits per cell, reliability decreased, thereby requiring more complex controller
hardware and software to compensate. Use SLC NAND flash chips where reliability is a concern
erase blocks and erase cycles
• Similarly, memory cells in NAND flash chips is from 16 KiB to 512 KiB; erasing a block sets all bits to 1.
As before, each erase cycle damages memory cell, and after some #cycles, the erase block is unreliable
and is unusable anymore. The maximum number of erase cycles is as small as 1K cycles for TLC chips and
up to 100K for SLC..
does not maps into CPU address space
• NAND flash is read and written in pages, usually 2 or 4 KB and not byte-by-byte. Also, it cannot be mapped
into CPU address space, so code and data have to be copied into RAM before they can be accessed.
ECC - Error Correction Codes
• Used for detecting/correcting bit flips in data transfers to and from the chip.
• SLC chips generally use a simple hamming code, to correct a single-bit error in a page read.
• MLC and TLC chips need more sophisticated codes, such as Bose-Chaudhuri-Hocquenghem (BCH), which
corrects up to 8-bit errors per page.
OOB for ECC
• ECCs are stored in an extra area of memory per page known as out-of-band (OOB) area, or the spare area.
• SLC has 1B of OOB per 32B, so a 2 KB page device has OOB 64B/page, and for 4 KB page, it is 128B.
• MLC, TLC chips have larger OOB areas, to due to complex ECCs.
OOB for Bad blocks
• brand new chips can have up to 2% of their blocks marked bad
• During production, manufacturer tests all blocks and flags a failing block in the OOB area of each page in a
block. So, it is common for brand new chips have up to 2% of their blocks marked bad in this way.
• Save the OOB information for analysis before erasing the area, when there is a problem.
• Also, expect for a similar proportion of errors on erase before the erase cycle limit is reached.
• The NAND flash driver should detect this and avoid it as bad.
OOB for filesystem metadata
• some bytes are left once the space in OOB is used for ECC and bad blocks
• these free bytes are used by some flash filesystems to store filesystem metadata.
• therefore, many parts of the system are interested in the layout of the OOB area:
SoC ROM boot code, bootloader, kernel MTD driver, filesystem code, and tools to create fs images..
• Further, there is not much standardization, so there may be situations in which the bootloader writes data
using an OOB format that cannot be read by the kernel MTD driver.
needs a NAND flash controller
• It is a part of the SoC, and a corresponding driver is needed in the bootloader and kernel.
• The NAND flash controller.is needed for access – and handle the hardware interface for the chip, to transfer
data to and from pages, and includes hardware for error correction.
ONFI - Open NAND Flash Interface
• is a standard register-level interface for modern NAND flash chips. See http://www.onfi.org/
Modern NAND flash technology is complicated.
• Pairing NAND flash memory with a controller is no longer enough.
• It also needs interfaces to the hardware to abstract technical details, such as error correction.

## Slide 8
Storage Options
Managed Flash
Managed Flash
* well-defined hardware interface and a standard flash controller to hide
complexities of memory
¢ MultiMediaCard and,
* Secure Digital SD cards
* eMMC
¢ CF —- Compact Flash
* USB Flash Drive
* Universal Flash Storage
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
* https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3, O7
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Managed Flash
• Supporting flash memory in the OS esp. NAND is simpler if there is a well-defined hardware interface and a
standard flash controller. It hides the complexities of the memory. It means combining flash chips with a
microcontroller to offer an ideal storage device with a small sector size, and compatible with conventional fs.
• This is managed flash memory, and it is becoming more and more common.
• important types of these chips are Secure Digital (SD) cards and eMMC - the embedded variant.
MMC - MultiMediaCard and Secure Digital cards
• MMC was introduced in 1997 by SanDisk and Siemens as a form of packaged storage using flash memory.
• In 1999,SanDisk, Matsushita, and Toshiba created the Secure Digital (SD) card - based on MMC, but adds
encryption and DRM (the "secure" part of the name).
• Both were intended for consumer electronics such as digital cameras, music players, and similar devices.
• SD cards are dominant in consumer and embedded electronics, though encryption is seldom used.
• small packaging: mini SD and microSD;
large capacities: high capacity SDHC <=32 GB, and extended capacity SDXC up to 2TB.
• hardware interface for MMC and SD cards is very similar .. full-sized MMC cards can be used in full-sized
SD card slots - but not other way. Early versions of MMC used a 1-bit Serial Peripheral Interface (SPI);
more recent cards use a 4-bit interface.
SD card
• Inside an SD card there is a microcontroller and one or more NAND flash chips.
• The microcontroller implements a command set for reading and writing memory in sectors of 512 bytes;
and, manages the flash memory, performing the function of a flash translation layer.
• Is preformatted with a FAT filesystem: FAT16 on SDSC cards, FAT32 on SDHC, and exFAT on SDXC.
• and the quality of NAND flash chips and software on the microcontroller varies greatly between cards.
• A FAT fs is prone to file corruption so, it is questionable whether it iis reliable for deep embedded use.
• the prime use case for MMC and SD cards is for removable storage for cameras, tablets, and phones.
eMMC - Embedded MMC
• is simply MMC memory that is packaged and soldered on to the motherboard - using a 4- or 8-bit interface
for data transfer.
• The chips are intended to be used as storage for an operating system and are not preformatted with any fs.
CF - CompactFlash
• uses a subset of Personal Computer Memory Card International Association (PCMCIA) hardware interface.
• CF exposes memory through a parallel ATA interface and appears to the OS as a standard hard disk.
• They were common in x86-based single board computers and professional video and camera equipment.
USB flash drive
• memory is accessed through a USB interface and the controller implements the USB mass storage
specification, as well as the flash translation layer and interface to the flash chip, or chips.
• USB mass storage protocol, in turn, is based on the SCSI disk command set.
• usually preformatted with a FAT filesystem – similar to MMC and SD cards.
• main use case in embedded systems is to exchange data with PCs.
Universal Flash Storage (UFS)
• Is a recent addition to the list of options for managed flash storage
• like eMMC, it is packaged in a chip that is mounted on the motherboard
• has a high-speed serial interface and can achieve data rates greater than eMMC
• supports a SCSI disk command set.

## Slide 9
Accessing Flash Memory
from bootloader
Accessing Flash Memory
* need for bootloader to load kernel binaries and other images from
various flash devices, and
* perform system maintenance tasks such as erasing and
reprogramming flash memory.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
* https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Accessing Flash Memory
• need for bootloader to load kernel binaries and other images from various flash devices, and
• perform system maintenance tasks such as erasing and reprogramming flash memory.
• bootloader must have the drivers and infrastructure needed to support read, erase, and write operations on
the type of memory: whether it be NOR, NAND, or managed.
• While U-Boot is discussed, other bootloaders follow a similar pattern.
U-Boot and NOR flash
• U-Boot has drivers for NOR CFI chips in drivers/mtd and utilizes various erase commands to erase memory
and cp.b to copy data byte by byte, programming the flash cells.
• Suppose NOR flash memory is mapped from 0x40000000 to 0x48000000, of which 4 MB, starting at
0x40040000, is a kernel image.
To load a new kernel into flash, use these U-Boot commands:
=> tftpboot 100000 uImage
=> erase 40040000 403fffff
=> cp.b 100000 40040000 $(filesize)
The filesize variable in the preceding example is set by the tftpboot command, to the size of the file just
downloaded.
Storage Options
U-Boot and NAND flash
• For NAND flash, you need a driver for the NAND flash controller on your SoC, which you can find in the U-
Boot source code in the drivers/mtd/nand directory.
• You can use the nand command to manage memory using the erase, write, and read sub-commands. This
example shows a kernel image being loaded into RAM at 0x82000000 and then placed into flash, starting at
the 0x280000 offset
• To load a new kernel into flash, use these U-Boot commands:
=> tftpboot 82000000 uImage
=> nand erase 280000 400000
=> nand write 82000000 280000 $(filesize)
U-Boot can also read files stored in the JFFS2, YAFFS2, and UBIFS filesystems.
nand write will skip blocks that are marked as bad.
If the data being written is for a filesystem, make sure that the filesystem also skips bad blocks.
U-Boot and MMC, SD, and eMMC
• U-Boot has drivers for several MMC controllers in drivers/mmc.
• U-Boot can access raw kernel and filesystem images.
raw data is accessed using mmc read and mmc write at the user interface level
• U-Boot can also read files from the FAT32 and ext4 filesystems on MMC storage.
• U-Boot needs drivers to access NOR, NAND, and managed flash.
• The driver to use depends on the choice of NOR chip or the flash controller on the SoC.
• Accessing raw NOR and NAND flash from Linux involves additional layers of software.

## Slide 10
Accessing Flash Memory
from Linux
Accessing Flash Memory
+ is handled by MTD - Memory Technology Device subsystem
MTD consists of three layers:
* acore set of functions,
* aset of drivers for various types of chips, and
¢ user-level drivers to access flash memory as a char or a block device
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
* https://en.wikipedia.org/wiki/Toolchain
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Accessing Flash Memory is handled by MTD - Memory Technology Device subsystem
• provides the basic interfaces to read, erase, and write blocks of Raw NOR and NAND flash memory
• For NAND flash, there are also functions to handle the OOB area and identify bad blocks.
• For managed flash, drivers are needed to handle a particular hardware interface.
- MMC/SD cards and eMMC use the mmcblk driver, while
- CompactFlash and hard drives use the SCSI disk driver, sd.
- USB flash drives use the usb_storage driver, together with the sd driver.
MTD - Memory Technology Device subsystem
• MTD subsystem was started by David Woodhouse in 1999, and developed extensively thereafter.
• MTD consists of three layers:
- a core set of functions,
- a set of drivers for various types of chips, and
- user-level drivers that present the flash memory as a char device or a block device
• The chip drivers are at the lowest level and interface with flash chips.
NOR: Only a small number of drivers are needed for NOR flash chips, enough to cover the CFI standard
and variations, plus a few non-compliant chips, which are now mostly obsolete.
NAND: For NAND flash, a driver is needed for the NAND flash controller being used; which is usually
supplied as part of the board support package.
There are drivers for about 40 of them in the current mainline kernel, in the drivers/mtd/nand directory.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 11
Accessing Flash Memory
from Linux
MTD Partitions
partition flash memory into several areas, to provide space for
* a bootloader,
* akernel image, or
* a root filesystem.
MTD Partition Information
• read from /proc/mtd - for a summary of the configuration at runtime
• # cat /proc/mtd
dev: size erasesize name
mtd0: 00080000 00020000 "SPL"
mtd1: 000C3000 00020000 "U-Boot"
mtd2: 00020000 00020000 "U-BootEnv"
mtd3: 00400000 00020000 "Kernel"
mtd4: 07A9D000 00020000 "Filesystem“
Outcomes: O6
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: MTD Partitions
partition flash memory into several areas, to provide space for
• a bootloader,
• a kernel image, or
• a root filesystem.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 12
Filesystems for flash memory
Filesystems for flash memory
several challenges when it comes to making efficient use of flash
memory for mass storage:
Outcomes: O6
Notes: Filesystems for flash memory
several challenges when it comes to making efficient use of flash memory for mass storage:
• the mismatch between the size of an erase block and a disk sector,
• the limited number of erase cycles per erase block, and
• the need for bad block handling on NAND chips.
These differences are resolved by a flash translation layer, or FTL.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 13
Filesystems for flash memory
Flash translation layers
Filesystems for flash memory
Features include:
* Sub allocation
* Garbage collection
¢ Wear leveling
* Bad block handling
* Robustness
There are several ways to deploy the flash translation layer:
* In the filesystem: As with JFFS2, YAFFS2, and UBIFS.
¢ In the block device driver: The UBI driver, which UBIFS depends on,
implements some aspects of a flash translation layer.
* In the device controller: As with managed flash devices.
Outcomes: O4, O6
Notes: Filesystems for flash memory
A flash translation layer has the following features:
Sub allocation: Filesystems work best with a small allocation unit, traditionally a 512-byte sector.
This is much smaller than a flash erase block of 128 KB or more. Therefore, erase blocks are subdivided into
smaller units to avoid wasting large amounts of space.
Garbage collection: A consequence of suballocation is that an erase block will contain a mixture of good data
and stale data once the filesystem has been in use for a while. Since we can only free up whole erase blocks,
the only way to reclaim this free space is to coalesce the good data into one place, and then return the now
empty erase block to the free list. This is known as garbage collection, and is usually implemented as a
background thread.
Wear leveling: There is a limit on the number of erase cycles for each block. To maximize the lifespan of a
chip, it is important to move data around so that each block is erased roughly the same number of times.
Bad block handling: On NAND flash chips, avoid using any block marked bad and mark good blocks as bad if
they cannot be erased.
Robustness: Embedded devices may be powered off or reset without warning, so any filesystem should be
able to cope without corruption, usually by incorporating a journal or a log of transactions.
There are several ways to deploy the flash translation layer:
• In the filesystem: As with JFFS2, YAFFS2, and UBIFS.
• In the block device driver: The UBI driver, which UBIFS depends on, implements some aspects of a flash
translation layer.
• In the device controller: As with managed flash devices.

## Slide 14
Filesystems for flash memory
for NOR and NAND flash memory
Filesystems for flash memory
three such filesystems:
¢ JFFS2 (Journaling Flash File System 2):
« YAFFS2 (Yet Another Flash File System 2):
¢ UBIFS (Unsorted Block Image File System):
Outcomes: O6
Notes: Filesystems for flash memory
a filesystem that understands the peculiarities of the underlying technology:
three such filesystems:
• JFFS2 (Journaling Flash File System 2): This was the first flash filesystem for Linux and is still in use today.
It works for NOR and NAND memory, but is notoriously slow during mount.
• YAFFS2 (Yet Another Flash File System 2): This is similar to JFFS2, but specifically for NAND flash
memory. It was adopted by Google as the preferred raw flash filesystem on Android devices.
• UBIFS (Unsorted Block Image File System): This works in conjunction with the UBI block driver to create a
reliable flash filesystem. It works well with both NOR and NAND memory, and since it generally offers
better performance than JFFS2 or YAFFS2, it should be the preferred solution for new designs.
All of these use MTD as the common interface to flash memory.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 15
Filesystems for flash memory
for NOR and NAND flash memory: JFFS2
JFFS2
¢ JFFS2 is a log-structured filesystem that uses MTD to access flash memory.
* Ina log-structured fs, changes are written sequentially as nodes to flash
memory.
* Anode may contain changes to a directory, such as names of files created or
deleted, or it may contain changes to file data.
* After a while, a node may be superseded by information contained in
subsequent nodes and becomes an obsolete node.
* Both NOR and NAND flash are organized as erase blocks.
« Erasing a block sets all bits to 1.
Outcomes: O6
Notes: Journaling Flash File System had its beginnings in the software for the Axis 2100 network camera in 1999.
For many years, it was the only flash filesystem for Linux and has been deployed on many thousands of
different types of devices. Today, it is not the best choice, but it shows the beginning of the evolutionary path.
• JFFS2 is a log-structured filesystem that uses MTD to access flash memory.
In a log-structured fs, changes are written sequentially as nodes to flash memory. A node may contain
changes to a directory, such as names of files created or deleted, or it may contain changes to file data.
After a while, a node may be superseded by information contained in subsequent nodes and becomes an
obsolete node. Both NOR and NAND flash are organized as erase blocks. Erasing a block sets all bits to 1.
• JFFS2 categorizes erase blocks into three types:
• Free: This contains no nodes at all.
• Clean: This only contains valid nodes.
• Dirty: This contains at least one obsolete node.
• At any one time, there is one block receiving updates, which is called the open block.
If power is lost or the system is reset, the only data that can be lost is the last write to the open block.
In addition, nodes are compressed as they are written, increasing the effective storage capacity of the flash
chip, which is important if using expensive NOR flash memory.
• When the number of free blocks falls below a certain threshold, a garbage collector kernel thread is started,
which scans for dirty blocks, copies the valid nodes into the open block, and then frees up the dirty block.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 16
Filesystems for flash memory
for NOR and NAND flash memory: YAFFS2
YAFFS2
* The YAFFS filesystem was written specifically to handle NAND flash chips at
a time when JFFS2 did not.
¢ Subsequent changes to handle larger (2 KiB) page sizes resulted in YAFFS2.
¢ YAFFS is also a log-structured filesystem that follows the same design
principles as JFFS2.
* The different design decisions mean that it has a faster mount-time scan,
simpler and faster garbage collection, and has no compression, which
speeds up reads and writes at the expense of less efficient use of storage.
Outcomes: O1, O6
Notes: YAFFS2
• The YAFFS filesystem was written specifically to handle NAND flash chips at a time when JFFS2 did not.
• Subsequent changes to handle larger (2 KiB) page sizes resulted in YAFFS2.
• YAFFS is also a log-structured filesystem that follows the same design principles as JFFS2.
• The different design decisions mean that it has a faster mount-time scan, simpler and faster garbage
collection, and has no compression, which speeds up reads and writes at the expense of less efficient use
of storage.
• YAFFS is not limited to Linux; it has been ported to a wide range of operating systems.
It has a dual license: GPLv2, in order to be compatible with Linux, and a commercial license for other
operating systems. Unfortunately, the YAFFS code has never been merged into mainline Linux, so have to
patch the kernel.
• To get YAFFS2 and patch a kernel, use the following:
$ git clone git://www.aleph1.co.uk/yaffs2
$ cd yaffs2
$ ./patch-ker.sh c m <path to your link source>
Then, configure the kernel with CONFIG_YAFFS_YAFFS2.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 17
Filesystems for flash memory
for NOR and NAND flash memory: UBI & UBIFS
UBI - is a Volume manager flash memory
* provides ideal, reliable view of flash chip.
* maps physical erase blocks (PEB) to logical erase blocks (LEB).
¢ Bad blocks are not mapped to LEBs and are never used.
* UBl accesses the flash memory through the MTD layer.
¢ Additionally, it can divide an MTD partition into a number of UBI volumes,
which improves wear leveling
* fulfills two major requirements of a flash translation layer: wear leveling and
bad-block handling.
UBIFS - is a filesystem -- to follow next.
# ubiformat /dev/mtd6 -s 2048
# ubiattach -p /dev/mtd6 -O 2048
# ubimkvol /dev/ubi0 -N vol_1 -s 32MiB
# ubimkvol /dev/ubi0 -N vol_2 -m
Outcomes: O6
Notes: UBI
• The Unsorted Block Image (UBI) driver is a volume manager for flash memory that takes care of bad block
handling and wear leveling.
• It was implemented by Artem Bityutskiy and first appeared in Linux 2.6.22.
• In parallel with that, engineers at Nokia were working on a filesystem that would take advantage of the
features of UBI, which they called UBIFS; it appeared in Linux 2.6.27.
• Splitting the flash translation layer in this way makes the code more modular and also allows other
filesystems to take advantage of the UBI driver.
UBI
• provides ideal, reliable view of flash chip - maps physical erase blocks (PEB) to logical erase blocks (LEB).
• Bad blocks are not mapped to LEBs and are never used. If a block cannot be erased, it is marked as bad
and dropped from mapping. UBI keeps a count of number of times each PEB has been erased in header of
LEB, and then changes the mapping to ensure that each PEB is erased the same number of times.
• UBI accesses the flash memory through the MTD layer. As an extra feature, it can divide an MTD partition
into a number of UBI volumes, which improves wear leveling:
• imagine that there are two filesystems, one containing fairly static data, such as a root filesystem, and
other containing data that is constantly changing.
• If they are stored in separate MTD partitions, wear leveling only has an effect on the second one,
whereas if they are stored in two UBI volumes in a single MTD partition, the wear leveling takes place
over both areas of the storage, and the lifetime of the flash memory is increased.
• UBI fulfills two major requirements of a flash translation layer: wear leveling and bad-block handling.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 18
Filesystems for flash memory
for NOR and NAND flash memory: UBIFS
UBIFS
* UBIFS uses a UBI volume to create a robust filesystem
* adds sub-allocation and garbage collection to create a complete flash
translation layer.
* has write-back caching; flush frequently to persistent storage.
* minimum size of journal is 4 MB - so not suitable for very small flash devices.
Outcomes: O6
Notes: UBI and UBIFS
• UBIFS uses a UBI volume to create a robust filesystem
• adds sub-allocation and garbage collection to create a complete flash translation layer.
• has write-back caching, which means writes are much faster, but with the usual problem of potential loss of
data that has not been flushed from the cache to flash memory in the event of power down
• resolve problem by using fsync(2) and fdatasync(2) functions to force a flush of file data at crucial points.
• UBIFS has a journal for fast recovery in the event of power down.
Minimum size of the journal is 4 MiB, so UBIFS is not suitable for very small flash devices.
• Once the UBI volumes are created, mount them using the device node for the volume, such as /dev/ubi0_0
# mount -t ubifs ubi0:vol_1 /mnt
• Creating a filesystem image for UBIFS is a two-stage process:
first, create a UBIFS image using mkfs.ubifs, and then embed it into a UBI volume using ubinize.
$ mkfs.ubifs -r rootfs -m 2048 -e 124KiB -c 256 -o rootfs.ubi
• mkfs.ubifs is provided the page size with -m, the size of the UBI LEB with -e, and the maximum number
of erase blocks in the volume with -c.
• If the first volume is 32 MiB and an erase block is 128 KiB, then the number of erase blocks is 256.
So, it takes the contents of the rootfs directory and creates a UBIFS image named rootfs.ubi
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 19
Filesystems for flash memory
for managed flash: overview
Overview
* As the trend toward managed flash technologies continues, particularly
eMNC, consider how to use it effectively.
* as they appear to have the same characteristics as hard disk drives,
* yet underlying NAND flash chips have limitations of
large erase blocks with
limited erase cycles and
bad block handling.
Outcomes: O1, O6
Notes: Overview
As the trend toward managed flash technologies continues, particularly eMMC, consider
• how to use it effectively.
• as they appear to have the same characteristics as hard disk drives,
• yet underlying NAND flash chips have limitations of
large erase blocks with
limited erase cycles and
bad block handling.
• Also, need robustness in the event of losing power.
It is possible to use any of the normal disk filesystems, but choose one that reduces disk writes and has a
fast restart after an unscheduled shutdown.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 20
Filesystems for flash memory
tools for managed flash: flashbench
flashbench
* a tool to deduce erase block size and page size,
to make optimum use of the underlying flash memory
$ sudo ./flashbench -a /dev/mmcblk0 --blocksize=1024
Outcomes: O6
AI Layer: L1-BuildAssistant
Notes: flashbench
• a tool to deduce erase block size and page size,
to make optimum use of the underlying flash memory.
• initially written by Arnd Bergman, as described in LWN article available at https://lwn.net/Articles/428584
• get the code from https://github.com/bradfa/flashbench
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 21
Filesystems for flash memory
commands for managed flash: Discard and TRIM
Discard and TRIM
* commands that pass information about deleted sectors to the disk controller.
Outcomes: O6
Notes: Discard and TRIM
• when a file is deleted, only the modified directory node is written to storage, while the sectors containing the
file's contents remain unchanged
• so, when flash translation layer is in disk controller - e.g. managed flash, it does not know that this group of
disk sectors no longer contains useful data.
• additional commands that pass information about deleted sectors down to the disk controller has improved
this situation.
• the SCSI and SATA specifications have a TRIM command
and MMC has a similar command named ERASE
• In Linux, this feature is known as discard.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 22
Filesystems for flash memory
for managed flash: ext4
* extended filesystem, ext, has been the main filesystem for Linux desktops
since 1992.
ext4
* is current version and is very stable and well-tested.
¢ has ajournal that makes recovering from an unscheduled shutdown fast and
mostly painless.
* is agood choice for managed flash devices, and it is preferred for Android
devices with eMMC storage.
¢ further, if the device supports discard, mount with the -o discard option.
Outcomes: O6
AI Layer: L1-BuildAssistant
Notes: • extended filesystem, ext, has been the main filesystem for Linux desktops since 1992.
• ext4, is current version and is very stable and well-tested.
ext4
• has a journal that makes recovering from an unscheduled shutdown fast and mostly painless.
• is a good choice for managed flash devices, and it is preferred for Android devices with eMMC storage.
• further, if the device supports discard, mount with the -o discard option.
• To format and create an ext4 filesystem at runtime
# mkfs.ext4 /dev/mmcblk0p2
# mount -t ext4 -o discard /dev/mmcblk0p1 /mnt
genext2fs
• To create a filesystem image at build time, use genext2fs available at http://genext2fs.sourceforge.net.
• In this example, the block size is specified with -B and the number of blocks in the image with -b:
$ genext2fs -B 1024 -b 10000 -d rootfs rootfs.ext4
• genext2fs can make use of a device table to set the file permissions and ownership, with -D [file table].
• this will actually generate an image in Ext2 format.
• upgrade to Ext4 using tune2fs as follows (details of command options are in the tune2fs(8) man page):
$ tune2fs -j -J size=1 –O filetype,extents,uninit_bg,dir_index rootfs.ext4
$ e2fsck -pDf rootfs.ext4
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 23
Filesystems for flash memory
for managed flash: F2FS
F2FS
* is alog-structured filesystem that
- provides resilience in the face of power down and
- provides good write performance showing a twofold improvement over ext4.
* designed for managed flash devices, especially eMMC chips and SD cards.
¢ marked as experimental, indicating that it is not extensively deployed yet,
but some Android devices are using it
Outcomes: O1, O4, O6, O7
Notes: F2FS - Flash-Friendly File System, known as F2FS,
• is a log-structured filesystem
• designed for managed flash devices, especially eMMC chips and SD cards.
• written by Samsung and was merged into mainline Linux in 3.8.
• marked as experimental, indicating that it has not been extensively deployed yet,
but some Android devices are using it.
• takes into account the page and erase block sizes, and then tries to align data on these boundaries.
the log format
- provides resilience in the face of power down and
- provides good write performance showing a twofold improvement over ext4.
• a good description of the design of F2FS in kernel documentation in Documentation/filesystems/f2fs.txt,
• The mkfs.f2fs utility creates an empty F2FS filesystem with the -l label:
# mkfs.f2fs -l rootfs /dev/mmcblock0p1
# mount -t f2fs /dev/mmcblock0p1 /mnt
• There isn't (yet) a tool you can use to create F2FS filesystem images offline.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 24
Filesystems for flash memory
for managed flash: FAT 16/32
FAT16/32
* old Microsoft filesystems.
* continue to be important as a common format understood by most OSs.
* not suitable for storing critical files because they are prone to corruption and
make poor use of the storage space
¢ Linux supports FAT16 through the msdos filesystem and both FAT32 and
FAT 16 through the vfat filesystem
Outcomes: O6
AI Layer: L1-BuildAssistant
Notes: FAT16/32, - old Microsoft filesystems, FAT16 and FAT32.
• continue to be important as a common format understood by most operating systems.
• When an SD card or USB flash drive is bought, it is almost certain to be formatted as FAT32 and, in some
cases, the on-card microcontroller is optimized for FAT32 access patterns.
• Also, some boot ROMs require a FAT partition for second-stage bootloader – e.g. TI OMAP-based chips,.
• FAT formats are definitely not suitable for storing critical files because they are prone to corruption and
make poor use of the storage space.
• Linux supports FAT16 through the msdos filesystem and both FAT32 and FAT16 through the vfat filesystem.
• To mount a device, say an SD card, on the second MMC hardware adapter:
# mount -t vfat /dev/mmcblock1p1 /mnt
• FAT32 has a limitation of 32 GiB on the device's size.
• Devices of a larger capacity are formatted using Microsoft exFAT format, and it is required for SDXC cards.
• There is no kernel driver for exFAT, but is supported by means of a user space FUSE driver.
• exFAT is proprietary to Microsoft, so there could be licensing implications for this format on a device.
IMPORTANT NOTE In the past, there were licensing issues with vfat driver, for infringing a patent held by
Microsoft.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 25
Filesystems for flash memory
for managed flash: Read-only compressed filesystems
Read-only compressed filesystems
* Compressing data is useful if there is not quite enough storage to fit
everything in.
¢ However, if the files are never going to be written, as is usually the case with
the root filesystem, better compression ratios can be achieved by using a
read-only compressed filesystem.
Outcomes: O6
Build Path: rootfs
Notes: Read-only compressed filesystems
• Compressing data is useful if there is not quite enough storage to fit everything in.
• Both JFFS2 and UBIFS do on-the-fly data compression by default.
• However, if the files are never going to be written, as is usually the case with the root filesystem, better
compression ratios can be achieved by using a read-only compressed filesystem.
• Linux supported several of these: romfs, cramfs, and squashfs.
• The first two are obsolete now
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 26
Filesystems for flash memory
for managed flash: SquashFS
SquashFS
* no mechanism for modifying any of the files at runtime.
only way to update is to erase whole partition and program in a new image
* isnot bad-block aware
so must be used with reliable flash memory such as NOR flash, or
can be on NAND flash so long as UBI is used for an emulated, reliable MTD
Outcomes: O6
Notes: SquashFS
• was written as a replacement for cramfs - by Phillip Lougher in 2002 .
• existed as a kernel patch for a long time, eventually merged into mainline Linux in version 2.6.29 in 2009.
• is very easy to use:
create a filesystem image using mksquashfs and install it to the flash memory:
$ mksquashfs rootfs rootfs.squashfs
resulting filesystem is read-only, so there is no mechanism for modifying any of the files at runtime.
- only way to update a SquashFS filesystem is to erase the whole partition and program in a new image.
• is not bad-block aware and so must be used with reliable flash memory such as NOR flash.
• can be used on NAND flash so long as UBI is used to create an emulated, reliable MTD.
• Enable CONFIG_MTD_UBI_BLOCK kernel configuration,
to create a readonly MTD block device for each UBI volume.
• A read-only filesystem is great for immutable contents.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 27
Filesystems for flash memory
for managed flash: tmpfs
tmpfs
* some files that have a short lifetime or have no significance after a reboot.
* such files are put into /tmp, and so it makes sense to keep these files from
reaching permanent storage.
* no device node for tmpfs,
* default maximum size is half the physical RAM
* amount of memory used will grow and shrink as files are created and deleted
Outcomes: O6
Build Path: RT
AI Layer: L1-BuildAssistant
Notes: tmpfs is ideal, when
• some files that have a short lifetime or have no significance after a reboot.
• such files are put into /tmp, and so it makes sense to keep these files from reaching permanent storage.
• create a temporary RAM-based filesystem by simply mounting tmpfs:
$ mount -t tmpfs tmp_files /tmp
• like procfs and sysfs, there is no device node for tmpfs, so a placekeeper string tmp_files was used above.
• The amount of memory used will grow and shrink as files are created and deleted.
• The default maximum size is half the physical RAM.
• It is a disaster if tmpfs became that large, so it is a very good idea to cap it with -o size parameter.
The parameter can be given in bytes, KiB (k), MiB (m), or GiB (g), like this, for example:
# mount -t tmpfs -o size=1m tmp_files /tmp
• In addition to /tmp, some subdirectories of /var contain volatile data, and it is a good practice to use tmpfs
for them as well, either by creating a separate filesystem for each or by using symbolic links.
Buildroot does this::
/var/cache -> /tmp
/var/lock -> /tmp
/var/log -> /tmp
/var/run -> /tmp
/var/spool -> /tmp
/var/tmp -> /tmp
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 28
Filesystems for flash memory
making the root filesystem read-only
Making the root filesystem read-only
* such files are put into /tmp, and so it makes sense to keep these files from
reaching permanent storage.
* no device node for tmpfs,
¢ default maximum size is half the physical RAM
* amount of memory used will grow and shrink as files are created and deleted
Outcomes: O6
Build Path: rootfs
AI Layer: L1-BuildAssistant
Notes: Making the root filesystem read-only
• to make a target device able to survive unexpected events, including file corruption, and still be able to boot
and achieve at least a minimum level of functionality.
• is a key part of achieving the goal because it eliminates accidental overwrites.
• is easy: replace rw with ro on the kernel command line or
use an inherently read-only filesystem such as SquashFS.
However, you will find that there are a few files and directories that are traditionally writable:
• /etc/resolv.conf: is written by network configuration scripts to record the addresses of DNS name servers.
The information is volatile, so you simply have to make it a symlink to a temporary directory; for example,
/etc/resolv.conf -> /var/run/resolv.conf.
• /etc/passwd: This file, along with /etc/group, /etc/shadow, and /etc/gshadow, stores user and group names
and passwords. They need to be symbolically linked to an area of persistent storage.
• /var/lib: Many applications expect to be able to write to this directory and keep permanent data here.
One solution is to copy a base set of files to a tmpfs filesystem at boot time and then bind mount /var/lib to
the new location. It can be done by sequence of commands such as these into one of the boot scripts:
$ mkdir -p /var/volatile/lib
$ cp -a /var/lib/* /var/volatile/lib
$ mount --bind /var/volatile/lib /var/lib
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 29
Filesystems for flash memory
choices and options: summary
choices and options: summary of options available
+ looked at the technology behind solid-state memory and at the many types of
filesystems.
« In most cases, storage requirements are divided into these three categories.
¢ Permanent, read-write data: Runtime configuration, network parameters,
passwords, data logs, and user data
¢ Permanent, read-only data: Programs, libraries, and configurations files that are
constant; for example, the root filesystem
* Volatile data: Temporary storage; for example, /tmp
Outcomes: O6
Build Path: rootfs
Notes: choices and options: summary of options available
• looked at the technology behind solid-state memory and at the many types of filesystems.
• In most cases, storage requirements are divided into these three categories.
• Permanent, read-write data: Runtime configs, network parameters, passwords, data logs, user data
choices for read-write storage are as follows:
• NOR: UBIFS or JFFS2
• NAND: UBIFS, JFFS2, or YAFFS2
• eMMC: ext4 or F2FS
• Permanent, read-only data: Programs, libraries, config files that are constant; e.g. the root filesystem
For read-only storage, you can use any of these, mounted with the ro attribute:
Additionally, if you want to save space, you could use SquashFS.
Finally, for volatile storage, there is only one choice: tmpfs.
• Volatile data: Temporary storage; for example, /tmp
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 30
Summary Notes
* Flash Memory.
* Filesystems.
Further reading
¢ General MTD documentation:
http://www.linux-mtdinfradead.org/doc/general.html
¢ Flash-Friendly File System (F2FS), by Joo-Young Hwang:
https://elinux.org/images/1/12/Elc2013_Hwang.pdf
¢ An F2FS teardown, by Neil Brown:
https://Iwn.net/Articles/518988/
Outcomes: O6
Notes: 1. Flash memory has been the storage technology of choice for embedded Linux from the beginning.
2. Over the years, Linux has gained very good support, from low-level drivers up to flash-aware filesystems,
with the latest being UBIFS.
3. As the rate at which new flash technologies are introduced increases,
it is becoming harder to keep pace with the changes at the high end.
4. System designers are increasingly turning to managed flash in the form of eMMC, to provide a stable
hardware and software interface that is independent of the memory chips inside.
5. Embedded Linux developers are beginning to get to grips with these new chips.
6. Support for TRIM in ext4 and F2FS is well-established, and it is slowly finding its way into the chips
themselves.
7. Also, the appearance of new filesystems that have been optimized to manage flash, such as F2FS, is a
welcome step forward.
8. However, the fact remains that flash memory is not the same as a hard disk drive.
9. You have to be careful when you're minimizing the number of filesystem writes – especially as the higher
density TLC chips may be able to support as few as 1,000 erase cycles.

## Slide 31
Quiz
Canvas
¢ 10 Questions
¢ 45 Mins
¢ 6 Attempts
¢ Highest Retained

## Slide 32
Assignment
1. Setup buildroot for your target
example 2/2a/2b for rpi4/rpi3B+/rpi3B
in the zip file.
2. Copy to SD Card and boot up the Rpi.
3. Submit screenshot of the build and run.
Outcomes: O2, O7
AI Layer: L1-BuildAssistant
Notes: Assignment
1. Setup buildroot for your target
example 2/2a/2b for rpi4/rpi3B+/rpi3B
in the zip file.
2. Copy to SD Card and boot up the Rpi.
3. Submit screenshot of the build and run.

## Slide 33
Summary
In This Chapter
¢ Storage Strategy — flash memory, fs for flash memory
* Assignment
* Quiz
Notes: CHAPTER OVERVIEW
In This Chapter, We Discussed
1. Storage Strategy – flash memory, fs for flash memory
2. Assignment
3. Quiz
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 34
Summary
In This Chapter
¢ Overview of Embedded Linux Systems
* Introduction to Embedded Linux Systems
¢ Examples of Embedded Linux Systems
¢ Hardware for Embedded Linux Systems
* System Architecture of Embedded Linux Systems
* Environment for Embedded Linux Systems Development
* No Assignment
* Quiz
Outcomes: O1
Notes: CHAPTER OVERVIEW
In This Chapter, We saw
1. Overview of Embedded Linux Systems
2. Introduction to Embedded Linux Systems
3. Examples of Embedded Linux Systems
4. Hardware for Embedded Linux Systems
5. System Architecture of Embedded Linux Systems
6. Environment for Embedded Linux Systems Development
7. No Assignment
8. Quiz