## Slide 1
Configure and Build
Kernel and root fs
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Design Decisions to be made before development starts
The kernel is the third element of embedded Linux.
It is responsible for managing resources and interfacing with hardware, and so it affects every aspect of the
final software build.
It is usually tailored to a particular hardware configuration, however
- device trees allow the creation of a generic kernel tailored to particular hardware.
how to get a kernel for a board? and
how to configure and compile it?
what is Bootstrap, focusing on the part the kernel plays?
what are device drivers and how they pick up information from the device tree?
The following main topics are the main topics discussed:
What does the kernel do?
Choosing a kernel
Building the kernel
Booting the kernel
Porting Linux to a new board
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 2
Chapter Objectives
In This Chapter
¢ What does the kernel do?
¢ Choosing, Building and Booting a kernel
* Porting Linux to a new board
¢ Assignment
* Quiz
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: CHAPTER OVERVIEW
In This Chapter, We Will Discuss
1. Selecting hardware for Embedded Linux
2. Storage Strategy – flash memory, fs for flash memory
3. Assignment
4. Quiz
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 3
Why Linux ?
* Started 1991 by Linus Torvalds
* he wrote a kernel
* he used components from the GNU project, especially the toolchain,
the C library, and basic command-line tools
* gives Linux a lot of flexibility in the way it is used
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O3
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: History of Linux
• Linux began in 1991 when Linus Torvalds wrote an operating system for Intel 386- and 486-based PC’s.
He was inspired by the Minix operating system written by Andrew S. Tanenbaum 4 years earlier. Linux
differed in many ways from Minix; the main difference being that it was a 32-bit virtual memory kernel and
the code was open source, later released under the GPL v2 license. He announced it on August 25, 1991.
• Linus did not write an operating system, rather he wrote a kernel, which is a component of an operating
system. To create a complete operating system with user space commands and a shell command
interpreter, he used components from the GNU project, especially the toolchain, the C library, and basic
command-line tools. That distinction remains today and gives Linux a lot of flexibility in the way it is used.
• The Linux kernel is combined with a GNU user space to create a full Linux distribution that runs on desktops
and servers, and is called GNU/Linux; it can be combined with an Android user space to create the
wellknown mobile operating system, or it can be combined with a small BusyBox based user space to
create a compact embedded system.
• By removing the toolchain, slimmer runtime images are deployed without a compiler or header files.
• By decoupling user space from the kernel, additional options in terms of init systems (runit versus
systemd), C libraries (musl versus glibc), and package formats (.apk versus .deb).
• Contrast this with the BSD operating systems, FreeBSD, OpenBSD, and NetBSD, in which the kernel, the
toolchain, and the user space are combined into a single code base.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 4
Why Kernel ?
* The kernel, is one of the most important elements in the system.
* The kernel has three main objectives:
* to manage resources,
* to interface with hardware, and
* to provide an API that offers a useful level of abstraction to user space
programs
* gives Linux a lot of flexibility in the way it is used
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Why Kernel
• The kernel has three main objectives:
• to manage resources,
• to interface with hardware, and
• to provide an API that offers a useful level of abstraction to user space programs
• Applications running in user space run at a low CPU privilege level.
They only make library calls.
• C library translates these user-space functions, into kernel system calls.
• System call interface is architecture-specific e.g. trap or sw intr, and switches CPU from low-privilege
user mode to high-privilege kernel mode allowing access to all memory addresses and CPU registers.
• The system call handler dispatches the call to the appropriate kernel subsystem:
• memory allocation calls go to the memory manager,
• filesystem calls to the filesystem code, and so on.
• Some calls access underlying hardware and are passed down to a device driver.
• The hardware can itself invoke the kernel by raising an interrupt.
• Interrupts can only be handled in a device driver, never by a user space application.
• All the useful things that an application does, is through the kernel.
• The kernel, is one of the most important elements in the system.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 5
Choosing a kernel
* Choice is between
* use latest version of software or
* use long-term support of the code base, due to the need for handling
vendor-specific additions.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Choosing a Kernel
• Choice is between
• use latest version of software or
• use long-term support of the code base, due to the need for handling vendor-specific additions.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 6
Choosing a kernel
Kernel Development Cycle
¢ Versions
* Before July 2011 - odd numbers (2.1.x, 2.3.x, 2.5.x) were for developers
and even numbers were for end users.
¢ From ver 2.6 on, dev. branch -odd numbers- was dropped, as it slowed
rate of new features available..
* In July 2011 the ver 2.6.39 was bumped to 3.0
* Since then, in April 2015 and March 2019, he bumped the major from 3
to 4 and 4 to 5 respectively
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Kernel Development Cycle
• Linux is developed at a fast pace - a new version being released every 8 to 12 weeks.
• release numbering of kernel version numbers are constructed has changed a bit in recent years.
• Before July 2011, it was a three-number version scheme with version numbers that looked like 2.6.39.
The middle number indicated whether it was a developer or stable release;
odd numbers (2.1.x, 2.3.x, 2.5.x) were for developers and even numbers were for end users.
• From ver 2.6 on, dev. branch -odd numbers- was dropped, as it slowed rate of new features available..
• Then, the jump from 2.6.39 to 3.0 in July 2011 was because Linus felt that numbers were becoming too
large; there was no huge leap in features or architecture of Linux between those two versions.
• Since then, in April 2015 and March 2019, he bumped the major from 3 to 4 and 4 to 5 respectively,
dropping middle number, again purely for neatness, not because of any large architectural shift.
• Linus manages the development kernel tree.
• Follow him by cloning the Git tree: $ git clone git://git.kernel.org/pub/scm/linux/kernel/git/torvalds/linux.git
• This will check out into the subdirectory linux. And, keep up to date by running git pull in that directory.
• a full cycle of kernel dev. has a merge window of 2 weeks, in which Linus accepts patches for new features.
• Code incorporated during the merge window has to be fairly mature.
At the end of merge window, a stabilization phase begins, during which Linus produces weekly release
candidates with version numbers ending in -rc1, -rc2, and so on, usually up to -rc7 or -rc8.
During this time, people test the candidates and submit bug reports and fixes.
When all significant bugs have been fixed, the kernel is released.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 7
Choosing a kernel
Stable and long-term support releases
* The rapid rate of change of Linux is a good thing,
but it does not fit very well
* it brings new features into the mainline code base.
* as compared to the longer life cycle of embedded projects.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Choosing a Kernel
• The rapid rate of change of Linux is a good thing, but it does not fit very well
• it brings new features into the mainline code base.
• as compared to the longer life cycle of embedded projects.
• After the release of a mainline kernel (maintained by Linus Torvalds),
it is moved to the stable tree (maintained by Greg Kroah-Hartman).
• To address this, there are
• stable releases and
• long-term releases.
• Bug fixes are applied to the stable kernel, while the mainline kernel begins the next development cycle.
• Point releases of the stable kernel are marked by a third number, 3.18.1, 3.18.2, and so on.
Before version 3, there were four release numbers, 2.6.29.1, 2.6.39.2, and so on.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 8
Building a kernel
Getting the source
* The rapid rate of change of Linux is a good thing,
but it does not fit very well
* it brings new features into the mainline code base.
* as compared to the longer life cycle of embedded projects.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Getting the source.
• Raspberry Pi 4, BeagleBone Black, and the ARM Versatile PB, are well supported by the mainline kernel
• so use the long-term kernel available at www.kernel.org .
• as compared to the longer life cycle of embedded projects.
$ wget https://cdn.kernel.org/pub/linux/kernel/v5.x/linux-5.4.50.tar.xz
$ tar xf linux-5.4.50.tar.xz
$ mv linux-5.4.50 linux-stable
• There is a lot of code here.
There are over 57,000 files in the 5.4 kernel containing C source code, header files, and assembly code,
amounting to a total of over 14 million lines of code, as measured by the SLOCCount utility.
• worth knowing basic layout of code and to know somewhat, where to look for a particular component.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 9
Building a kernel
Understanding kernel configuration
* The rapid rate of change of Linux is a good thing,
but it does not fit very well
* it brings new features into the mainline code base.
* as compared to the longer life cycle of embedded projects.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Linux kernel configuration.
• suits different reqs, from small, dedicated device such as a smart thermostat to a complex mobile handset.
• there are many thousands of configuration options.
getting config. right is a task itself, but before getting into that, lets see how the configuration works.
Kconfig - config mechanism
• and build system that it integrates with is called Kbuild. both are documented in Documentation/kbuild.
• Kconfig/Kbuild are similarly used in other projects as well .. crosstool-NG, U-Boot, Barebox, and BusyBox.
• configuration options are declared in a hierarchy of files named Kconfig,
it is using a syntax described in Documentation/kbuild/kconfiglanguage.rst.
• the top-level Kconfig looks like this:
mainmenu "Linux/$(ARCH) $(KERNELVERSION) Kernel
Configuration"
comment "Compiler: $(CC_VERSION_TEXT)"
source "scripts/Kconfig.include"
[…]
• And the first line of arch/Kconfig is this:
source "arch/$(SRCARCH)/Kconfig“
• It includes architecture-dependent configuration file, which sources other Kconfig files,
depending on which options are enabled.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 10
Building a kernel
using local kernel versioning
¢ Identify the kernel version and release ..
using make kernelversion and make kernelrelease targets
* If configuration is changed from default, append version information, by
setting CONFIG_LOCALVERSION.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O2
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Using LOCALVERSION to identify a kernel.
• Identify the kernel version and release .. using make kernelversion and make kernelrelease targets:
$ make ARCH=arm kernelversion
5.4.50
$ make ARCH=arm kernelrelease
5.4.50
• It is reported at runtime with uname and is also used in naming directory where kernel modules are stored.
• If configuration is changed from default, append version information, by setting CONFIG_LOCALVERSION.
e.g., if a kernel is marked the -ldd identifier and version 1.0, then define local version in menuconfig:
• Running make kernelversion produces same output as before, but make kernelrelease:
$ make ARCH=arm kernelrelease
5.4.50-melp-v1.0
.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 11
Building a kernel
using kernel modules
¢ Identify the kernel version and release ..
using make kernelversion and make kernelrelease targets
* If configuration is changed from default, append version information, by
setting CONFIG_LOCALVERSION.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O2, O5
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: using kernel modules.
• device and kernel functions are loaded at runtime, depending on hardware detected and features required.
• Without it, every driver and feature has to be statically linked into the kernel, making it infeasibly large.
• Yet, on the other hand, with embedded devices, the hardware and kernel configuration are known at the
time of the kernel build, and therefore modules are not so useful.
• In fact, they could be a problem because they create a version dependency between the kernel and the root
filesystem, which could cause boot failures if one is updated but not the other.
• Therefore, it is quite common for embedded kernels to be built without any modules at all.
• However, there are a few cases where kernel modules are a good idea in embedded systems:
• when there are
• proprietary modules, for the licensing reasons given in the preceding section.
• reduce boot time by deferring the loading of non-essential drivers.
• several drivers to load, and it would take up too much memory to compile them statically.
• e.g. you have a USB interface that supports a range of devices.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 12
Compiling - Kbuild
using kernel modules
¢ Identify the kernel version and release ..
using make kernelversion and make kernelrelease targets
* If configuration is changed from default, append version information, by
setting CONFIG_LOCALVERSION.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O2, O5
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Compiling – Kbuild.
• As before, the kernel build system, Kbuild, is a set of make scripts that take the configuration information
from the .config file, work out the dependencies, and compile everything that is necessary to produce a
kernel image.
• This kernel image contains all the statically linked components, possibly a device tree binary, and possibly
one or more kernel modules.
• The dependencies are expressed in makefiles that are in each directory with buildable components.
• For instance, the following two lines are taken from drivers/char/Makefile:
obj-y += mem.o random.o
obj-$(CONFIG_TTY_PRINTK) += ttyprintk.o
• The obj-y rule unconditionally compiles a file to produce the target, so mem.c and random.c are always part
of the kernel. In the second line, ttyprintk.c is dependent on a configuration parameter.
• If CONFIG_TTY_PRINTK is y, it is compiled as a built-in;
• if it is m, it is built as a module; and
• if the parameter is undefined, it is not compiled at all.
• For most targets, just typing make -with the appropriate ARCH and CROSS_COMPILE,
works, but take it one step at a time.
• See the prior chapter for the meaning of the CROSS_COMPILE make variable.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 13
Compiling - Kbuild
Build artifacts
* vmlinux and
* System.map
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Build artifacts.
• A kernel build generates two files in the top-level directory: vmlinux and System.map.
• The first, vmlinux, is the kernel as an ELF binary. If kernel is compiled with debug enabled
(CONFIG_DEBUG_INFO=y), it will contain debug symbols to be used with debuggers such as kgdb.
• Also use other ELF binary tools, such as size to measure the length of each section (text, data, and bss)
$ arm-cortex_a8-linux-gnueabihf-size vmlinux
text data bss dec hex filename
14005643 7154342 403160 21563145 1490709 vmlinux
• System.map contains the symbol table in a human-readable form.
• Most bootloaders cannot handle ELF code directly.
There is a further stage of processing that takes vmlinux and places binaries in arch/$ARCH/boot that are
suitable for the various bootloaders:
• Image: vmlinux converted to raw binary format.
• zImage: For the PowerPC architecture, this is just a compressed version of Image, which implies that
the bootloader must do the decompression. For all other architectures, the compressed Image is
piggybacked onto a stub of code that decompresses and relocates it.
• uImage: zImage plus a 64-byte U-Boot header.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 14
Compiling device trees
¢ $ make ARCH=arm dtbs
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O7
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Compiling device trees.
• to build the device tree, or trees for a multi-platform build.
• The dtbs target builds device trees according to the rules in arch/$ARCH/boot/dts/Makefile, using the device
tree source files in that directory.
• The following is a snippet from building the dtbs target for multi_v7_defconfig:
$ make ARCH=arm dtbs
[…]
DTC arch/arm/boot/dts/alpine-db.dtb
DTC arch/arm/boot/dts/artpec6-devboard.dtb
DTC arch/arm/boot/dts/at91-kizbox2.dtb
DTC arch/arm/boot/dts/at91-nattis-2-natte-2.dtb
DTC arch/arm/boot/dts/at91-sama5d27_som1_ek.dtb
[…]
• The compiled .dtb files are generated in the same directory as the sources.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 15
Compiling modules
$ make -j 4 ARCH=arm CROSS_COMPILE=arm-cortex_a8-linux-gnueabihf-
modules
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O7
AI Layer: L1-BuildAssistant
Notes: Compiling modules.
• If some features are to be built as modules, build them separately using the modules target:
$ make -j 4 ARCH=arm CROSS_COMPILE=arm-cortex_a8-linux-gnueabihf- modules
• The compiled modules have a .ko suffix and are generated in the same directory as the source code,
meaning that they are scattered all around the kernel source tree.
• Finding them is a little tricky, but use the modules_install make target to install them in the right place.
• The default location is /lib/modules in your development system, which is certainly not what should be.
• To install them in the staging area of a root filesystem provide the path using INSTALL_MOD_PATH:
$ make -j4 ARCH=arm CROSS_COMPILE=arm-cortex_a8-linux-gnueabihf-
INSTALL_MOD_PATH=$HOME/rootfs modules_install
• Kernel modules are put into the /lib/modules/[kernel version] directory, relative to the root of the filesystem.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 16
Cleaning kernel sources
* make clean
* make mrproper
¢ make distclean
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Cleaning kernel sources.
• here are the three make targets for cleaning the kernel source tree:
• clean: Removes object files and most intermediates.
• mrproper: Removes all intermediate files, including the .config file. Use this target to return the source
tree to the state it was in immediately after cloning or extracting the source code. If you are curious
about the name, Mr. Proper is a cleaning product common in some parts of the world. The meaning of
make mrproper is to give the kernel sources a really good scrub.
• distclean: This is the same as mrproper, but also deletes editor backup files, patch files, and other
artifacts of software development.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 17
Building a 64-bit kernel for the
Raspberry Pi 4
* there is already support for the Raspberry Pi 4 in the mainline kernel:
Or, use as the author notes
+ Raspberry Pi Foundation's fork of Linux
https://github.com/raspberrypillinux at it is more stable.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O7
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Building a 64-bit kernel for the Raspberry Pi 4.
• there is already support for the Raspberry Pi 4 in the mainline kernel:
• also, the author notes Raspberry Pi Foundation's fork of Linux https://github.com/raspberrypi/linux is more
stable.
• The 4.19.y branch of that fork is also more actively maintained than that same fork's rpi-5.4.y branch.
• Since the Raspberry Pi 4 has a 64-bit quad core ARM Cortex-A72 CPU, use a GNU toolchain from Arm that
targets AArch64 GNU/Linux to crosscompile a 64-bit kernel for it.
• This prebuilt toolchain can be downloaded from
https://developer.arm.com/tools-and-software/open-source-software/developertools/
gnu-toolchain/gnu-a/downloads:
$ cd ~
$ wget https://developer.arm.com/-
/media/Files/downloads/gnu-a/10.2-2020.11/binrel/gcc-arm-10.2-2020.11-x86_64-aarch64-none-linux-
gnu.tar.xz
$ tar xf gcc-arm-10.2-2020.11-x86_64-aarch64-nonelinux-gnu.tar.xz
$ mv gcc-arm-10.2-2020.11-x86_64-aarch64-none-linuxgnu gcc-arm-aarch64-none-linux-gnu
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 18
Building a kernel for the
BeagleBone Black
« here is the complete sequence of commands to build a kernel, the modules, and a
device tree for the BeagleBone Black, using the crosstool-NG ARM Cortex A8 cross
compiler:
$ cd linux-stable
$ make ARCH=arm CROSS_COMPILE=arm-cortex_a8-linuxgnueabihf-mrproper
$ make ARCH=arm multi_v7_defconfig
$ make -j4 ARCH=arm CROSS_COMPILE=arm-cortex_a8-linux-gnueabihf-zlmage
$ make -j4 ARCH=arm CROSS_COMPILE=arm-cortex_a8-linux-gnueabihf-modules
$ make ARCH=arm CROSS_COMPILE=arm-cortex_a8-linuxgnueabihf-dtbs
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O3, O7
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Building a kernel for the BeagleBone Black.
• here is the complete sequence of commands to build a kernel, the modules, and a device tree for the
BeagleBone Black, using the crosstool-NG ARM Cortex A8 cross compiler:
$ cd linux-stable
$ make ARCH=arm CROSS_COMPILE=arm-cortex_a8-linuxgnueabihf-mrproper
$ make ARCH=arm multi_v7_defconfig
$ make -j4 ARCH=arm CROSS_COMPILE=arm-cortex_a8-linux-gnueabihf-zImage
$ make -j4 ARCH=arm CROSS_COMPILE=arm-cortex_a8-linux-gnueabihf-modules
$ make ARCH=arm CROSS_COMPILE=arm-cortex_a8-linuxgnueabihf-dtbs
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 19
Building a kernel for the
QEMU
* Here is the sequence of commands to build Linux for the ARM Versatile PB that is
emulated by QEMU, using the crosstool-NG v5TE compiler:
$ cd linux-stable
$ make ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-mrproper
$ make -j4 ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-zlmage
$ make -j4 ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-modules
$ make ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-dtbs
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O3, O7
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Building a kernel for the QEMU.
• Here is the sequence of commands to build Linux for the ARM Versatile PB that is emulated by QEMU,
using the crosstool-NG v5TE compiler:
$ cd linux-stable
$ make ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-mrproper
$ make -j4 ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-zImage
$ make -j4 ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-modules
$ make ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-dtbs
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 20
Booting the kernel
* Here is the sequence of commands to build Linux for the ARM Versatile PB that is
emulated by QEMU, using the crosstool-NG v5TE compiler:
$ cd linux-stable
$ make ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-mrproper
$ make -j4 ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-zlmage
$ make -j4 ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-modules
$ make ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-dtbs
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O3, O7
Build Path: toolchain
AI Layer: L1-BuildAssistant
Notes: Booting the kernel.
• Booting Linux is highly device-dependent.
• We will see how it works for the Raspberry Pi 4, BeagleBone Black, and QEMU.
• For other target boards, consult the information from vendor or from the community project, if there is one.
• At this point, we have the kernel image files and the device tree blobs for the Raspberry Pi 4, BeagleBone
Black, and QEMU.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 21
Booting the Raspberry Pi 4
* Raspberry Pis use a proprietary bootloader provided by Broadcom instead of
UBoot.
¢ Unlike previous Raspberry Pi models, the Raspberry Pi 4's bootloader
resides on an onboard SPI EEPROM rather than on a microSD card.
* Still need to put the kernel image and device tree blobs for the Raspberry Pi
4 ona microSD to boot the 64-bit kernel.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O7
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Booting the Raspberry Pi 4.
• Raspberry Pis use a proprietary bootloader provided by Broadcom instead of UBoot.
• Unlike previous Raspberry Pi models, the Raspberry Pi 4's bootloader resides on an onboard SPI EEPROM
rather than on a microSD card.
• Still need to put the kernel image and device tree blobs for the Raspberry Pi 4 on a microSD to boot the
64-bit kernel.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 22
Booting the BeagleBone Black
* need a microSD card with U-Boot installed, as described in the Installing U-
Boot section.
* Insert the microSD card into a card reader and from the linux-stable directory,
* copy the arch/arm/boot/zImage and arch/arm/boot/dts/am335x-boneblack.dtb
files to the boot partition.
¢ Unmount the card and insert it into the BeagleBone Black.
* Start a terminal emulator, such as gtkterm, and be prepared to press the
spacebar as soon as the U-Boot messages appear.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O6, O7
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Booting the BeagleBone Black.
• To begin, need a microSD card with U-Boot installed, as described in the Installing U-Boot section.
• Insert the microSD card into a card reader and from the linux-stable directory,
• copy the arch/arm/boot/zImage and arch/arm/boot/dts/am335x-boneblack.dtb files to the boot partition.
• Unmount the card and insert it into the BeagleBone Black.
• Start a terminal emulator, such as gtkterm, and be prepared to press the spacebar as soon as the U-Boot
messages appear.
• Next, power on the BeagleBone Black and press the space bar.
• It should show a U-Boot prompt. .
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 23
Booting QEMU
* Raspberry Pis use a proprietary bootloader provided by Broadcom instead of
UBoot.
¢ Unlike previous Raspberry Pi models, the Raspberry Pi 4's bootloader
resides on an onboard SPI EEPROM rather than on a microSD card.
* Still need to put the kernel image and device tree blobs for the Raspberry Pi
4 ona microSD to boot the 64-bit kernel.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O7
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: Booting the BeagleBone Black.
• Assuming that qemu-system-arm is already installed, launch it with the kernel and the .dtb file for the ARM
Versatile PB, as follows:
$ QEMU_AUDIO_DRV=none \
qemu-system-arm -m 256M -nographic -M versatilepb -
kernel \ zImage
-append "console=ttyAMA0,115200" -dtb versatilepb.
dtb
• Note that setting QEMU_AUDIO_DRV to none is just to suppress error messages from QEMU about
missing configurations for the audio drivers, which is not used.
• As with the Raspberry Pi 4 and BeagleBone Black, this will end with kernel panic and the system will halt.
• To exit from QEMU, press Ctrl + A and then x (two separate keystrokes).
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 24
Kernel panic
* Kernel panic occurs when the kernel encounters an unrecoverable error.
+ By default, it will print out a message to the console and then halt.
* Or, reboot
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Kernel Panic.
• Kernel panic occurs when the kernel encounters an unrecoverable error.
• By default, it will print out a message to the console and then halt.
• You can set the panic command-line parameter to allow a few seconds before reboots following a panic.
• In this case, the unrecoverable error is no root filesystem, illustrating that a kernel is useless without a user
space to control it.
• Fix by providing a root filesystem, either as a ramdisk or on a mountable mass storage device.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 25
The kernel command line
* Kernel panic occurs when the kernel encounters an unrecoverable error.
+ By default, it will print out a message to the console and then halt.
* Or, reboot
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: The kernel command line.
• The kernel command line is a string that is passed to the kernel by the bootloader, via the bootargs variable
in the case of U-Boot; it can also be defined in the device tree or set as part of the kernel configuration in
CONFIG_CMDLINE.
• Some examples of the kernel command line are seen already, but there are many more.
• Here is a shorter list of the most useful ones, with a complete list in Documentation/kernelparameters.txt.
• debug: Sets console log level to highest level, 8, to ensure that all kernel messages are seen on console.
• init=: The init program to run from a mounted root filesystem, which defaults to /sbin/init.
• lpj=: Sets loops_per_jiffy to a given constant. There is a description of the significance of this below.
• panic=: Behavior when kernel panics: if greater than zero, it gives the number of seconds before rebooting;
if it is zero, it waits forever (this is the default); or if it is less than zero, it reboots without any delay.
• quiet: Sets console log level to silent, suppressing all but emergency messages. Since most devices have a
serial console, it takes time to output all strings. So, reducing #messages with this option reduces boot time.
• rdinit=: The init program to run from a ramdisk. It defaults to /init.
• ro: Mounts the root device as read-only. Has no effect on a ramdisk, which is always read/write.
• root=: The device on which to mount the root filesystem.
• rootdelay=: The number of seconds to wait before trying to mount the root device; defaults to zero. Useful
if the device takes time to probe the hardware, but also see rootwait.
• rootfstype=: The filesystem type for the root device. In many cases, it is auto-detected during mount, but it
is required for jffs2 filesystems.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 26
Building a Root FS
* Kernel panic occurs when the kernel encounters an unrecoverable error.
+ By default, it will print out a message to the console and then halt.
* Or, reboot
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: Building a Root FS.
• The techniques described here are broadly known as roll your own or RYO.
• Back in the early days of embedded Linux, this was the only way to create a root filesystem.
• There are still some use cases where an RYO root filesystem is applicable, for example, when the
amount of RAM or storage is very limited, for quick demonstrations, or for any case in which your
requirements are not (easily) covered by the standard build system tools.
• These cases are quite rare.
• the purpose of this chapter is educational; it is not meant to be a recipe for building everyday embedded
systems: use the tools described in the next chapter for this.
• The first objective is to create a minimal root filesystem that will give us a shell prompt.
• Then, using this as a base, add scripts to start up other programs and configure a network interface and
user permissions.
• There are worked examples for both the BeagleBone Black and QEMU targets.
• Knowing how to build the root filesystem from scratch is a useful skill, and it will help to understand what is
going on when we look at more complex examples in later.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 27
What should be in the root filesystem?
* The kernel gets a root filesystem, either as an initramfs passed as a pointer
from the bootloader or by mounting the block device given on the kernel
command line by the root= parameter.
* Once it has a root filesystem, the kernel will execute the first program, by
default named init, as earlier.
¢ Then, as far as the kernel is concerned, its job is complete.
* need these components - to make a minimal root filesystem:
It is now up to the init program to begin starting other programs and bring the
system to life.
e httns://hootlin com/doc/training/ambedded-linuy/ambedded-linuy-clides ndf
Outcomes: O6
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: What should be in the root filesystem?
• The kernel gets a root filesystem, either as an initramfs passed as a pointer from the bootloader or by
mounting the block device given on the kernel command line by the root= parameter.
• Once it has a root filesystem, the kernel will execute the first program, by default named init, as earlier.
• Then, as far as the kernel is concerned, its job is complete. It is now up to the init program to begin starting
other programs and bring the system to life.
• need these components - to make a minimal root filesystem:
• init: This is the program that starts everything off, usually by running a series of scripts.
• shell: need a shell for a command prompt but,, also to run shell scripts called by init and other programs.
• daemons: A daemon is a background program to provide service to others. e.g. system log (syslogd) and
secure shell (sshd). The init program starts initial set of daemons to support main system applications. In
fact, init is itself a daemon: it is the daemon that provides the service of launching other daemons.
• shared libraries: Most programs are linked with shared libraries and so they must be present in root fs.
• configuration files: configs for init and other daemons is stored in text files, usually in /etc directory.
• device nodes: These are the special files that give access to various device drivers.
• proc and sys: These two pseudo filesystems represent kernel data structures as a hierarchy of directories
and files. Many programs and library functions depend on /proc and /sys.
• kernel modules: if some parts of kernel are configured aw modules, they are installed in the root filesystem,
usually in /lib/modules/[kernel version].
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 28
root filesystem
the directory layout
* The kernel gets a root filesystem, either as an initramfs passed as a pointer
from the bootloader or by mounting the block device given on the kernel
command line by the root= parameter.
* Once it has a root filesystem, the kernel will execute the first program, by
default named init, as earlier.
¢ Then, as far as the kernel is concerned, its job is complete.
* need these components - to make a minimal root filesystem:
It is now up to the init program to begin starting other programs and bring the
system to life.
e httns://hootlin com/doc/training/ambedded-linuy/ambedded-linuy-clides ndf
Outcomes: O6
Build Path: bootloader
AI Layer: L1-BuildAssistant
Notes: the directory layout
• Linux kernel does not care about file and dir layouts beyond that named by init= or rdinit=.
• As an example, compare file layout of Android to that of a Linux distribution: they are completely different.
• However, files are expected to be in certain places, and it helps developers if devices use a similar layout.
• The basic layout of most Linux systems is defined in the Filesystem Hierarchy Standard (FHS), available at
https://refspecs.linuxfoundation.org/fhs.shtml.
• The FHS covers all the implementations of Linux operating systems, from the largest to the smallest.
• Embedded devices tend to use a subset based on their needs, but it usually includes the following:
/bin: Programs essential for all users
/dev: Device nodes and other special files
/etc: System configuration files
/lib: Essential shared libraries, for example, those that make up the C library
/proc: Information about processes represented as virtual files
/sbin: Programs essential to the system administrator
/sys: Information about devices and their drivers represented as virtual files
/tmp: A place to put temporary or volatile files
/usr: Additional programs, libraries, and admin utils, in /usr/bin, /usr/lib, and /usr/sbin directories,
/var: A hierarchy of files and directories that may be modified at runtime, for example, log messages,
some of which must be retained after boot
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 29
Why Busybox?
¢ Even for a basic root filesystem, the shell needs approximately 50
utilities, which presents two problems.
¢ Firstly, tracking down the source code for each one and cross-
compiling it would be quite a big job.
* Secondly, the resulting collection of programs would take up several
tens of megabytes, which was a real problem in the early days of
embedded Linux when a few megabytes was all that was available.
* To solve this problem, BusyBox was created.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O6
Build Path: rootfs
Notes: Why Busybox?
The shell is a way of launching other programs, and a shell script is little more than a list of programs to run,
with some flow control and a means of passing information between programs.
• To make a shell useful, it needs the utility programs that the Unix command line is based on.
• Even for a basic root filesystem, it needs approximately 50 utilities, which presents two problems.
• Firstly, tracking down the source code for each one and cross-compiling it would be quite a big job.
• Secondly, the resulting collection of programs would take up several tens of megabytes, which was a
real problem in the early days of embedded Linux when a few megabytes was all that was available.
• To solve this problem, BusyBox was created.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 30
Busybox
Introduction
* a typical installation of BusyBox is that of a single program with a
symbolic link for each applet, but it behaves exactly as if it were a
collection of individual applications.
* BusyBox has over 300 applets, including an init program, several shells
of varying levels of complexity, and utilities for most admin tasks.
* There is even a simple version of the vi editor so you can change text
files on your device.
* A typical BusyBox binary will only enable several dozen applets.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O1, O4, O6
Build Path: rootfs
AI Layer: L1-BuildAssistant
Notes: Why Busybox?
• Early BusyBox had nothing to do with embedded Linux.
• project started in 1996 by Bruce Perens for Debian installer to boot Linux from a 1.44 MB floppy disk.
• this was about size of storage on embedded devices, and so embedded Linux community quickly took it up.
• BusyBox has been at the heart of embedded Linux ever since.
• It was written from scratch to perform the essential functions of the essential Linux utilities.
• The developers used 80:20 rule: most useful 80% of program is implemented in 20% of the code.
• Hence, BusyBox tools implement a subset of functions of desktop equivalents, but they do enough of it to
be useful in the majority of cases.
• BusyBox employs combines all the tools together into a single binary, making it easy to share code between
them.
• It works like this: BusyBox is a collection of applets, each of which exports a main function in the form
[applet]_main.
• For example, the cat command is implemented in coreutils/cat.c and exports cat_main. The main function of
BusyBox itself dispatches the call to the correct applet, based on the command-line arguments.
• launch BusyBox with the name of the applet to run, followed by any arguments the applet expects:
$ busybox cat my_file.txt
• A better way to get BusyBox to run cat applet is to create a symbolic link from /bin/cat to /bin/busybox:
$ ls -l bin/cat bin/busybox
-rwxr-xr-x 1 root root 892868 Feb 2 11:01 bin/busybox
lrwxrwxrwx 1 root root 7 Feb 2 11:01 bin/cat -> busybox
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 31
Busybox
Building BusyBox
* a typical installation of BusyBox is that of a single program with a
symbolic link for each applet, but it behaves exactly as if it were a
collection of individual applications.
* BusyBox has over 300 applets, including an init program, several shells
of varying levels of complexity, and utilities for most admin tasks.
* There is even a simple version of the vi editor so you can change text
files on your device.
* A typical BusyBox binary will only enable several dozen applets.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O4, O6
Build Path: rootfs
AI Layer: L1-BuildAssistant
Notes: Building Busybox
• BusyBox uses the same Kconfig and Kbuild system as the kernel, so crosscompiling is straightforward.
• Get the source by cloning the BusyBox Git repo and checking out the version needed :
$ git clone git://busybox.net/busybox.git
$ cd busybox
$ git checkout 1_31_1
• or download the corresponding TAR file from
https://busybox.net/downloads/.
• Then, configure BusyBox by starting with default config, to enable almost all the features of BusyBox:
$ make distclean
$ make defconfig
• At this point, run make menuconfig to fine-tune the configuration.
• For example, set the install path in Busybox Settings | Installation Options (CONFIG_PREFIX) to point to
the staging directory.
• Then, you can cross-compile in the usual way.
• If the intended target is the BeagleBone Black, use this command:
$ make ARCH=arm CROSS_COMPILE=arm-cortex_a8-linuxgnueabihfIf
• or, if the intended target is the QEMU emulation of a Versatile PB, use this command:
$ make ARCH=arm CROSS_COMPILE=arm-unknown-linuxgnueabi-
• In either case, the result is the executable busybox.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 32
Libraries for the root filesystem
* a typical installation of BusyBox is that of a single program with a
symbolic link for each applet, but it behaves exactly as if it were a
collection of individual applications.
* BusyBox has over 300 applets, including an init program, several shells
of varying levels of complexity, and utilities for most admin tasks.
* There is even a simple version of the vi editor so you can change text
files on your device.
* A typical BusyBox binary will only enable several dozen applets.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O4, O6
Build Path: rootfs
AI Layer: L1-BuildAssistant
Notes: Libraries for the root filesystem
• Programs are linked with libraries.
• Link them all statically, in which case, there would be no libraries on the target device.
• But, this takes up an unnecessarily large amount of storage if there are more than two or three programs.
So, there is the need to copy shared libraries from the toolchain to the staging directory.
• How do you know which libraries?
• One option is to copy all of the .so files from the sysroot directory of the toolchain. Instead of trying to
predict which libraries to include, just assume that the image will eventually need them all. This is
certainly logical and, if the need is for creating a platform to be used by others for a range of
applications, it would be the correct approach. Be aware, though, that a full glibc is quite large.
In the case of a crosstool-NG build of glibc 2.22, the libraries, locales, and other supporting files come to
33 MiB. Of course, cut down on that considerably using musl libc or uClibc-ng.
• Another option is to cherry-pick only those libraries that you require, for which you need a means of
discovering library dependencies.
• Use the readelf command for this task:
$ cd ~/rootfs
$ arm-cortex_a8-linux-gnueabihf-readelf -a
bin/busybox | grep "program interpreter"
[Requesting program interpreter: /lib/ld-linuxarmhf.so.3]
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 33
Libraries for the root filesystem
* a typical installation of BusyBox is that of a single program with a
symbolic link for each applet, but it behaves exactly as if it were a
collection of individual applications.
* BusyBox has over 300 applets, including an init program, several shells
of varying levels of complexity, and utilities for most admin tasks.
* There is even a simple version of the vi editor so you can change text
files on your device.
* A typical BusyBox binary will only enable several dozen applets.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O4, O6
Build Path: rootfs
AI Layer: L1-BuildAssistant
Notes: Device nodes
• Most devices in Linux are represented by device nodes,
• in accordance with the Unix philosophy that everything is a file (except network interfaces, which are
sockets).
• A device node may refer to a block device or a character device.
• Block devices are mass storage devices, such as SD cards or hard drives.
• A character device is pretty much anything else, once again, with the exception of network interfaces.
• The conventional location for device nodes is the directory called /dev.
• For example, a serial port may be represented by the device node called /dev/ttyS0.
• Device nodes are created using the program named mknod (short for make node):
mknod <name> <type> <major> <minor>
• The parameters to mknod are as follows:
• name is the name of the device node that you want to create.
• type is either c for character devices or b for a block device.
• major and minor are a pair of numbers that are used by the kernel to route file requests to the
appropriate device driver code.
• There is a list of standard major and minor numbers in kernel sources in the Documentation/devices.txt file.
• To create device nodes for all the devices you want to access on a system, do so manually using the mknod
command or create them automatically at runtime using one of the device managers
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 34
proc and sysfs filesystems
* a typical installation of BusyBox is that of a single program with a
symbolic link for each applet, but it behaves exactly as if it were a
collection of individual applications.
* BusyBox has over 300 applets, including an init program, several shells
of varying levels of complexity, and utilities for most admin tasks.
* There is even a simple version of the vi editor so you can change text
files on your device.
* A typical BusyBox binary will only enable several dozen applets.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O4, O6
Build Path: rootfs
AI Layer: L1-BuildAssistant
Notes: proc and sysfs filesystems
• proc and sysfs are two pseudo filesystems that give a window into the inner workings of the kernel.
• They both represent kernel data as files in a hierarchy of directories: when you read one of the files, the
contents you see do not come from disk storage; it has been formatted on the fly by a function in the kernel.
• Some files are also writable, meaning if it is of the correct format and you have sufficient permissions, it will
modify the value stored in the kernel's memory.
• In other words, proc and sysfs provide another way to interact with device drivers and other kernel code.
The proc and sysfs filesystems should be mounted on the directories called /proc and /sys:
# mount -t proc proc /proc
# mount -t sysfs sysfs /sys
• Although they are very similar in concept, they perform different functions.
• proc has been part of Linux since the early days. Its original purpose was to expose information about
processes to the user space, hence the name. To this end, there is a directory for each process named
/proc/<PID>, which contains information about its state. The process list command, ps, reads these files
to generate its output. In addition, there are files that give information about other parts of the kernel, for
example, /proc/cpuinfo tells you about the CPU, /proc/interrupts has information about interrupts, and so
on. Finally, in /proc/sys, there are files that display and control the state and behavior of kernel
subsystems, especially scheduling, memory management, and networking. The manual page is the best
reference for the files you will find in the proc directory, which you can see by typing man 5 proc.
• On the other hand, the role of sysfs is to present the kernel driver model to the user space. It exports a
hierarchy of files relating to devices and device drivers and the way they are connected to each other.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 35
Mounting filesystems
* a typical installation of BusyBox is that of a single program with a
symbolic link for each applet, but it behaves exactly as if it were a
collection of individual applications.
* BusyBox has over 300 applets, including an init program, several shells
of varying levels of complexity, and utilities for most admin tasks.
* There is even a simple version of the vi editor so you can change text
files on your device.
* A typical BusyBox binary will only enable several dozen applets.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O4, O6
Build Path: rootfs
AI Layer: L1-BuildAssistant
Notes: Mounting filesystems
• The mount command allows to attach one fs to a directory within another, forming a hierarchy of fs.
• The one at the top, which was mounted by the kernel when it booted, is called the root filesystem.
• The format of the mount command is as follows:
mount [-t vfstype] [-o options] device directory
• The parameters of mount are as follows:
vfstype is the type of filesystem.
options is a comma-separated list of mount options.
device is the block device node the filesystem resides on.
directory is the directory you want to mount the filesystem on.
• There are various options you can give after -o; have a look at the manual page mount(8) for more
information. As an example, if you wanted to mount an SD card containing an ext4 filesystem in the first
partition onto the directory called /mnt, you would type the following code:
# mount -t ext4 /dev/mmcblk0p1 /mnt
• Assuming the mount succeeds, you would be able to see the files stored on the SD card in the /mnt
directory. In some cases, you can leave out the filesystem type and let the kernel probe the device to find
out what is stored there. If mounting fails, you may first need to unmount the partition in case your Linux
• distro is configured to automount all the partitions on an SD card when it is inserted.
• Looking at the example of mounting the proc filesystem, there is something odd: there is no device node,
such as /dev/proc, since it is a pseudo filesystem and not a real one.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 36
Transferring the root filesystem to the target
* initramfs.
¢ disk image.
¢ network filesystem.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O2, O4, O6
Build Path: rootfs
Notes: Transferring the root filesystem to the target
After creating a skeleton root filesystem in a staging directory, the next task is to transfer it to the target. There
are three possibilities:
• initramfs: Also known as a ramdisk,
it is a filesystem image that is loaded into RAM by the bootloader.
Ramdisks are easy to create and have no dependencies on mass storage drivers.
They can be used in fallback maintenance mode when the main root filesystem needs updating.
They can even be used as the main root filesystem in small embedded devices, and they are commonly
used as the early user space in mainstream Linux distributions.
As the contents of the root filesystem are volatile, and any changes made in the root filesystem at
runtime will be lost when the system next boots.
It would need another storage type to store permanent data such as configuration parameters.
• Disk image:
It is a copy of the root filesystem formatted and ready to be loaded onto a mass storage device on the
target. For example, it could be an image in the ext4 format ready to be copied onto an SD card, or it
could be in the jffs2 format ready to be loaded into flash memory via the bootloader.
Creating a disk image is the most common option.
• Network filesystem:
Staging directory is exported to the network via an NFS server and mounted by the target at boot time.
This is common during the development phase, in preference to repeated cycles of creating a disk
image and reloading it onto the mass storage device, which is quite a slow process.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 37
Transferring the root filesystem to the target
Creating a boot initramfs
* initramfs.
¢ disk image.
¢ network filesystem.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O2, O4, O6
Build Path: rootfs
Notes: Creating a boot initramfs
• An initial RAM filesystem, or initramfs, is a compressed cpio archive.
• cpio is an old Unix archive format, but easier to decode and so requiring less code in the kernel.
• configure kernel with CONFIG_BLK_DEV_INITRD to support initramfs.
• there are three different ways to create a boot ramdisk:
• as a standalone cpio archive,
• as a cpio archive embedded in the kernel image, and
• as a device table
that the kernel build system processes as part of the build.
• The first option gives the most flexibility because kernels and ramdisks can be mixed and matched.
However, it means that there are two files to deal with instead of one, and not all bootloaders have the
facility to load a separate ramdisk.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 38
The init program
* initramfs.
* disk image.
* network filesystem.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O6
Build Path: rootfs
Notes: The init program
• Running a shell, or even a shell script, at boot time is fine for simple cases, but really you need something
more flexible.
• Normally, Unix systems run a program called init that starts up and monitors other programs.
• Over the years, there have been many init programs. For now, looking at the init program from BusyBox.
• The init program begins by reading the configuration file, /etc/inittab.
• Here is a simple example that is adequate for our needs:
::sysinit:/etc/init.d/rcS
::askfirst:-/bin/ash
• The first line runs a shell script, rcS, when init is started.
• The second line prints the message Please press Enter to activate this console to the console and starts a
shell when you press Enter.
• The leading - before /bin/ash means that it will become a login shell, which sources /etc/profile and
$HOME/.profile before giving the shell prompt.
• One of the advantages of launching the shell like this is that job control is enabled.
• The most immediate effect is that you can use Ctrl + C to terminate the current program.
• Maybe it wasn’t noticed it before, but when the ping program is run and find you can't stop it!
• BusyBox init provides a default inittab if none is present in the root filesystem.
• It is a little more extensive than the preceding one.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 39
Configuring user accounts
* initramfs.
* disk image.
* network filesystem.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O6
Build Path: rootfs
Notes: Configuring user accounts
• It is not good practice to run all programs as root, since if one program is compromised by an outside
attack, then the whole system is at risk.
• It is preferable to create unprivileged user accounts and use them where full root is not necessary.
• Usernames are configured in /etc/passwd.
It has one line per user, with seven fields of information separated by colons, which are, in order following:
login name
hash code used to verify the password or, more usually, an x to indicate that the password is stored in
/etc/shadow
user ID
group ID
comment field, often left blank
user's home directory
shell this user will use (optional)
• Here is a simple example in which we have user root with UID 0 and user daemon with UID 1:
root:x:0:0:root:/root:/bin/sh
daemon:x:1:1:daemon:/usr/sbin:/bin/false
• Setting the shell for user daemon to /bin/false ensures that any attempt to log on with that name will fail.
• Various programs have to read /etc/passwd in order to look up usernames and UIDs, and so the file has to
be world-readable.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 40
managing device nodes
* initramfs.
* disk image.
* network filesystem.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O6
Build Path: rootfs
Notes: managing device nodes
• Creating device nodes statically with mknod is quite hard work and inflexible.
• There are other ways to create device nodes automatically on demand:
devtmpfs: This is a pseudo filesystem that you mount over /dev at boot time. The kernel populates it
with device nodes for all the devices that the kernel currently knows about, and it creates nodes for new
devices as they are detected at runtime. The nodes are owned by root and have default permissions of
0600. Some well-known device nodes, such as /dev/null and /dev/random, override the default to 0666.
To see exactly how this is done, take a look at the Linux source file drivers/char/mem.c and see how
struct memdev is initialized.
mdev: This is a BusyBox applet that is used to populate a directory with device nodes and to create new
nodes as needed. There is a configuration file, /etc/mdev.conf, which contains rules for ownership and
the mode of the nodes.
udev: This is the mainstream equivalent of mdev. You will find it on desktop Linux and in some
embedded devices. It is very flexible and a good choice for higher-end embedded devices. It is now part
of systemd.
• Although both mdev and udev create the device nodes themselves, it is easier to just let devtmpfs do the
job and use mdev/udev as a layer on top to implement the policy for setting ownership and permissions.
The devtmpfs approach is the only maintainable way to generate device nodes prior to user space startup.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 41
configuring the network
* initramfs.
* disk image.
* network filesystem.
+ https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Outcomes: O6
Build Path: rootfs
Notes: Configuring the network
• Next, let's look at some basic network configurations so that to communicate with the outside world.
• Assume that there is an Ethernet interface, eth0, and that it only needs a simple IPv4 configuration.
• These examples use the network utilities that are part of BusyBox, and they are sufficient for a simple use
case, using the old-but-reliable ifup and ifdown programs.
• The main network configuration is stored in /etc/network/interfaces.
need to create these directories in the staging directory:
etc/network
etc/network/if-pre-up.d
etc/network/if-up.d
var/run
• For a static IP address, /etc/network/interfaces would look like this:
auto lo
iface lo inet loopback
auto eth0
iface eth0 inet static
address 192.168.1.101
netmask 255.255.255.0
network 192.168.1.0
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 42
Summary Notes
* Kernel Build.
* Root Filesystem.
Further reading
* So You Want to Build an Embedded Linux System? by Jay Carlson:
https://jaycarlson.net/embedded-linux/
¢ Linux Kernel Development, Third Edition, by Robert Love
¢ Linux Weekly News: https://Iwn.net
¢ BeagleBone Forum: https://beagleboard.org/discuss#bone forum embed
¢ Raspberry Pi Forums: https://www.raspberrypi.org/forums/
Outcomes: O6, O7
Build Path: kernel
AI Layer: L1-BuildAssistant
Notes: 1. What makes Linux so powerful is the ability to configure the kernel however needed.
2. The definitive place to get the kernel source code is https://www.kernel.org/ ,
but the source will need to be obtained for a particular SoC or board from the vendor of that device or a third
party that supports that device.
3. The customization of the kernel for a particular target may consist of changes to the core kernel code,
additional drivers for devices that are not in mainline Linux, a default kernel configuration file, and a device
tree source file.
4. Normally, start with the default configuration for your target board and then tweak it by running one of the
configuration tools, such as menuconfig. One of the things to consider at this point is whether the kernel
features and drivers should be compiled as modules or built in. Kernel modules are usually no great
advantage for embedded systems, where the feature set and hardware are usually well defined. However,
modules are often used as a way to import proprietary code into the kernel, and also to reduce boot time by
loading nonessential drivers after booting.
5. Building the kernel produces a compressed kernel image file named zImage , bzImage, or uImage,
depending on the bootloader you will be using and the target architecture. A kernel build will also generate
any kernel modules (as .ko files) that you have configured, and device tree binaries (as .dtb files) if
yourtarget requires them.
6. The kernel is the core of a Linux-based system, but it cannot work by itself. It requires a root filesystem that
contains the user space components. The root filesystem can be a ramdisk or a filesystem accessed via a
block device

## Slide 43
Quiz
Canvas
¢ 10 Questions
¢ 45 Mins
¢ 6 Attempts
¢ Highest Retained

## Slide 44
Assignment
1. Setup buildroot for your target
example 2/2a/2b for rpi4/rpi3B+/rpi3B
in the zip file.
2. Copy to SD Card and boot up the Rpi.
3. Submit screenshot of the build and run.
Outcomes: O2, O7
AI Layer: L1-BuildAssistant
Notes: Assignment
1. Setup buildroot for your target
example 2/2a/2b for rpi4/rpi3B+/rpi3B
in the zip file.
2. Copy to SD Card and boot up the Rpi.
3. Submit screenshot of the build and run.

## Slide 45
Summary
In This Chapter
¢ Storage Strategy — flash memory, fs for flash memory
* Assignment
* Quiz
Notes: CHAPTER OVERVIEW
In This Chapter, We Discussed
1. Storage Strategy – flash memory, fs for flash memory
2. Assignment
3. Quiz
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 46
Summary
In This Chapter
¢ Overview of Embedded Linux Systems
* Introduction to Embedded Linux Systems
¢ Examples of Embedded Linux Systems
¢ Hardware for Embedded Linux Systems
* System Architecture of Embedded Linux Systems
* Environment for Embedded Linux Systems Development
* No Assignment
* Quiz
Outcomes: O1
Notes: CHAPTER OVERVIEW
In This Chapter, We saw
1. Overview of Embedded Linux Systems
2. Introduction to Embedded Linux Systems
3. Examples of Embedded Linux Systems
4. Hardware for Embedded Linux Systems
5. System Architecture of Embedded Linux Systems
6. Environment for Embedded Linux Systems Development
7. No Assignment
8. Quiz