## Slide 1
Linux Systems Programming
Notes: After the kernel has booted
• Introducing init: BusyBox init, System V init ,system
• Using BusyBox runit
• Using Processes & Threads: Understanding Scheduling and IPC
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 2
Chapter Objectives
In This Chapter
¢ Introducing init: BusyBox init, System V init, systemd
¢ Using BusyBox runit
* Using Processes & Threads: Understanding Scheduling and IPC
¢ Assignment
* Quiz
Notes: CHAPTER OVERVIEW
In This Chapter, We Will Discuss
1. Introducing init: BusyBox init, System V init, systemd
2. Using BusyBox runit
3. Using Processes & Threads: Understanding Scheduling and IPC
4. Assignment
5. Quiz
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 3
Why init?
init
* why it is so important to the rest of the system.
* many possible implementations of init
* three main ones are: BusyBox init, System V init, and system
overview of how it works and the types of systems it suits best
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Notes: Init - why it is so important to the rest of the system - many possible implementations of init
• three main ones are: BusyBox init, System V init, and system
• overview of how it works and the types of systems it suits - trade-off between size, complexity, and flexibility.
After the kernel has booted:
• kernel bootstrap code finds a root fs, either initramfs or a fs specified by root= on the kernel command line,
and then executes a program that, by default, is /init for initramfs and /sbin/init for a regular fs.
• init is the ancestor of all other processes – it has root privilege, and since it is the first process to run, it has
a process ID (PID) of 1; and, if, for some reason, init cannot be started, the kernel will panic.
• job of init program is to take control of the boot process in user space and set it running.
a dedicated init daemon performs the following tasks:
• manages the life cycle of the system from bootup to shutdown.
• during boot, after the kernel transfers control, the init program starts other daemon programs and
configures system parameters and other things needed to get the system into a working state.
• launches a login daemon, such as getty, on terminals that allow a login shell.
• adopts orphan processes due to their immediate parent terminating and does process cleanup, as needed.
• restarts terminated daemons.
• handles system shutdown.
• handles other runtime events, such as new hardware and the loading and unloading of modules.
this is what systemd does.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 4
Init
introduction
Init - many possible implementations of init
+ three most likely seen in embedded devices are
BusyBox init, System V init, and systemd.
* Buildroot builds all three with BusyBox init as the default.
* Yocto Project builds either with systemd or System V init (default).
Yocto's Poky-tiny distribution ships with BusyBox init.
most other distribution layers do not.
* https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Notes: Init - many possible implementations of init
• three most likely seen in embedded devices are: BusyBox init, System V init, and systemd.
• Buildroot builds all three with BusyBox init as the default.
• Yocto Project builds either with systemd or System V init (default). Yocto's Poky-tiny uses BusyBox init.
Most other distribution layers do not.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 5
Init
BusyBox Init
BusyBox init — minimal program for running shell scripts, from a config
file /etc/inittab
* scripts placed in the /etc/init.d directory.
* config file having rules for starting programs at bootup and to stop
them at shutdown - contains a list of programs to run, one per line,
using a format: <id>::<action>:<program>
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Notes: BusyBox init – minimal program
• runs shell scripts, placed in the /etc/init.d directory.
• from a config file /etc/inittab having rules for starting programs at bootup and to stop them at shutdown.
It contains a list of programs to run, one per line, with this format: <id>::<action>:<program>
id: controlling terminal for the command.
action: includes conditions to run the command
program: program to run.
• actions are as follows:
sysinit: run when init starts - - before any of the other types of actions.
respawn: Run program and restart it if it terminates. typically used to run a program as a daemon.
askfirst: same as respawn, but prints “Please press Enter to activate” to console, and runs it when Enter
has been pressed. It is used to start an interactive shell without prompting for username or password.
once: Run program once but do not attempt to restart it if it terminates.
wait: Run program and wait for it to complete.
restart: rerun program when init receives SIGHUP signal, to reload the inittab file.
ctrlaltdel: run program when init receives the SIGINT signal, due to pressing Ctrl + Alt + Del on the console.
shutdown: Runs the program when init shuts down.
For simple projects with a small number of daemons, and a login shell on a serial terminal,
it is easy to write the scripts manually.
• It is appropriate for a roll your own (RYO) embedded Linux.
However, handwritten init scripts rapidly become unmaintainable as configuration list increases.
It is not modular and so needs updating each time a new component is added or removed.
Buildroot init scripts
Buildroot and BusyBox init
• effective use of BusyBox init for many years.
• two scripts in /etc/init.d/ named
• rcS - runs start scripts at bootup and iterates over all scripts in /etc/init.d/ with names that begin with a
capital S followed by two digits - in numerical order.
• rcK – runs kill scripts at shutdown and similarly iterates over all the scripts beginning with a capital K
followed by two digits and runs them in numerical order.
• easy for Buildroot packages to supply their own start and kill scripts, with two-digit number to impose order
in which they should be run
• If you are using Buildroot, this is transparent.
• If not, you could use it as a model for writing own BusyBox init scripts.
Buildroot and System V init
• Like BusyBox init, System V init relies on shell scripts inside /etc/init.d and an /etc/inittab configuration file.
• While both are similar in many ways, System V init has more features and a much longer history.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 6
Init
System V Init
* inspired from Unix System V and so dates back to the mid-1980s.
* common in desktop, server and many embedded systems till recently
however, in recent years, it has been replaced by systemd.
* BusyBox init daemon is a trim down form of System V init; however,
System V init has two advantages:
* boot scripts are easier to add packages at build time or runtime.
* collection of programs to be started or stopped in one step
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Notes: System V init
• inspired from Unix System V and so dates back to the mid-1980s.
version most often found in Linux distributions was written initially by Miquel van Smoorenburg.
• Until recently, it’s init daemon was common for desktop, server and many embedded systems.
however, in recent years, it has been replaced by systemd.
• BusyBox init daemon is a trim down form of System V init; however, System V init has two advantages:
• boot scripts are in a well-known/modular format, so easier to add packages at build time or runtime.
• collection of programs to be started or stopped in one go when using run levels and switching from one
level to another.
• There are eight runlevels, numbered from 0 to 6, plus S:
• S: Runs startup tasks
• 0: Halts the system
• 1 to 5: Available for general use and are used as needed.
e.g. on desktop Linux distributions, the conventional assignment is as follows:
• 1: Single user
• 2: Multi-user without network configuration
• 3: Multi-user with network configuration
• 4: Not used
• 5: Multi-user with graphical login
• 6: Reboots the system
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 7
Init
systemd
* System V init is a simple init daemon that has served well for decades.
* However, it lacks ability to monitor services and restart them if needed.
* Therefore, most popular Linux distributions have moved on to systemd.
https://bootlin.com/doc/training/embedded-linux/embedded-linux-slides.pdf
Notes: systemd - https://www.freedesktop.org/wiki/Software/systemd/ , is a system and service manager.
• systemd is state of the art and evolving rapidly - common on desktop, server and embedded Linux system,
especially on more complex devices.
• project initiated in 2010 by Lennart Poettering and Kay Sievers .. integrated set of tools around init daemon.
• also includes device management (udev) and logging, among other things.
how is it better than System V init for embedded systems?
• configuration is simpler and more logical - systemd has unit config files written in a well-defined format.
• explicit dependencies between services, rather than a two-digit number to determine when scripts are run.
• set permissions and resource limits for each service, which is important for security.
• monitor services and restart them if needed.
• parallel start to services - reducing boot time.
As with System V init, here are embedded use cases with examples based on Yocto Project 3.1 release, with
systemd version 244.
building systemd with the Yocto Project and Buildroot
• The default init daemon in the Yocto Project is System V - and select systemd, add to conf/local.conf:
INIT_MANAGER = "systemd"
• Buildroot uses BusyBox init by default.
select systemd through menuconfig under System configuration | Init system menu.
• configure the toolchain to use glibc for the C library, since systemd does not support uClibc-ng or musl.
• also, there are restrictions on the version and configuration of the kernel.
a full list of library and kernel dependencies is in README file at top level of the systemd source code.
Introducing targets, services, and units
• Before describing how systemd works, there are three key concepts to look at:
unit: A configuration file that describes a target, a service, and several other things. Units are text files
that contain properties and values.
service: A daemon that can be started and stopped, very much like a System V init service.
target: A group of services like a System V init runlevel, but more general.
There is a default target that is the group of services that are started at boot time.
• systemctl command is used to change states and find out what is going on.

## Slide 8
Summary Notes
+ Init: BusyBox init, System V init and systemd.
Notes: 1. Every Linux device needs an init program of some kind.
2. When designing a system that only launches a small number of daemons at startup and remains fairly static
after that, then BusyBox init is sufficient.
3. And, it is usually a good choice if using Buildroot as the build system.
4. On the other hand, in a system with complex dependencies between services at boot time or runtime, and
storage space is available, then systemd would be the best choice.
5. Even without the complexity, systemd has some useful features in the way it handles watchdogs, remote
logging, and so on, so give it serious thought.
6. Meanwhile, System V init lives on.
It is well understood, and there are init scripts already in existence for every component that is important to
us, and is the default init for the Yocto Project reference distribution (Poky).
7. While systemd is faster than System V init for a similar workload, for a very fast boot, neither beats the
simple BusyBox init with minimal boot scripts.
8. There is a lesser-known init system that is well suited for embedded Linux systems: BusyBox runit – which
offers the power and flexibility of systemd without the added complexity and overhead.
9. If Buildroot is the build system and BusyBox init does not meet the needs, then there are many good
reasons to consider BusyBox runit instead.
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 9
Quiz
Canvas
¢ 10 Questions
¢ 45 Mins
¢ 6 Attempts
¢ Highest Retained
Notes: Quiz
Good Luck!

## Slide 10
Assignment
1. using pthreads and IPC
2. Submit screenshot of the build and run.
Notes: Assignment
1. using pthreads and IPC
2. Submit screenshot of the build and run.

## Slide 11
Summary
In This Chapter
¢ Storage Strategy — flash memory, fs for flash memory
* Assignment
* Quiz
Notes: CHAPTER OVERVIEW
In This Chapter, We Discussed
1. Storage Strategy – flash memory, fs for flash memory
2. Assignment
3. Quiz
Mastering Embedded Linux Programming By Frank Vasquez, Chris Simmonds (Packt – Publisher)

## Slide 12
Summary
In This Chapter
¢ Overview of Embedded Linux Systems
* Introduction to Embedded Linux Systems
¢ Examples of Embedded Linux Systems
¢ Hardware for Embedded Linux Systems
* System Architecture of Embedded Linux Systems
* Environment for Embedded Linux Systems Development
* No Assignment
* Quiz
Notes: CHAPTER OVERVIEW
In This Chapter, We saw
1. Overview of Embedded Linux Systems
2. Introduction to Embedded Linux Systems
3. Examples of Embedded Linux Systems
4. Hardware for Embedded Linux Systems
5. System Architecture of Embedded Linux Systems
6. Environment for Embedded Linux Systems Development
7. No Assignment
8. Quiz